## Slide 1: E-waste in EECCA countries
Dr. Kees Baldé
balde@unu.edu
c.balde@cbs.nl

## Slide 2: United Nations University and Statistics Netherlands
Green Growth
Waste statistics
Environment Statistics
UNU: Think-tank of United Nations
  Our team - mainly e-waste
Statistical harmonization of e-waste measurement
Capacity building
  Kenya, China, El-Salvador, etc
  Training post graduate students and managers on e-waste management
  Etc.
Projects for national governments (USA, European Commission, Ethiopia, Japan, etc.)

## Slide 3: What is e-waste?
Everything with a plug or battery
Many appliances

## Slide 4: Methodology: e-waste quantities
Comtrade trade database
Trade in HS codes per country analysed
  1995-2012
  175 countries
  260 HS codes
  Average weight
  Sales = import - export
Link to 54 product categories
Statistical routines
  Outlier detection on time series
  Outlier detection international comparison
  Missing value replacement
  Extrapolation of time series to 1980
E-waste generated
  Lifetime profiles for the 54 categories

## Slide 5: E-waste amounts (Mt)
Chart: 
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Lamps | 0.65541 | 0.70922 | 0.76233 | 0.81532 | 0.86732 | 0.91949 | 0.97225 | 1.0256 | 0.96758
Large equipment | 7.9978 | 8.4415 | 8.9761 | 9.5645 | 10.1954 | 10.8776 | 11.6095 | 12.3785 | 12.7966
Small equipment | 11.5039 | 12.2189 | 12.9476 | 13.6946 | 14.4488 | 15.2253 | 16.0243 | 16.8335 | 16.4534
Small IT and telecommunication equipment | 2.2546 | 2.4081 | 2.5624 | 2.6708 | 2.78 | 2.8964 | 3.0212 | 3.153 | 2.9758
Temperature exchange equipment | 3.7296 | 3.9835 | 4.2476 | 4.5374 | 4.84 | 5.1591 | 5.4938 | 5.8371 | 6.1468
Screens, monitors, and equipment containing screens (..) | 5.1888 | 5.4665 | 5.7089 | 5.924 | 6.083 | 6.1902 | 6.2568 | 6.2974 | 6.0968

## Slide 6: E-waste generation in 2012
>15 kg/inh
5 to 15 kg/inh
< 5 kg/inh

## Slide 7: Good recycling of e-waste
Toxic removal
Pre-processing
End-processing
Toxic removal
Manual dismantling
Mechanical separation
  Shredding, breaking, milling, and sequential sorting
Combination of dismantling and mechanical separation
Base metal refinery
Precious metal refinery
Plastics recycling
Battery recycling
Other component treatment
Disposal

## Slide 8
8
Afgelopen maandag

## Slide 9
9

## Slide 10: Documented and reported collection percentage of e-waste generated
EU: ± 40%
China: ± 5%
USA+CAN: ± 11%
Japan: ± 40%
Australia: ± 1%

## Slide 11: Flows are largely undocumented…
??? %
??? %
??? %
??? %

## Slide 12: Informal recycling in very poor African countries
Notes: Due to decreasing life spans, minituarisation in design, recycling becomes even harder.
In the current reality  hazardous substances are released when treated improperly

## Slide 14: Informal recycling techniques in China
Labour intensive in manual dismantling, sorting
  Use of simple tools and techniques
Reuse:
  Batteries, cartridges, power supplies, cables, circuit boards and chips etc.
Material recycling:
  Precious metals (acid stripping), ferrous and non-ferrous metals and plastics
Limited technologies and equipment
No occupational protection, no emission control measures

## Slide 17: Impact on health
Exposure to lead
  Mental development of children, toxic to kidneys
When burning PVC  dioxins
  One of the most hazardous carcinogens (cancer)
Hexavalent Chromium
  Kidney, liver, DNA
Brominated Frame retardants
  Fetal damage
Cadmium
  Cancer, toxic to kidneys
Source: e-stewards.org/the-e-waste-crisis

## Slide 18: Resource and job potential
Nicht gleich Wert
Nicht gleich Wert
At least 57 elements:
Materials
Base metals
Precious metals
Rare earth metals
Plastics
Glass
....
Hazardous materials
Mercury
CFCs
Lead
Flame retardants
....

## Slide 19
Challenges vs. opportunities in emerging economies for e-waste
19
Lack of investment and technology
Lack of formal collection system
Lack of financing schemes
Lack of national e-waste legislations
Presence of the informal sector
Growing e-waste streams (domestic and import)
Challenge
Opportunity
(Relative) low labor cost
Available technological know-how
and management experience
Create jobs + create revenue

## Slide 20: Role of Government
Ministry of Environment
  Formulate law
  Monitoring of e-waste volumes
  Define Collection targets
    E-waste collected vs. e-waste generated
  Minimum recycling standards of collected e-waste
  Enforce
Environmental inspection
  Basel Convention
    Inspection of shipments (illegal imports from OECD countries)
  Inspect on inferior recycling standards

## Slide 21: Private sector involvement
Extended producer responsibility
  Importer or producer is responsible for proper recycling of e-waste
  Set up collection of e-waste
  Set recycling standards
  Can be financed via visible fee upon sale reflecting recycling costs
    Fridge: 8 euro, TV 2 euro, etc.
    E-waste recycling is also profitable in EU for most categrories

## Slide 22: Data monitoring
National Statistics Institute or Environmental Protection Agency
  Sales – household statistics (possession studies), and household expenditure statistics
  Sales (Apparent consumption approach): Domestic Production + Import - Export
  Waste Statistics – waste collection
  Data is independently measured: with a purpose for to measure target in e-waste laws

## Slide 23: How to measure e-waste?
Sales
  Stays in household (lifetime)
E-waste generated
  Sales after use phase (lifetime period).
Separate e-waste collection
  Compliant with national law
Collection with other wastes
  Other recycling (with metal scrap, lower quality recycling)
  Waste Bin (bad consumer behaviour)
Indicators
  Total Sales (kg/inh)
  Total waste generated (kg/inh)
  E-waste collection rate = Separate E-waste collection / e-waste generated

## Slide 24: Formulated in E-waste guidelines
Guide countries to measure relevant parameters
  http://ias.unu.edu/en/research/e-waste-quantification.html#outputs

## Slide 25: EECCA countries
1.9 Mt of e-waste in total region in 2014
Annual growth rate: 5%
Gold: Worth 560 million Euro annually
Other valuables: ± 1800 million euro annually
http://www.step-initiative.org/index.php/WorldMap.html
7-9 kg/inh
5-7 kg/inh
3-5 kg/inh
1-3 kg/inh

## Slide 26: % of population covered with regulations on e-waste
Chart: 
| No | Pending | Yes
 | 0.79233 | 0.16063 | 0.047045

## Slide 27: What else can UNU offer: Example Kazakhstan (unit: kt)
Steady 6 to 7 % yearly Growth rate
126 million kg of e-waste per year in Kazakhstan
Worth 31 million USD of gold in this e-waste
Country |  | YEAR | 2014
Kazakhstan | E-waste generated | Total | 126
 |  | Lamps | 2
 |  | Large Equipment | 32
 |  | Screens | 18
 |  | Small Equipment | 48
 |  | Small IT | 6
 |  | Cooling and Freezing equipment | 15

## Slide 28: Separate collection of e-waste
Unknown for all EECCA countries so far …

## Slide 29: Raise hands
Questions
  1) Are there regulations on E-waste?

## Slide 30: Raise hands
Questions
  1) Are there regulations on E-waste?
  2) Is there data on sales in your country
7-9 kg/inh
5-7 kg/inh
3-5 kg/inh
1-3 kg/inh

## Slide 31: Raise hands
Questions
  1) Are there regulations on E-waste?
  2) Is there data on sales in your country
  3) Is there data on separate E-waste collection in your country?
Unknown data

## Slide 32: Ideas for potential project
Data validation
Data gathering on collection of e-waste
Impact assessment
  Recycling performance of e-waste
  Recycling potential of e-waste (urban mine)
  Creation of green jobs in recycling
  Environmental burden
  Societal impact
Raise hands if interested
Please give us feedback on your thoughts…is it interesting for your country?