#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2001/23

12 April 2001

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Nineteenth session, 2-6 July 2001,

# agenda item 8 (b))

# EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

# Classification of ammonium nitrate emulsions, suspensions and gels

# New entry for Ammonium Nitrate Emulsions in Class 1

# Transmitted by the expert from Sweden

1.	BACKGROUND

During the twenty-first session of the Committee of Experts on the Transport of dangerous Goods, December 2000, it was decided to create a new entry for Ammonium Nitrate Emulsions, suspensions or gels, intermediate for blasting explosives (ANE:s), in 5.1 (UN No. 3375).

It was further decided to have a working group meeting during the spring of 2001 to discuss and give suggestions for suitable test methods to be used when assigning substances to this new entry.

2.	JUSTIFICATION

When testing candidates for UN No. 3375, a number of the substances will show such properties that they should be classified in Division 1.5. However, there exist no suitable entry in 1.5, neither is it allowed to transport such substances in tanks.

GE.01-

The author believe that as a consequence of the decision to assign UN No. 3375 for ANE:s it is logical to have a similar entry in Class 1 which allows tank transport for such substances.

3.	PROPOSAL

3.1	To create a new entry in 1.5 D as follows:

| UN No. (1) | Name and description (2) | Class or Division (3) | Subsi- diary risk (4) | UN packing group (5) | Special provi- sions (6) | Limited quantities (7) | Packagings and IBC’s | Portable tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction (8) | Special provision (9) | Portable tank instruction (10) | Portable tank special provision (11) |
| 05xy | AMMONIUM NITRATE EMULSION or SUSPENSION or GEL, intermediate for blasting explosives | 1.5 | D | III | 309 3XY | NONE | P101 |  | TXXX | TP9 |

3.2	Create a new special provision 3XY as follows:

This entry may only be used for substances that do exhibit explosive properties of Class 1 when tested in accordance to Test Series 1 and 2 of Class 1 or for those substances that do not pass the 8(b), 8(c) or 8(d) tests  (see Manual of Tests and Criteria, Part I).

  - Create a new portable tank instruction TXXX as follows:

| Portable tank instruction | Minimum test pressure (bar) | Minimum shell thickness | Pressure-relief requirements | Bottom opening requirements |
| --- | --- | --- | --- | --- |
| TXXX | 1.5 | See 6.7.2.4.2 | Normal | See 6.7.2.6.3 |

This portable tank instruction have the same properties as T2.

4.	Consequential amendments to 4.2.4.2

As a consequence of the proposal 4.2.4.2 need to be amended in such a way that tank transport is allowed for ANE:s. The authors suggestion of this amendment is as follows:

1) 	Change the first sentence of 4.2.4.2.1 to read “Portable tank instructions apply to dangerous goods of all Classes.

2) Create a new 4.2.4.2.2 to read “Of the substances in Class 1, only Ammonium nitrate emulsions, suspensions or gels according to UN No 05xy are allowed to be transported in tanks. This substance are assigned to portable tank instruction TXXX.

# ___________

# Text boxes

STSTE

Secretariat