UN/SCETDG/22/INF.45

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Twenty-second session, 2-6 December 2002,

agenda item 3)

Working group on organometallic substances

Document ST/SG/AC.10/C.3/2002/60:

2.4.5	Add a new footnote "2" against the title of figure 2.4.2 to read as follows:

"2	Test methods N.1 to N.5 can be found in the Manual of Test and Criteria, Part III, Section 33.".

Dangerous Goods List

Amend the entries for UN Nos. 3391, 3393, 3395 and 3400 as follows:

| UN No. | Name and description | Class or division | Subsi- diary Risks | UN packing group | Special provi-sions | Limited quanti-ties | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruc-tion | Special provi-sions | Instructions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| 3391 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC | 4.2 |  | I | 274 | NONE | P404 IBC04 | PP86 B14 | T21 | TP2 TP7 TPXX |
| 3393 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC, WATER REACTIVE | 4.2 | 4.3 | I | 274 | NONE | P404 IBC04 | PP86 B14 | T21 | TP2 TP7 TPXX |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE | 4.3 |  | I | 274 | NONE | P403 IBC04 |  | T9 | T7 TPXX |
|  |  | 4.3 |  | II | 274 | 500 g | P410 IBC04 |  | T3 | TPXX |
|  |  | 4.3 |  | III | 223 274 | 1 kg | P410 IBC06 |  | T1 | TPXX |
| 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 |  | II | 274 | 500 g | P410 IBC06 |  | T3 | TPXX |
|  |  | 4.2 |  | III | 223 274 | 1 kg | P002 IBC08 |  | T1 | TPXX |

Replace the entries for UN Nos. 3396, 3397 and 3398 with the entries proposed in paragraph 4.2 of document ST/SG/AC.10/C.3/2002/71 with modifications, as follows:

| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE | 4.3 | 4.1 | I | 274 | NONE | P403 IBC04 |  | T9 | TP7 TPxx |
|  |  | 4.3 | 4.1 | II | 274 | 500 g | P001 IBC01 |  | T3 | TPxx |
|  |  | 4.3 | 4.1 | III | 223 274 | 1 kg | P410 IBC06 |  | T1 | TPxx |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER REACTIVE, SELF-HEATING | 4.3 | 4.2 | I | 274 | NONE | P403 IBC04 |  | T9 | TP7 TPxx |
|  |  | 4.3 | 4.2 | II | 274 | 500 g | P410 IBC04 |  | T3 | TPxx |
|  |  | 4.3 | 4.2 | III | 223 274 | 1 kg | P410 IBC06 |  | T1 | TPxx |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER REACTIVE | 4.3 |  | I | 274 | NONE | P403 IBC04 |  | T13 | TP2 TP7 |
|  |  | 4.3 |  | II | 274 | 500 g | P410 IBC04 |  | T7 | TP2 TP7 |
|  |  | 4.3 |  | III | 223 274 | 1 kg | P410 IBC06 |  | T7 | TP2 TP7 |

Document INF 34:

Retain all substances listed in paragraph 2 of INF.34 (UN Nos. 1366, 1370, 2005, 2445, 3051, 3052, 3053 and 3076) and add a new special provision YYY against each of these entries to read as follows:

"YYY	It is intended that this entry will be deleted from modal requirements effective on 1 January 2007. Irrespective of 2.0.2.2, in the interim period, this entry or the appropriate generic entry may be used.".

Other entries proposed for deletion in paragraph 3 of ST/SG/AC.10/C.3/2002/71 are deleted (UN Nos. 2003, 3049, 3050, 3203, 3207 and 3372).

--------------------------