#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.4/2002/16/Add.9

23 October 2002

ENGLISH

# Original: ENGLISH and FRENCH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

##### Sub-Committee of Experts on the

# Globally Harmonized System of Classification

# and Labelling of Chemicals

# (Fourth session, 9-11 December 2002

agenda item 2)

# Globally Harmonized System of Classification

# and Labelling of Chemicals (GHS)

Submitted by the GHS Editorial Group

Annex 6

Examples of Arrangements of the GHS Label Elements

Annex 6

Examples of arrangements

of the GHS label elements

##### A6.1 	Example 1

The product  is a liquid substance:

- classified under GHS as skin corrosive category 1B and flammable liquid category 3.

- UN Model Regulations on the Transport of Dangerous Goods classification is corrosive liquid, flammable, N.O.S., - UN 2920.

A6.1.1	Label for large receptacle (200 litre drum) for transport, emergency response and workplace audiences

| UN 2920 | 2-methyl tetramethylenexxxxx |
| --- | --- |
| Corrosive liquid, flammable, N.O.S. | Danger |
| (2-methyl tetramethylenexxxxx) | Causes severe skin burns and serious eye damage Highly flammable liquid and vapour Avoid contact with skin and eyes Keep away from heat and ignition sources |
| First aid: For skin contact, remove contaminated clothing and wash affected area thoroughly with water. If irritation develops, seek medical attention. For eye contact, immediately flush eyes with flowing water for at least 15 minutes and seek medical attention. |
| GHS Example Company, Akron, NWT, Canada. Telephone (888) 888-8888 |

A6.1.2	Label for small workplace receptacle (10 litre) packaged inside an outer transport packaging – for workplace audience

2-methyl tetramethylenexxxxx

Danger

Causes severe skin burns and serious eye damage Highly flammable liquid and vapour Avoid contact with skin and eyes Keep away from heat and ignition sources

First aid: For skin contact, remove contaminated clothing and wash affected area thoroughly with water. If irritation develops, seek medical attention. For eye contact, immediately flush eyes with flowing water for at least 15 minutes and seek medical attention.

GHS Example Company, Akron, NWT, Canada Telephone (888) 888-8888

A6.1.3	Un transport markings and labels for the outer packaging of a “combined” transport packaging containing receptacles – for  transport and emergency response audiences.

Note: Only the UN transport markings and labels are required for such outer packagings.

UN 2920

Corrosive liquid, flammable, N.O.S. (2-methyl tetramethylenexxxxx)

A6.2 	Example 2

The product is a liquid mixture:

- classified under GHS as toxic to reproduction, category  1B and flammable liquid, category 3.

- UN Model Regulations on the Transport of Dangerous Goods classification is flammable liquid - UN 1263.

A6.2.1	Label for large receptacle (200 litre drum) for transport, emergency response and workplace audiences

|  | ZZZ Red Paint |
| --- | --- |
|  | Danger |
| UN 1263 Paint | May damage fertility or the unborn child Highly flammable liquid and vapour ** Contains lead pigments and cellosolve acetate Keep away from heat and ignition sources Keep away from food and drink Avoid contact with skin and eyes and inhalation of vapour Wash hands thoroughly after use and before eating |
| First aid: For skin contact, remove contaminated clothing and wash affected area thoroughly with water. If irritation develops, seek medical attention. For eye contact, immediately flush eyes with flowing water for at least 15 minutes and seek medical attention. |
| GHS Example plc, Leeds, England. Telephone 44 999 999 9999 |

** 	Note: competent authorities may choose to not require disclosure of ingredient identities on the label of products intended for workplace use only – See Part I,par. 1.4.10.5.1 (a) (iii).

A6.2.2	Label for small workplace receptacle (10 litre) packaged inside an outer tarnsport packaging – for workplace audience

ZZZ Red Paint

DANGER

May damage fertility or the unborn child Highly flammable liquid and vapour ** Contains lead pigments and cellosolve acetate

Keep away from heat and ignition sources Keep away from food and drink Avoid contact with skin and eyes and inhalation of vapour Wash hands thoroughly after use and before eating

First aid: For skin contact, remove contaminated clothing and wash affected area thoroughly with water. If irritation develops, seek medical attention. For eye contact, immediately flush eyes with flowing water for at least 15 minutes and seek medical attention.

GHS Example plc, Leeds, England. Telephone 44 999 999 9999

** 	NOTE: competent authorities may choose to not require disclosure of ingredient identities on the label of products intended for workplace use only.

A6.2.3	Un transport markings and labels for the outer packaging of a “combined” transport packaging containing receptacles – for  transport and emergency response audiences.

Note: Only the UN transport markings and labels are required for such outer packagings.

UN 1263 Paint

# Text boxes

STSTE

Secretariat