| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/2002/54 20 August 2002 ENGLISH Original: ENGLISH and FRENCH |
| --- | --- | --- |

##### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-twenty-eighth session,

12-15 November 2002, agenda item 5.2.8.)

DRAFT CORRIGENDUM 1 TO REVISION 3 OF REGULATION No. 37

(Filament lamps)

Transmitted by the Working Party on Lighting

and Light-Signalling (GRE)

Note:  The text reproduced below was adopted by GRE at its forty-eighth session and is transmitted for consideration to WP.29 and AC.1.  It is based on document TRANS/WP.29/GRE/2002/23, section A only, not amended (TRANS/WP.29/GRE/48, para. 86).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Annex 1,

Sheet P21/4W/1, the table, correct the cap designation "BAZ 15s" to read "BAZ 15d".

Sheet W3W/1, the table, correct the cap designation "W2.2x9.5d" to read "W2.1x9.5d".

Sheet S3/1, the drawing, correct the text "FILAMENT LAMPS FOR MOPEDS" to read "FILAMENT LAMP FOR MOPEDS".

Sheet H6W/1, footnote 3/, correct the words "no projections of soldering" to read "no projections or soldering".

Sheet H7/3, the table, for dimensions "h1" and "h2", column "Standard filament lamp", delete the references to footnote "7/".

Sheet P27W/1, the table, for "Rated values", "Watts", column "Standard filament lamp", correct the value "21" to read "27".

Sheet W21W/1, the table, for angle "", column "Filament lamps of normal production", both for "min." and for "max." values, insert the reference to footnote "2/".

Sheet H10/2, the table, (French only).

Sheet P19W/2, the table, for angle "α", column "Filament lamps of normal production", for "max." value, delete the reference to footnote "1/".

Sheet P24W/2, the table, for angle "α", column "Filament lamps of normal production, for "max." value, delete the reference to footnote "1/".

_________