## Slide 1: Informal Document No. 16 52nd GRRF,16-18 September 2002 Agenda Item 6. Submission by the United States of America for information on the status of rulemaking on tire pressure monitoring systems Tire Pressure Monitoring Systems Final Rule

## Slide 2: Background
U.S. Congress mandated a final rule to require a warning system “in motor vehicles to indicate to the operator when a tire is significantly under-inflated” be completed by November 1, 2001
Congress mandated that this rule must take effect by November 1, 2003

## Slide 3: TPMS Final Rule
Final Rule published on June 5, 2002
Petitions for Reconsideration period closed July 22, 2002
Agency received 13 petitions for reconsideration on a variety of the issues in the final rule
Agency preparing its response to these petitions for reconsideration

## Slide 4: Effective Dates
Final rule is effective August 5, 2002
Vehicles must be equipped with TPMS based on a phase-in beginning November 1, 2003
Phase-in period ends October 31, 2006
Beginning November 1, 2006 all light vehicles are required to be equipped with a TPMS.

## Slide 5: Compliance Option 1
Requires driver to be notified when 1 to 4 tires are 25% under recommended inflation pressure or at 20 psi, whichever is greater
  Essentially requires direct systems to meet requirements
  This choice requires the most-capable current system, so it both ensures the greatest safety benefits and costs more

## Slide 6: Compliance Option 2
Requires driver to be notified when 1 tire is 30% under recommended inflation pressure or at 20 psi, whichever is greater
  Permits both direct systems and indirect systems
  This choice permits continued use of indirect systems, so it results in lower costs, but the lesser performance may result in lesser safety benefits

## Slide 7: Low Tire Pressure Activation
Tire Type | Max. Inflation Pressure (kPa) | Min. Activation Pressure (kPa)
P-metric - Standard | 240 300 350 | 140 140 140
P-metric – Extra Load | 280 340 | 160 160
LT load range C | 350 | 200
LT load range D | 450 | 260
LT load range E | 550 | 320

## Slide 8: Phase-in Requirements
Any of the two compliance options may be used for vehicles manufactured between November 1, 2003 and October 31, 2006
10% production: November 1, 2003 – October 31, 2004
35% production: November 1, 2004 – October 31, 2005
65% production: November 1, 2005 – October 31, 2006
100% production: November 1, 2006 and after
Tire pressure survey will be conducted to evaluate tire pressures of vehicles with indirect TPMS and without any TPMS
Second part of final rule to be issued by March 1, 2005, based on survey findings

## Slide 9: Second Part of Final Rule
Second part of final rule will be issued by March 1, 2005
Decision on which compliance option becomes the sole requirement will be based on the findings of the tire pressure survey
Agency tentatively believes that Compliance Option 1 would best meet Congressional intent

## Slide 10: Petitions for Reconsideration
Major Issues
  Replacement tires
  Calibration procedures
  Telltale symbol
  Warning activation within 10 minutes
  Disablement of TPMS
  Concerns of small volume manufacturers

## Slide 11: Summary
Agency to decide on issues in Final Rule -Petitions for Reconsideration
Expect to be issued by late-2002 or early-2003
Docket 8572 will remain open for public to submit any new data; web site is dms.dot.gov
Tire pressure survey is expected to be initiated in 2003
Agency decision on final requirement by March 2005