## Slide 1: ISOFIX FRENCH PROPOSAL (DOCUMENTS TRANS/WP29/GRSP/2001/14Rev1; 2001/15Rev1 and 2001/16Rev1)
GRSP 13-17/05/2002

## Slide 2: MAIN PRINCIPLES
     ISOFIX "universal" type : Forward Facing Child Restraint System (CRS) with two low anchorages + top tether.
    ISOFIX "semi-universal" : Forward or Rearward Facing Child Restraint System with two low anchorages and other(s) anti- rotation device(s) (legform, lower tether,…).
    Keep the current R 44 criteria (dummies and criteria, pulse,…).
    Only M1 vehicle type have to be equiped with anchorages.
    To guarantee the setting of ISOFIX CRF in the car (fixtures)

## Slide 3: PROVISIONS REQUIRED FOR CAR (1)
     2 ISOFIX positions (3 anchorages) for any M1 vehicle, except for M1 with only 1 seat row (no ISOFIX position is required).
     Each ISOFIX position shall permit the installation of fixture(s)
     1 ISOFIX position has to be installed at the second seat row.
     ISOFIX position not located on a vehicle seat is allowed.
     Integrated "build in" CRS are taken into account for the 2 ISOFIX positions to be provided.

## Slide 4: PROVISIONS REQUIRED FOR CAR (2)
     Instructions for ISOFIX anchorages and restrictions for seat adjustment have to be indicated in the vehicle handbook
     Post-equipment anchorages have to fulfil the provisions.
     Each ISOFIX position is defined according fixtures : 3 rearward facing and 2 forward facing.
     If an ISOFIX position is provided on front side passenger seat protected with a frontal airbag, a deactivation device shall be fitted.

## Slide 5: PROVISIONS REQUIRED FOR CAR (3)
3 Static tests are performed to check the strength of the anchorages and the excursion of the S-FAD :
     1 test with the 3 anchorages, longitudinal, F= 8kN : no failure of anchorages and excursion limited to 125 mm
     1 test with the 2 low anchorages, longitudinal, F= 8kN : criteria idem test 1.
     1 test with the 2 low anchorages, oblique (75°), F= [5kN] : no failure of anchorages and excursion limited to [125 mm].

## Slide 6: PROVISIONS FOR ISOFIX CHILD RESTRAINT SYSTEM
     A new mass group is introduced in Regulation 44 : "1+" for 15-22 kg children.
     ISOFIX CRS design have to comply within the external dimensions of fixture(s).
     Two tests are performed for Forward Facing ISOFIX Child Restraint :
        Small dummy with the shorter distance of the top tether strap.
        Heavier dummy with the longuer distance of the top tether strap.

## Slide 7: ISOFIX FRENCH PROPOSAL (DOCUMENTS TRANS/WP29/GRSP/2001/14Rev1; 2001/15Rev1 and 2001/16Rev1)
GRSP 13-17/05/2002