## Slide 1
May 2002
Child Restraint Systems
A Field study of Misuse
Helena Menezes
José Dias

## Slide 2
Based on ISO-13215-1
Misuse severity assessment
Based on consequences of misuse
Field Study
May 2002
No misuse
Slight misuse
Serious misuse
Very serious misuse

## Slide 3
Observations summary
About 500 CRS inspected
70 CRS models
May 2002
G0/I and GI
62 %
G0 and G0+
20 %
GI/II/III
12 %
Not Identified
6%

## Slide 4
May 2002
Misuse distribution
No misuse
Slight misuse
Serious misuse
Very serious misuse
CRS with
Harness
CRS with
no Harness
100 %
80 %
60 %
40 %
20 %
0 %
On CRSs with and without harness

## Slide 5
R44 Supplement 2
May 2002
“…in the immediate area where the child’s head rests within the child restraint and on the visible surface of the child restraint system, rearward-facing restraints shall have the following label permanently attached…”
4.5.

## Slide 6
May 2002
R44 Supplement 2
“…in the immediate area where the child’s head rests within the child restraint and on the visible surface of the child restraint system, rearward-facing restraints shall have the following label permanently attached…”
4.5.

## Slide 7: CI recommends 1. GRSP ask Technical Services Group to tighten up application of current Supplement 2 requirements to ensure label position is correct
May 2002

## Slide 8: CI recommends 2. Tightening of requirements to eliminate flag style labels.
May 2002

## Slide 9
Misuse Modes on CRSs with Harness
Children facing forward too soon
May 2002
Rearward facing
Forward facing
CRS orientation according to age
0-6 m
6-9 m
9-12 m
12-18 m
100 %
80 %
60 %
40 %
20 %
0 %

## Slide 10
Rearward Facing versus Forward Facing
May 2002
CRS group use according to age
G0 and G0+
G0/I and GI
0-6 m
6-9 m
9-12 m
12-18 m
100 %
80 %
60 %
40 %
20 %
0 %
Group 0+ not being used much after 9 months
Seat shells too small for children
Leg room insufficient to maintain rearward facing

## Slide 11
May 2002
Harness slot height versus 50%tile and 95%tile shoulder height when sitting
50%tile 9 months
50%tile 18 months
95%tile 18 months
35
30
25
20
15
10
5
0
Model 1
Model 2
G0+ CRS Dimensions vs Child Dimensions
cm
Two of the most popular seats in Portugal do not have harness slots at heights compatible with children up to 18 months old
Source: CR 13387:1999 (CEN)

## Slide 12
May 2002
50%tile 9 m  95%tile 6 m
50%tile 12 m
50%tile 18 m
95%tile 12 m
95%tile 18 m
95%tile 9 m
CRS depth versus P50 and P95 leg length
45
40
35
30
25
20
15
10
5
0
Model 1
Model 2
cm
G0+ CRS Dimensions vs Child Dimensions
Indication that space for legs is key limiting factor cited by parents for keeping children rear facing in current products
Source: CR 13387:1999 (CEN)

## Slide 13
May 2002
G0+ CRS Dimensions vs Child Dimensions
CI recommends
GRSP reviews CRS shell size and legroom requirements for 0+ products to enable children to be kept rear facing longer

## Slide 14
May 2002
Harness adjustment limited by yoke coming to end of travel

## Slide 15
May 2002
CI recommends
GRSP introduces requirements that harness must be capable of being adjusted to all sizes of intended users.

## Slide 16
Instructions on the CRS
May 2002
Clear Specification of orientation of CRS in car needed

## Slide 17
May 2002
CI recommends
GRSP introduces improved requirements for seat marking to indicate forward and rearward orientation of CRS in car

## Slide 18
May 2002
R 44.03 says
If the restraint is to be used in combination with an adult
safety belt the correct routing of the webbing shall be clearly
indicated by means of a drawing permanently attached to the
restraint.

## Slide 19
Instructions on the CRS
4.3. “…Permanently attached”?
May 2002

## Slide 20
May 2002
CI recommends
GRSP ad hoc improves application of current requirement for permanent marking

## Slide 21
CRS and vehicle incompatibilities
May 2002
Model 1
Model 2
Model 3
60 %
50 %
40 %
30 %
20 %
10 %
0 %
Model 4
Vehicle Incompatibility Rate for R44-03 Universal Category
But ...
Revision 03 marked a clear improvement over revision 02
Still, in almost 20% of the cases it was impossible to install the CRS in the vehicle

## Slide 22
May 2002
ISOFIX is intended to provide compatible mounting for the CRS in the vehicle.
In developing ISOFIX requirements, great emphasis needs to be placed on the ease of use of ISOFIX seats, and the provision of clear effective information to the consumer

## Slide 23
May 2002
Summary
Improved application of existing requirements:
Supplement 2 – Position of warnings
Permanence of all labels

## Slide 24
May 2002
Summary
Upgraded requirements needed for
Supplement 2 warning – no flags
CRS shell size and legroom for 0+
Harness adjustment to fit all sizes
Showing orientation of seat in car

## Slide 25
May 2002
Summary
The experience with current Universal restraints implies that maximum care should be taken with the usability requirements for the new generation of ISOFIX systems