## Slide 1: ES2- Concerns
OICA
31st session of GRSP
May 2002

## Slide 2: ES2 - Concerns
EEVC WG12 has reported on the « Development and evaluation of the ES2 dummy »
This report raises questions on some remaining key-points

## Slide 3: ES2 - Concerns
Variation of performance criteria between ES1 and ES2
Directional sensitivity
Inter-rib homogeneity
Thorax damping characteristics and stiffness
Interactions between body segments

## Slide 4: ES2 - Concerns Variation of performance criteria
CEVE report: ES2 criteria has lower criteria than ES1 in biofidelity tests
It is the contrary in pendulum tests
Only 7.6 m/s sled tests are fully exploitable. Nevertheless, results on ES1 tests are highly spread
In 10.3 m/s sled tests, maximum deflection is always reached for the uppermost rib

## Slide 5: ES2 - Concerns Directional sensitivity
Possible increase of deflection on ES2 at negative angles: 10%
No data on ES1 at negative angles

## Slide 6: ES2 - Concerns Inter-rib homogeneity
Unexpected lack of inter-rib homogeneity not explained
Uppermost rib deflection often increase with ES2 whilst the mean deflection decreases; criteria is based on the higher deflection

## Slide 7: ES2 - Concerns Thorax damping characteristics and stiffness
Friction is eliminated in ES2 and compensated by increasing tuning spring
ES2 thorax stiffer and less damped

## Slide 8: ES2 - Concerns Thorax damping characteristics and stiffness
The observed frequency in some FST is a consequence of elastic rebound of ribs
This leads to high VC value due to high velocity at high deflections

## Slide 9: ES2 - Concerns Interactions between body segments
ES2 pelvis stiffness is lower
ES2 pelvis is highly sensitive to angle
Effects on thorax have to be investigated

## Slide 10: ES2 - Concerns Conclusions
Does ES2 improve real safety ?
  Agreement on back plate
  Need for further explanations on other key-points