## Slide 1: ANCHORAGE STRENGTH REQUIREMENTS
George Mouchahoir
Office of Performance Standards
National Highway Traffic Safety Administration
May, 2002

## Slide 2: BASIS FOR STRENGTH REQUIREMENTS
FORCE
DURATION OF FORCE APPLICATION
DISPLACEMENT CRITERIA

## Slide 3: STRENGTH CALCULATION
Force = mass X acceleration
  System mass (child restraint system (CRS) and child)
  Acceleration of vehicle

## Slide 4: MASS ASSUMPTIONS
  22.7 kg (50 lb) for child
  (Current mass limit of FMVSS No. 213)
  7 kg (15.4 lb) for CRS
System Mass (m) = CRS + child
= 29.7 kg (65.4 lb)

## Slide 5: US VEHICLE FLEET CRASH PULSES PEAK VALUES
MY99 Saturn SC1

## Slide 6: AVERAGE PEAK VEHICLE ACCELERATION

## Slide 7: FORCE COMPUTATION
Maximum dynamic force expected to act through the center of gravity (cg) of the CRS is:
= [System mass]X[acceleration]
= [29.7 kg][(48.4 g)(9.81 m/s2)]
= 14,101 N
 15 kN (3371 lb)

## Slide 8: MISUSE STRENGTH REQUIREMENTS
Misuse test: Two lower anchorages of CRS attached only
  Force of 11 kN will assure that at least a minimum level of protection is provided when the tether is not used to attach CRS to the vehicle in forward direction, and
  Force of 5 kN in lateral direction

## Slide 9: DURATON OF FORCE
For 3 anchorages attached:
Pull force as linearly as practicable to 15 kN in 24 s  t  30 s, and maintain at a 15 kN level for 1 second

## Slide 10: DURATION OF FORCE FOR MISUSE CASE
Forward force direction – Pull force as linearly as practicable to a full force application of 11 kN in 24 s  t  30 s, and maintain at an 11 kN level, currently, for 10 seconds
Lateral direction – Pull force as linearly as practicable to a full force application of 5 kN in 24 s  t  30 s, and maintain at a 5 kN level, currently, for 10 seconds

## Slide 11: DISPLACEMENT REQUIREMENTS
Test Description | Maximum Force Limit | Maximum Displacement Limit
Forward direction, with tether attached | 15.0 kN | 125 mm
Forward direction, lower anchorages only | 11.0 kN | 125 mm
Lateral direction | 5.0 kN | 125 mm