Informal Document No. 16

32nd GRSP, agenda item B.1.5.
								Prepared by the expert from 									Germany

The Informal document has been prepared by the expert from Germany and relates to document 

- TRANS/WP.29/GRSP/2002/18 -,

PROPOSAL FOR DRAFT 03 SERIES OF AMENDMENTS TO REGULATION No. 29

(Cabs of commercial vehicles)

1. Introduction and Justification:

The British Delegation deserves our appreciation for having put together the different views in one paper.

However, the document needs to be studied very carefully.
The proposed modifications have very limited potential to reduce the number of injured drivers and co-drivers of vehicles of category N with cabs / chassis. This can be demonstrated by the interpretation of the existing accident data, see figures 1a, 1b, 2 and 3.
In our view this proposal leads to new cab design only but not to a noticeable reduction of the number of accidents and the number of injured people.

A short time success could be expected by enforcing EC Regulation No.16, that means recommendation of compulsory wearing of seat belts.

In addition, one should also focus on active safety, that means avoiding accidents instead of reducing accident consequences only. Key words in this respect are: lane control, automatic distance control and electronic stability control.

Germany proposes to study the UK-Proposal and to amend the existing ECE Regulation 29, Revision 1 Amendment 1 as follows:

2. Proposed modification of the existing text of the Regulation

2.1 Existing text (ECE-Regulation 29,Revision 1 Amendment 1)

- SCOPE
This Regulation applies to commercial vehicles which are intended for carriages of goods. It does not apply to agricultural tractors and machinery.

2.2 Proposed text

1 	SCOPE 

	The Regulation applies to vehicles of category N with separate driver´s 	cab and a technically permissible maximum mass exceeding 2000kg. 
	Vehicles meeting the requirements of Regulation 94 and its 01 series of 	amendments are exempted from the requirements of this Regulation. It does 	not apply to agricultural tractors and machinery

Figure 1a and 1b:

Figure 2:

Federal Statistical Office, Germany

Figure 3:

Federal Statistical Office, Germany