#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2003/28

14 April 2003

# ENGLISH ONLY

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-third session,  30 June-4 July 2003,

# agenda item 2)

# TRANSPORT OF GASES

Miscellaneous proposals relative to pressure receptacles for Class 2

## Transmitted by the expert from the United States of America

Introduction

Based on discussions concerning filling limits for pressure receptacles the expert from the United States of America agreed to sponsor a study by the National Institute for Standardization and Technology. The results of the study and a comparison of the NIST values and the P200 values are provided in the table provided as annex to this document.

Annex

Side-by-side comparison of filling ratio values from UN and DOT with the values calculated by NIST

| UN# | Name | Tc (C) ISO11622 | Ptest(bar) UN, abs. | Filling Ratio | Percentage Difference |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | UN | 49 CFR | NIST | UN VS NIST | NIST VS DOT | UN VS DOT |
| 3159 | 1,1,11,2-tetrafluoroethane (R134a) | 101.1 | 23 | 1.04 |  | 1.06 | 1.71 | N/A | N/A |
| 2035 | 1,1,1-trifluoroethane (R143a) | 73.1 | 36 | 0.75 |  | 0.79 | 5.66 | N/A | N/A |
| 1030 | 1,1-difluoroethane (R152a) | 113.5 | 19 | 0.79 | 0.82 | 0.79 | 0.51 | 0.51 | 0.00 |
| 1959 | 1,1-difluoroethylene | 29.7 | 251 | 0.77 | 0.80 | 0.77 | 0.18 | 5.37 | 5.19 |
| 1010 | 1,2-butadiene | 176.1 | 11 | 0.59 |  | 0.58 | -1.06 | N/A | N/A |
| 1958 | 1,2-dichloro-1,1,2,2-tetrafluoroethane (R114) | 145.7 | 11 | 1.30 |  | 1.31 | 0.81 | N/A | N/A |
| 1010 | 1,3-butadiene | 152 | 11 | 0.55 |  | 0.55 | 0.78 | N/A | N/A |
| 1012 | 1-butylene | 146.4 | 11 | 0.53 |  | 0.53 | -0.51 | N/A | N/A |
| 2517 | 1-chloro-1,1-difluoroethane (R142b) | 137.1 | 11 | 0.99 | 1.04 | 0.99 | 0.31 | -0.70 | -1.01 |
| 1021 | 1-chloro-1,2,2,2-tetrafluoroethane (R124) | na | 13 | 1.20 |  | 1.21 | 0.43 | N/A | N/A |
| 1983 | 1-chloro-2,2,2-trifluoroethane | 150 | 11 | 1.18 |  | 1.19 | 0.84 | N/A | N/A |
| 2044 | 2,2-dimethylpropane | 160.6 | 11 | 0.53 |  | 0.53 | -0.06 | N/A | N/A |
| 1001 | acetylene | na | 61 | na |  | 0.08 | na | N/A | N/A |
| 1001 | acetylene | na | 53 | na |  | 0.07 | na | N/A | N/A |
| 3374 | acetylene | na | 53 | na |  | 0.07 | na | N/A | N/A |
| 3374 | acetylene | na | 61 | na |  | 0.08 | na | N/A | N/A |
| 1005 | Ammonia, Anhydrous | 132.4 | 34 | 0.53 | 0.56 | 0.55 | 4.07 | 2.10 | -1.89 |
| 2188 | arsine | 99.9 | 43 | 1.10 |  | 1.17 | 5.97 | N/A | N/A |
| 1741 | boron trichloride | 178.8 | 11 | 1.19 |  | 1.20 | 0.83 | N/A | N/A |
| 1008 | boron trifluoride, BF3 | -12.2 | 226 | 0.72 |  | 0.76 | 6.56 | N/A | N/A |
| 1008 | boron trifluoride, BF3 | -12.2 | 301 | 0.86 |  | 0.89 | 3.77 | N/A | N/A |
| 2901 | bromine chloride | na | 11 | 1.50 |  | 0.00 |  | N/A | N/A |
| 1745 | bromine pentafluoride | na | 11 | na |  | 2.26 | na | N/A | N/A |
| 1746 | bromine trifluoride | na | 11 | na |  | 2.49 | na | N/A | N/A |
| 2419 | bromotrifluoroethylene | 184.8 | 11 | 1.19 |  | 1.64 | 37.97 | N/A | N/A |
| 1009 | Bromotrifluoromethane | 66.8 | 121 | 1.44 |  | 1.47 | 1.98 | N/A | N/A |
| 1009 | Bromotrifluoromethane | 66.8 | 251 | 1.60 |  | 1.59 | -0.39 | N/A | N/A |
| 1009 | Bromotrifluoromethane (R13B1) | 66.8 | 43 | 1.13 | 1.35 | 1.31 | 15.66 | 5.12 | -9.73 |
| 1011 | Butane | 152 | 11 | 0.51 |  | 0.52 | 1.36 | N/A | N/A |
| 1013 | Carbon Dioxide | 30.1 | 191 | 0.66 | 0.77 | 0.68 | 2.28 | -0.74 | -3.03 |
| 1013 | Carbon Dioxide | 30.1 | 251 | 0.75 | 0.80 | 0.76 | 1.83 | 10.96 | 9.33 |
| 2417 | carbonyl fluoride | 14.7 | 201 | 0.47 |  | 0.72 | 52.98 | N/A | N/A |
| 2417 | carbonyl fluoride | 14.7 | 301 | 0.70 |  | 0.83 | 18.28 | N/A | N/A |
| 2204 | carbonyl sulphide | 102 | 27 | 0.84 |  | 0.89 | 5.87 | N/A | N/A |
| 1017 | chlorine | 144 | 23 | 1.25 | 1.32 | 1.25 | 0.17 | 0.17 | 0.00 |
| 2548 | chlorine pentafluoride | 142.6 | 14 | 1.49 |  | 1.61 | 7.78 | N/A | N/A |
| 1749 | chlorine trifluoride | 153.7 | 31 | 1.40 |  | 1.57 | 11.98 | N/A | N/A |
| 1974 | chlorodifluorobromomethane | 153.7 | 11 | 1.61 |  | 1.63 | 1.36 | N/A | N/A |
| 1018 | Chlorodifluoromethane (R22) | 96.2 | 30 | 1.03 | 1.07 | 1.04 | 0.97 | -0.97 | -1.94 |
| 1020 | Chloropentafluoroethane (R115) | 80 | 26 | 1.08 | 1.14 | 1.11 | 2.51 | 0.64 | -1.85 |
| 1022 | Chlorotrifluoromethane (R13) | 28.8 | 101 | 0.83 |  | 0.82 | -0.89 | N/A | N/A |
| 1022 | Chlorotrifluoromethane (R13) | 28.8 | 121 | 0.90 |  | 0.90 | -0.15 | N/A | N/A |
| 1022 | Chlorotrifluoromethane (R13) | 28.8 | 191 | 1.04 | 1.11 | 1.04 | -0.11 | 3.74 | 3.85 |
| 1022 | Chlorotrifluoromethane (R13) | 28.8 | 251 | 1.10 |  | 1.11 | 0.73 | N/A | N/A |
| 1012 | cis-2-butylene | 162.4 | 11 | 0.55 |  | 0.56 | 1.70 | N/A | N/A |
| 1026 | cyanogen | 126.6 | 101 | 0.70 |  | 0.79 | 13.04 | N/A | N/A |
| 1589 | cyanogen chloride | 215 | 21 | 1.03 |  | 1.06 | 3.37 | N/A | N/A |
| 2601 | cyclobutane | 186.8 | 11 | 0.63 |  | 0.63 | 0.23 | N/A | N/A |
| 1027 | cyclopropane | 125.2 | 21 | 0.53 | 0.58 | 0.55 | 4.07 | 0.28 | -3.77 |
| 1911 | diborane | 16 | 251 | 0.07 |  | 0.30 | 323.28 | N/A | N/A |
| 1028 | Dichlorodifluoromethane (R12) | 112 | 19 | 1.15 | 1.21 | 1.16 | 0.86 | -2.60 | -3.48 |
| 1029 | dichlorofluoromethane (R21) | 178.5 | 11 | 1.23 |  | 1.24 | 0.98 | N/A | N/A |
| 2189 | dichlorosilane | 176.3 | 11 | 0.90 |  | 1.10 | 22.53 | N/A | N/A |
| 3252 | Difluoromethane (R32) | 78 | 49 | 0.78 |  | 0.82 | 5.20 | N/A | N/A |
| 1033 | dimethyl ether | 126.9 | 19 | 0.58 |  | 0.58 | 0.71 | N/A | N/A |
| 1032 | dimethylamine | 164.6 | 11 | 0.59 | 0.62 | 0.59 | 0.07 | 0.07 | 0.00 |
| 1035 | Ethane | 32.3 | 96 | 0.25 |  | 0.25 | 1.20 | N/A | N/A |
| 1035 | Ethane | 32.3 | 121 | 0.29 | 0.38 | 0.30 | 4.08 | -18.61 | -23.45 |
| 1035 | Ethane | 32.3 | 301 | 0.39 | 0.39 | 0.40 | 2.59 | 8.03 | 5.64 |
| 1037 | ethyl chloride | 187.2 | 11 | 0.80 |  | 0.81 | 1.14 | N/A | N/A |
| 2453 | ethyl fluoride | 102.2 | 31 | 0.57 |  | 0.63 | 10.59 | N/A | N/A |
| 1039 | ethyl methyl ether | 164.7 | 11 | 0.64 |  | 0.63 | -1.81 | N/A | N/A |
| 2452 | ethylacetylene | 190.5 | 11 | 0.57 |  | 0.59 | 2.89 | N/A | N/A |
| 1036 | ethylamine | 183.4 | 11 | 0.61 |  | 0.61 | 0.58 | N/A | N/A |
| 1962 | Ethylene | 9.2 | 226 | 0.34 | 0.35 | 0.34 | 1.34 | 10.02 | 8.82 |
| 1962 | Ethylene | 9.2 | 301 | 0.37 | 0.39 | 0.38 | 2.66 | 6.54 | 4.05 |
| 1040 | ethylene oxide | 195.8 | 16 | 0.78 |  | 0.79 | 1.38 | N/A | N/A |
| 2192 | germane | 34.8 | 251 | 1.02 |  | 1.00 | -2.05 | N/A | N/A |
| 3296 | heptafluoropropane (R227ea) | 100 | 16 | 1.20 |  | 1.22 | 1.62 | N/A | N/A |
| 2420 | hexafluoroacetone | 84.1 | 23 | 1.08 |  | 1.14 | 5.78 | N/A | N/A |
| 2193 | Hexafluoroethane (R116) | 19.7 | 201 | 1.10 |  | 1.13 | 2.95 | N/A | N/A |
| 1858 | hexafluoropropylene | 86.2 | 23 | 1.11 |  | 1.13 | 1.93 | N/A | N/A |
| 1048 | hydrogen bromide | 89.9 | 61 | 1.54 |  | 1.52 | -1.17 | N/A | N/A |
| 1050 | hydrogen chloride | 51.5 | 101 | 0.30 |  | 0.38 | 25.88 | N/A | N/A |
| 1050 | hydrogen chloride | 51.5 | 121 | 0.56 |  | 0.59 | 5.61 | N/A | N/A |
| 1050 | hydrogen chloride | 51.5 | 151 | 0.67 |  | 0.66 | -0.79 | N/A | N/A |
| 1050 | hydrogen chloride | 51.5 | 201 | 0.74 | 0.78 | 0.72 | -2.35 | 10.05 | 12.16 |
| 1051 | hydrogen cyanide | 183.5 | 101 | 0.55 |  | 0.61 | 11.56 | N/A | N/A |
| 1052 | hydrogen fluoride | na | 11 | 0.84 |  | 0.83 | -0.72 | N/A | N/A |
| 2197 | hydrogen iodide | 150.8 | 24 | 2.25 |  | 2.28 | 1.19 | N/A | N/A |
| 2202 | hydrogen selenide | 138 | 32 | 1.60 |  | 1.57 | -1.91 | N/A | N/A |
| 1053 | hydrogen sulphide | 100 | 56 | 0.67 | 0.70 | 0.68 | 1.69 | 8.27 | 6.72 |
| 2495 | iodine pentafluoride | na | 11 | na |  | 2.95 | na | N/A | N/A |
| 1969 | Isobutane | 134.9 | 11 | 0.49 |  | 0.49 | 0.38 | N/A | N/A |
| 1055 | isobutylene | 144.7 | 11 | 0.52 |  | 0.53 | 1.49 | N/A | N/A |
| 1062 | methyl bromide | 194 | 11 | 1.51 |  | 1.51 | 0.26 | N/A | N/A |
| 1063 | methyl chloride | 143 | 18 | 0.81 | 0.85 | 0.82 | 0.98 | -2.70 | -3.70 |
| 2454 | Methyl Fluoride (R41) | na | 301 | 0.36 |  | 0.63 | 74.95 | N/A | N/A |
| 1064 | methyl mercaptan | 196.8 | 11 | 0.78 | 0.83 | 0.79 | 0.89 | N/A | N/A |
| 1061 | methylamine | 156.9 | 14 | 0.58 | 0.62 | 0.59 | 1.74 | -1.68 | -3.45 |
| 1067 | nitrogen dioxide | 158 | 11 | 1.30 |  | 1.31 | 0.48 | N/A | N/A |
| 2451 | Nitrogen Trifluoride | -39.3 | 201 | 0.50 |  | 0.63 | 26.79 | N/A | N/A |
| 2451 | Nitrogen Trifluoride | -39.3 | 301 | 0.75 |  | 0.82 | 9.80 | N/A | N/A |
| 1069 | nitrosyl chloride | 167.5 | 14 | 1.10 | 1.21 | 1.15 | 4.27 | 4.09 | 0.00 |
| 1070 | nitrous oxide | 36.4 | 181 | 0.68 |  | 0.66 | -2.23 | N/A | N/A |
| 1070 | nitrous oxide | 36.4 | 226 | 0.74 | 0.77 | 0.73 | -1.16 | 7.03 | 8.11 |
| 1070 | nitrous oxide | 36.4 | 251 | 0.75 |  | 0.76 | 1.01 | N/A | N/A |
| 2422 | octafluorobut-2-ene | 98.3 | 13 | 1.34 |  | 1.31 | -1.92 | N/A | N/A |
| 1976 | Octafluorocyclobutane (RC318) | 115.3 | 12 | 1.34 |  | 1.33 | -0.94 | N/A | N/A |
| 2424 | Octafluoropropane (R218) | 71.9 | 26 | 1.09 |  | 1.13 | 3.70 | N/A | N/A |
| 3220 | Pentafluoroethane (R125) | 66.3 | 50 | 0.95 |  | 1.03 | 8.63 | N/A | N/A |
| 3220 | Pentafluoroethane (R125) | 66.3 | 37 | 0.72 |  | 1.00 | 38.63 | N/A | N/A |
| 3083 | perchloryl fluoride | 95.2 | 34 | 1.21 |  | 1.23 | 1.49 | N/A | N/A |
| 3154 | perfluoroethylvinylether | 132.8 | 11 | 0.98 |  | 1.22 | 24.22 | N/A | N/A |
| 3153 | perfluoromethylvinylether | 87 | 21 | 0.75 |  | 1.05 | 40.16 | N/A | N/A |
| 1076 | phosgene | 182.3 | 21 | 1.23 |  | 1.24 | 1.10 | N/A | N/A |
| 2199 | phosphine | 51.9 | 226 | 0.30 | 0.00 | 0.50 | 67.15 | N/A | N/A |
| 2199 | phosphine | 51.9 | 251 | 0.45 |  | 0.51 | 13.80 | N/A | N/A |
| 2198 | phosphorous pentafluoride | 19 | 201 | 0.90 |  | 1.12 | 24.45 | N/A | N/A |
| 2198 | phosphorous pentafluoride | 19 | 301 | 1.34 |  | 1.25 | -6.94 | N/A | N/A |
| 2200 | propadiene | 120.7 | 23 | 0.50 |  | 0.51 | 2.66 | N/A | N/A |
| 1978 | Propane | 96.8 | 26 | 0.42 |  | 0.43 | 2.62 | N/A | N/A |
| 1077 | Propylene | 92.4 | 31 | 0.43 |  | 0.44 | 2.25 | N/A | N/A |
| 3337 | R404A | na | 37 | 0.82 |  | 0.89 | 8.56 | N/A | N/A |
| 3338 | R407A | na | 37 | 0.94 |  | 0.99 | 4.81 | N/A | N/A |
| 3339 | R407B | na | 39 | 0.93 |  | 1.00 | 7.53 | N/A | N/A |
| 3340 | R407C | na | 36 | 0.95 |  | 0.98 | 3.49 | N/A | N/A |
| 2602 | R500 | na | 23 | 1.01 |  | 1.00 | -0.77 | N/A | N/A |
| 1973 | R502 | na | 32 | 1.05 |  | 1.05 | -0.22 | N/A | N/A |
| 2599 | R503 | na | 32 | 0.11 |  | 0.12 | 8.90 | N/A | N/A |
| 2599 | R503 | na | 43 | 0.20 |  | 0.17 | -12.71 | N/A | N/A |
| 2599 | R503 | na | 101 | 0.66 |  | 0.64 | -3.37 | N/A | N/A |
| 2194 | selenium hexafluoride | na | 37 | 1.46 |  | 1.77 | 21.22 | N/A | N/A |
| 2203 | silane | -3.5 | 226 | 0.32 |  | 0.33 | 3.84 | N/A | N/A |
| 2203 | silane | -3.5 | 251 | 0.36 |  | 0.35 | -4.03 | N/A | N/A |
| 1859 | silicon tetrafluoride | -14.2 | 201 | 0.74 |  | 0.96 | 30.31 | N/A | N/A |
| 1859 | silicon tetrafluoride | -14.2 | 301 | 1.10 |  | 1.17 | 6.62 | N/A | N/A |
| 2676 | stibine | 173 | 21 | 1.20 |  | 1.94 | 61.47 | N/A | N/A |
| 1079 | Sulphur Dioxide | 157.5 | 15 | 1.23 | 1.28 | 1.23 | -0.04 | -1.66 | -1.63 |
| 1080 | Sulphur Hexafluoride | 45.6 | 71 | 1.04 |  | 1.06 | 2.23 | N/A | N/A |
| 1080 | Sulphur Hexafluoride | 45.6 | 141 | 1.33 | 1.36 | 1.34 | 0.62 | 10.33 | 9.77 |
| 1080 | Sulphur Hexafluoride | 45.6 | 161 | 1.37 |  | 1.38 | 0.39 | N/A | N/A |
| 2418 | sulphur tetrafluoride | 91 | 31 | 0.91 |  | 1.37 | 50.59 | N/A | N/A |
| 2191 | sulphuryl fluoride | 91 | 51 | 1.10 | 1.19 | 1.12 | 2.13 | 5.64 | 3.64 |
| 2195 | telurium hexafluoride | 83.2 | 21 | 1.00 |  | 2.37 | 137.02 | N/A | N/A |
| 1081 | tetrafluoroethylene | 33.3 | 201 | na | 1.10 | 1.04 | na | 13.83 | N/A |
| 1982 | Tetrafluoromethane (R14) | -45.7 | 201 | 0.62 |  | 0.71 | 14.76 | N/A | N/A |
| 1982 | Tetrafluoromethane (R14) | -45.7 | 301 | 0.94 |  | 0.90 | -4.76 | N/A | N/A |
| 1012 | trans-2-butylene | 155.5 | 11 | 0.54 |  | 0.54 | 0.18 | N/A | N/A |
| 3057 | trifluoroacetylchloride | 109 | 18 | 1.17 |  | 1.21 | 3.41 | N/A | N/A |
| 1082 | trifluorochloroethylene | 105.8 | 20 | 1.13 | 1.17 | 1.12 | -1.20 | -3.00 | -1.77 |
| 1984 | Trifluoromethane (R23) | 26 | 191 | 0.87 |  | 0.88 | 1.19 | N/A | N/A |
| 1984 | Trifluoromethane (R23) | 26 | 251 | 0.95 |  | 0.96 | 1.02 | N/A | N/A |
| 1083 | trimethylamine | 160.2 | 11 | 0.56 | 0.59 | 0.57 | 1.40 | -0.38 | -1.79 |
| 2196 | tungsten hexafluoride | 170 | 11 | 2.70 |  | 3.13 | 15.74 | N/A | N/A |
| 1085 | vinyl bromide | 198 | 11 | 1.37 |  | 1.38 | 0.79 | N/A | N/A |
| 1086 | vinyl chloride | 156.5 | 13 | 0.81 | 0.85 | 0.82 | 0.79 | -2.89 | -3.70 |
| 1860 | vinyl fluoride | 54.7 | 251 | 0.64 | 0.65 | 0.65 | 1.27 | 4.34 | 3.13 |
| 1087 | vinyl methyl ether | 171.6 | 11 | 0.67 | 0.71 | 0.67 | 0.68 | -0.81 | -1.49 |
| 2036 | Xenon | 16.6 | 131 | 1.24 |  | 1.28 | 3.13 | N/A | N/A |

Note: Colors indicate approximate level of uncertainty in density calculation.

Yellow: these fluids have dedicated equations of state; uncertainty less than 1%

Blue: estimated with extended corresponding states model using experimental data to obtain parameters; uncertainty less than 3%

Green: estimated with extended corresponding states model with estimated parameters and limited data; uncertainly greater than 3%

na = Data Not Available

N/A = DOT Data Not Available

NIST = National Institute of Standards and Technology

DOT = U.S. Department of Transportation

UN = United Nations Model Regulations (See Table P200 for Filling Ratios)

# Text boxes

STSTE

Secretariat