|  |  | INF.28/Rev.1 |
| --- | --- | --- |

P903 (b)

Used cells and batteries, with a gross weight of not more than [40 g] collected for disposal, together with other used batteries or alone, may be carried, without being individually protected, under the following conditions:

(1) In 1H2 drums or 4H2 boxes conforming the packing group II performance level for solids;

(2) In collecting trays with a gross mass of less than 30 kg made from non-conducting material meeting the general conditions of 4.1.1.1, 4.1.1.2. and 4.1.1.5. to 4.1.1.8.

Additional requirements The empty space in the packaging shall be filled with appropriate cushioning material so as to restrict the relative movements of the batteries during carriage. Hermetically sealed packagings shall be fitted with a venting device according to subsection 4.1.1.8. The venting device shall be so designed that an overpressure cause by gases does not exceed 10 kPa.

"636 (a)	Used cells and batteries collected and presented for carriage between the place where they are collected from consumers and the disposal facility, together with other batteries or alone, are not subject to the other provisions of RID/ADR if they meet the following conditions:

(i)	The gross weight of each cell or battery does not exceed [40 g];

(ii)	The provisions of instruction P903 (b) (2) are complied with;"

-----------------------------------