## Slide 1
“CUT-OFF” LINE IN AFS DRAFT REGULATION EXPLANATION TO INFORMAL DOCUMENT No. 8
Tomasz Targosiński
Poland
This document is distributed to the Experts on Lighting and Light-Signalling only.
The document as a whole or in parts cannot be used for other purposes than GRE without written permission of the author.
Informal document No. 9
(50th GRE, 7-11 April 2003,
agenda item 3.2.)

## Slide 2: INFLUENCE OF TOLERANCES OF VERTICAL AIMING ON LIGHTING RANGE AFS CLASS C (BASIC) PASSING BEAM
According to Draft XXX proposals:
Annex 9 P. 1.2.1. the "horizontal part" does not exceed a vertical extent of  = 0.2 deg up or down
Annex 3 Table 2 Class C (basic): the “cut-off” shall be positioned at 0.57deg
In case of using a standard headlamp at standard mounting height at 0.75m, assuming „cut-off” line tolerance of Δβ = 0.2deg, lighting range will vary 56m to 116m, which can be accepted.

## Slide 3: INFLUENCE OF TOLERANCES OF VERTICAL AIMING ON LIGHTING RANGE AFS CLASS E (MOTORWAY) AND CLASS W (WET ROAD) PASSING BEAM
According of Draft XXX proposal:
Annex 3 Table 2 Class E (motorway) and W(wet road):
the “cut-off” shall be positioned not above 0.23deg and not below 0.57deg
In case of using AFS Class E and W passing beams of one pair of lighting units at standard height of 0.75m, lighting range will vary from 56m to 1430m (considering rising of the beam from 0.57degD to 0.23degD) when tolerance of vertical aiming is Δβ = 0.2deg.

## Slide 4: INFLUENCE OF TOLERANCES OF VERTICAL AIMING ON LIGHTING RANGE AFS CLASS E (MOTORWAY) AND CLASS W (WET ROAD) PASSING BEAM
Conclusion: „Horizontal part” of „cut-off” shall be aimed with tolerance of not more than Δβ = 0.1deg.
To obtain the same lighting range for AFS lighting units mounted at 0.3m as for AFS lighting units mounted at standard mounting height 0.75m, the “horizontal part” shall be positioned not below 0.23degD and not above 0.09degD.
Problems considering Δβ = 0.2deg:
  lighting range on the road surface can change from 40m to „infinity”
  „cut-off” can be positioned over 0.43degD and under 0.11degU over horizon. This
  can cause direct intensive glare

## Slide 5: DOUBLE „CUT-OFF” LINE PHENOMENON AIMING ON 25M MEASURING SCREEN
According of Draft XXX proposal:
Annex 9 P.3.1. Measurements of the illumination E on the aiming screen are performed by vertical scanning through the “horizontal part” of “cut-off”(...) at a 10 m distance or at any greater distance ...

## Slide 6: DOUBLE „CUT-OFF” LINE PHENOMENON AIMING ON 10M MEASURING SCREEN
Conclusion: “Cut-off” line of each lighting unit, and not “cut-off” line of passing beam or installation unit, has to be aimed separately to avoid multiple „cut-off” line problem.
Double „cut-off” line can be the result of projection of „cut-off” lines coming from two or more lighting units.

## Slide 7: PROPOSAL OF OF “CUT-OFF” LINE AIMING BEFORE MEASUREMENTS
New definition: INITIAL LIGHTING UNIT - lighting unit specified by an applicant used for aiming the „cut-off” line before photometric measurements (TRANS/WP.29/GRE/2002/44rev.1)
Suggested procedure of aiming of the “cut-off” line:
1. Aiming the „cut-off” line for initial lighting unit.
2. Measuring the illumination E for lighting units incorporated in installation unit and not separately aimed.

## Slide 8: AMBIGUITIES OF „CUT-OFF” LINE DESCRIPTION IN DRAFT XXX
In many places of Draft XXX there is no clear distinction between “cut-off” line of passing beam and “cut-off” line of lighting unit e.g.:
According of Draft XXX proposals:
Annex 9 P.1. The "cut-off" line of a passing beam shall comply with the following
requirements ...
Annex 9 P.2.1 For lighting units contributing to the passing beam but providing no
“cut-off” or a horizontal “cut-off” line only ...
Annex 9 P.2.3. For each class, other than the class C (basic) passing beam: the shape and position of the "cut-off", if any, shall comply ...
Conclusion: Description of “cut-off” line of lighting unit should only be used.

## Slide 9: P.1.1. The "cut-off" line shall consist of (...) (iii) one clear "kink", [ambiguous definition] P.1.3. If there is no distinct "kink", the "kink point" shall be considered to be that point, where the 60 deg tangential line to the "shoulder line part" (...) [proposal in TRANS/WP.29/GRE/2002/44 rev.1] P.1.2.1. ... "horizontal part" does not exceed a vertical extend of  = 0.2 deg up or down within 0.5 deg and 4.5 deg left from the "kink"; ... [proposal in TRANS/WP.29/GRE/2002/44 rev.1] P.2.2.1. If the "horizontal part" of the "cut-off" line does not provide sufficient linearity and/or sharpness for a visual vertical adjustment the "cut-off" quality shall be evaluated for compliance with provisions laid down in paragraph 3. below,according to the discretion of the Technical Service. [ambiguous description] P.3. "cut-off" quality evaluation: P.3.1. ... After visual horizontal adjustment according to paragraph 2.1. above, the scanning is done at 1.5 deg, 2.5 deg and 3.5 deg left of V-V. [proposal in TRANS/WP.29/GRE/2002/44 rev.1]
COMMENTS AND SUGGESTIONS

## Slide 10: RESULTS DEPENDING ON USAGE OF „SHOULDER LINE PART” TOLERANCES
„Cut-off” line can be aimed differently depending on using or not using 0.2 deg tolerance of A and B lines:
1. If tolerances of lines A and B do not apply, green position “cut-off” line is obtained.
2. If tolerances of lines A and B apply, red position “cut-off” line is obtained.
Conclusion: Tolerances of A and B lines ±Δβ lead to different results of „cut-off” line aiming.
Proposal: Remove A and B lines ±Δβ tolerances from Draft XXX.
(as in TRANS/WP.29/GRE/2002/44rev.1)

## Slide 11: POSITION OF 60DEG TANGENTIAL LINE
Some of lighting units can have more than one „kink point” in „cut-off” line and it is difficult to decide which one is correct with respect to the tangential line inclined 60 deg to the „shoulder line part”.
Proposal: „Shoulder part” shall be approximated by slant line.
(Compare examples of “cut-off” line approximation)

## Slide 12: RESULTS OF DISCONTINUITY (THRESHOLD) OF „SHOULDER LINE PART”

## Slide 13: If there is discontinuity on the „shoulder line part” of „cut-off” line, there are two different possible ways of finding „kink point”: - using visual approximation by prolonging slant part of „cut-off” line - using 60deg tangential line According to Draft XXX the quality of horizontal part of „cut-off” is checked in three points (1.5deg, 2.5deg, 3.5deg) only. Results will depend on this way.
Conclusion: If “horizontal part” of „cut-off” line has small blur part, then in one situation the „cut-off” line quality can be estimated as correct and in the other as incorrect depending on chosen way of finding „kink point”.
RESULTS OF DISCONTINUITY OF „SHOULDER LINE PART”

## Slide 14: BLURRED „KINK POINT”
If the „kink point” is blurred it is difficult to locate correct place of „kink” and conclusion is similar to the previous example.

## Slide 15: DOUBLE „SHOULDER LINE PART”
If there is a double „shoulder line part”, there is a double „kink point”.

## Slide 16: PROPOSAL OF IMPROVING THE METHOD OF CUT-OFF LINE DETERMINING AND AIMING
Proposals of changes:
1. Vertical scanning „cut-off” line every 0.1deg
2. Tolerance range of the most „horizontal part” should be ±0.1deg.
3. 80% of „horizontal part” should be placed within ±0.2 deg tolerance range.
4. „Shoulder line part” should be approximated by slant line.

## Slide 17: THE PROCEDURE OF INSTRUMENTAL ADJUSTMENT OF „CUT-OFF” LINE EXAMPLE as proposed in TRANS/WP.29/GRE/2002/44 Rev.1

## Slide 18
VISUAL PRE-AIMING
VISUAL APPROXIMATION OF „CUT-OFF” LINE
Remark: Even if visual pre-aiming is not enough precise, the result of the proposed procedure will be correct.

## Slide 19
FIRST VERTICAL ADJUSTMENT
ORIGINAL STEP OF THE LOOP
Determining original approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.1.

## Slide 20
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.2.

## Slide 21
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 22
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 23
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 24
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 25
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 26
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 27
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 28
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 29
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 30
FIRST VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 31
FIRST VERTICAL ADJUSTMENT
FINAL STEP OF THE LOOP
First approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 32
Start „kink point” - horizontal place of visual pre-aiming
Initial „kink point” - result of first loop of procedure
Original approximation of „shoulder line part” and position of „kink point”, according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.2.1.
Remark: The position of initial “kink point” is very close to the position
of final “kink point”, independently of visual pre-aiming precision.
FIRST HORIZONTAL ADJUSTMENT
ORIGINAL STEP OF THE LOOP

## Slide 33
FIRST HORIZONTAL ADJUSTMENT
FINAL STEP OF THE LOOP
First approximation of “shoulder line part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1.

## Slide 34
SECOND VERTICAL ADJUSTMENT
ORIGINAL STEP OF THE LOOP
Determining the original approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.1.

## Slide 35
SECOND VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.2.

## Slide 36
SECOND VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.

## Slide 37
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.
SECOND VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP

## Slide 38
Determining the next approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.
SECOND VERTICAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP

## Slide 39
Second approximation of “horizontal part”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.1.3.
SECOND VERTICAL ADJUSTMENT
FINAL STEP OF THE LOOP

## Slide 40
SECOND HORIZONTAL ADJUSTMENT
ORIGINAL STEP OF THE LOOP
Original approximation of “shoulder line part” and position of “kink point”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.2.1.

## Slide 41
SECOND HORIZONTAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP
Determining the next approximation of “shoulder line part” and position of “kink point”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.2.2.

## Slide 42
Determining the next approximation of “shoulder line part” and position of “kink point”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.2.3.
SECOND HORIZONTAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP

## Slide 43
Determining the next approximation of “shoulder line part” and position of “kink point”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.2.3.
SECOND HORIZONTAL ADJUSTMENT
FOLLOWING STEP OF THE LOOP

## Slide 44
SECOND HORIZONTAL ADJUSTMENT
FINAL STEP OF THE LOOP
Second approximation of “shoulder line part” and position of “kink point”,
according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.2.3.

## Slide 45
Result of instrumental adjustment procedure, according to TRANS/WP.29/GRE/2002/44 Rev 1. Annex 9 p. 4.3.
Conclusion: Instrumental approximation of “cut-off” line is very consistent with average visual position of “cut-off” line.
FINAL RESULT OF THE PROCEDURE
INSTRUMENTAL APPROXIMATION OF “CUT-OFF” LINE

## Slide 46: EXAMPLES OF REAL „CUT - OFF” LINES OF STANDARD HEADLAMPS EXPLAINING AMBIGUITIES OF DEFINITIONS PROPOSED IN AFS DRAFT XXX Remark: Please, pay attention to multiplied “kink points”, different kinds of “kink points”, linear approximations of “shoulder line parts” and distances between “kink points” and maximums of illumination.

## Slide 47
DISCONTINUITY ON „HORIZONTAL PART”
Green line - instrumental approximation of „cut-off” line
Red points - points described in Draft XXX Annex 9 which form real „cut-off” line
Blue points - points of real cut-off line agreeing with approximation