## Slide 1
EPA’s Proposal for Nonroad Diesel Engines & Fuel
May 2003
U.S. Environmental Protection Agency
Office of Transportation and Air Quality
Informal document No. 13
(46th GRPE, 19-23 May 2003,
agenda item 10.)

## Slide 2: Scope of the Proposal
Proposal applies to nonroad diesels of all sizes, from 3 to 3,000 hp
  Used in a diversity of applications-- construction, farming, mining, industrial
Proposed fuel provisions apply to fuel used in nonroad diesels, locomotives, and marine engines
  But not to home heating fuel
  Nonroad fuel is not currently regulated by EPA
Proposal addresses serious health and welfare impacts from nonroad diesel fuel and equipment--
  ozone, fine PM
  in addition, diesel exhaust is likely to be carcinogenic to humans
These sources currently contribute 44% of total mobile source diesel PM and 12% of total mobile source NOx nationwide.
  Their contributions range even higher in many urban areas and will grow in the future.
Notes: 3P base / HD07 control Inventories
Virtually identical with three exceptions:
EGU (electric power companies) uses a more recent IPM model run
Relatively small nationwide
- removed emissions of residential incineration (cities stopped burning trash in apartment buildings in the 19902)
- growth projections for prescribed burning
  National forest service estimate seemed high
  Substantial increase in PM in south and west, even in the east with Georgia, Louisiana, Arkansas, and north Carolina).
Monitoring year
  HD07 1999
  3P 1999-2000

## Slide 3: Proposal Overview
A systems approach of reducing nonroad fuel sulfur levels to enable advanced emission control technology
  similar to 2007 diesel truck and fuel rule
500 ppm maximum sulfur nonroad diesel fuel in 2007
  based on substantial health benefits from sulfate and PM reductions
15 ppm nonroad fuel in 2010
  to enable engine standards
Engine standards representing reductions of >95% PM and ~90% NOx
  Standards phase in starting in 2008, fully phased in by 2014
Enhanced certification test requirements to ensure in-use emissions reductions