## Slide 1
WORKING GROUP 18
Jean-Yves LE COZ
Chairman
CHILD OCCUPANT SAFETY
Informal document No. GRSP-34-25

## Slide 2
Accidentology in cars...
In 1998 : 2 children killed each day as car passenger on European roads
From 1995 to 1999, number of children killed or injured is decreasing, situations contrasted according to countries

## Slide 3
European database - IRTAD
  Global comparison between 29 countries or regions
  No in-depth analysis
National databases
  Germany, France, United Kingdom, Sweden, Italy, Spain
  No compatibility
Results:
International databases are not sufficiently focussed on child safety to have a clear & detailled view of the situation.
Harmonization of accidentological data in EU to have a significant base statistically usable, credible and representative
Overview of existing databases

## Slide 4
Specific databases
  Mainly dealing for research
    CREST/CHILD: 628 restrained children
  Not representative of real world but focussed on severe crashes.
  Very detailled for - restraint systems,
  - crash severity and configuration, - injury description
  Only frontal and side impacts.
    CCIS: 425 children
  Not representative of real world but usefull for finding injuries.
  Type of restraint not always known
  Complete medical reports available.
    GIDAS: 168 children
  Most of the cases with severe injuries (AIS 2 +) are in the CREST
  database or to be input in the CHILD database.
Overview of existing databases

## Slide 5
Specific databases
  Mainly dealing for research
    LAB gn96: 1327 children
  Representative of car to car and car to obstacle crashes countryside
  crashes in France.
  Very detailled for - restraint systems,
  - crash severity and configuration, - injury description.
  Data on frontal, side, rear impacts and roll overs.
    Questionnaire : 230 children
  Not representative and injury level is defined by parents,
  Over-representativity of rear impacts.
    GDV : more than 350 children
  Most of the cases with severe injuries (AIS 2 +) are in the CRESTdb or
  to be input in the CHILD database.
Overview of existing databases

## Slide 6
Restrained children are better protected than unrestrained, especially when using an appropriate CRS.
The risk of severe injuries is small for properly restrained children up to a deltaV of 40 km/h in frontal impacts.
Swedish experience shows good results with rearward facing systems for children up to 3 years of age
Existing CRS have been mainly designed for protection in frontal impact.
CRS protection in side impacts is not sufficient
Determination of major injury mechanisms / type of CRS is possible for different type of impacts
General conclusions from databases

## Slide 7
EEVC WG 18 points out items
  for frontal impacts :
  Test bench (geometrical + properties)
  Severity of test (shape of pulse)
  Biofidelity and instrumentation of dummies,
  Criteria based on body segments on which injuries occur.
  for side impacts :
  Introduction of side requirements,
  Biofidelity, instrumentation of dummies and associated criteria

## Slide 8
Background and development of dummies...
P-serie dummies are in R44 today:
  Familly is complete
  They were adapted for evaluation of protection
  in frontal impact.
  Probably not the optimal dummies for all impact directions.
  Some criteria used are not relevant anymore.
Q-serie dummies :
  Familly is not complete:
  Q3 in production, Q1 and Q6 ready for production
  Q0 is developped (first prototypes available in CHILD)
  Q1 1/2 is under development, Q10 is possible.
  Designed for all impact directions.
  Criteria are available for some body segments in frontal impacts (research programs are working on the subject)

## Slide 9
Background and development of dummies...
Hybrid III family
They are designed for evaluation of
protection in frontal impact.
H3, H6, H10
Born in 1992, updated 1997
Criteria are available for some body segments
in frontal impacts
CRABI dummies
6m, 12m, 18m
Designed for all impact directions.
With or without airbag interaction
Criteria are available for some body segments
in frontal impacts

## Slide 10
ECE R-44 :
Resultant thoracic acceleration and vertical component of this acceleration
Head displacement
US FMWSS213 :
+ limitation of the HIC value
What is new ?
ISO/TC22/SC12/WG6
Technical report with some injury risk curves
CREST program results
CHILD program results
Criteria and injury mechanisms

## Slide 11
Accidentology in coaches and buses
No official European database is available.
Some countries have statistical data on situation of children in coaches and buses
For protection of children in buses and coaches, specific legislations exist but there is no common position.
From experts point of view:
  Necessity to limit the number of children transported to the number of seats available in the vehicle.
  It is better, as the major risk is the ejection, to have all children after a certain age restrained with a 3 pt belt than having them unrestrained. For younger ones the use of additional CRS should be required.
  Retractor systems should be better than static systems

## Slide 12
Main conclusions…
Too many children are not / not properly restrained in EU. Information, misuse reduction, and police actions are necessary
Knowledge both in accidents research and biomechanics has made a significant step these last years and this allows to think of a revision of R44 .
Step by step introduction of dummies and criteria seems to be possible.
Pursuit of the development of a family of biofidelic dummies, integrating biomechanical criteria when available.
Estimate the importance and the effect of misuse, measure the impact of the introduction of ISOFIX devices on that sensible point.
WORKING GROUP 18