## Slide 1: WorldSID Update
By WorldSID Task Group
To GRSP
2nd – 6th June, 2003

## Slide 2: Pre-Production Dummy Evaluation
Pre-production dummies purchased by government and industry around world
3 dummies purchased from Asia/Pacific Region
4 dummies purchased from European Region
5 dummies purchased from the America’s Region
Dummy delivery began March 2003
11 dummies purchased with a minimum of 64 channels of DAS, 64 channels of instrumentation
11th dummy to be delivered by June 4, 2003. (12th dummy to be ordered late 2003)

## Slide 3: Pre-Production Evaluation Programme

## Slide 4: Pre-Production Evaluation (cont.)

## Slide 5: Next Steps
Complete the delivery of pre-production dummies
Worldwide regulatory bodies, OEMs, suppliers, and researchers evaluate pre-production dummies
Comprehensive evaluation to include biofidelity
(ISO requirements and others eg. IHRA) & all other aspects
Production design freeze September 25, 2003
Dummy design to production dummy level
Production dummies available March 2004
Dummy is regulation ready 1st Quarter 2004

## Slide 6: Latest Vehicle Testing Experience
Transport Canada
Toyota Camry – comparison with ES-2
Latest prototype dummy
Configuration
IIHS Barrier 1500 kg
Camry 2001 - no side airbags
Impact 50 km/h 0°
Seat position 13/ 16
WorldSID/ES-2

## Slide 7
General Impressions
WorldSID easy to handle and position.
No issues with instrumentation or data acquisition.
Transport Canada Observations

## Slide 8
Summary
WorldSID abdominal and pelvic instrumentation enhance sensitivity to interior door geometry.
WorldSID shoulder shrugs and flexes, ES-2 rotates out of the way.
WorldSID seating posture causes initial head placement to be more forward.
WorldSID & ES-2 display comparable thorax deflection response.
Transport Canada Observations (cont’d)

## Slide 9: Complete Evaluation Results
Full results of comprehsive Pre-Production Dummy evaluation programme available autumn 2003
www.worldsid.org