Distr.
GÉNÉRALE

ST/SG/AC.10/C.3/2004/90
	2 septembre 2004

FRANÇAIS
	Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT DES 
MARCHANDISES DANGEREUSES ET DU SYSTÈME 
GÉNÉRAL HARMONISÉ DE CLASSIFICATION ET 
D’ÉTIQUETAGE DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport 
des marchandises dangereuses

Vingt-sixième session, 29 novembre-3 décembre 2004
Point 3 b) de l’ordre du jour provisoire

QUESTIONS EN SUSPENS OU PROPOSITIONS D’AMENDEMENTS 
AUX RECOMMANDATIONS RELATIVES AUX
MARCHANDISES DANGEREUSES

Matières autoréactives

Nouvelle préparation à ajouter à la liste du 2.4.2.3.2.3

Communication du Japon

La nouvelle préparation mentionnée ci-dessous satisfait aux critères du numéro ONU 3228, type E. La formule de renseignements et le procès-verbal d’épreuve sont joints au présent document en tant qu’annexes 1 et 2 respectivement. Un agrément pour le transport maritime de ces produits a déjà été délivré par le Ministère japonais de l’aménagement du territoire, de l’infrastructure et des transports.

Ces produits sont transportés du Japon vers les États-Unis d’Amérique et la Chine depuis plusieurs années et aucun incident ou accident n’a été observé.

Il est proposé d’ajouter cette préparation pour les matières autoréactives à la liste du 2.4.2.3.2.3 afin d’autoriser le transport dans les conditions appropriées.

Proposition

Ajouter la préparation suivante à la liste des matières autoréactives déjà classées au 2.4.2.3.2.3:

| Matière autoréactive: | Diazo-naphtoquinone-1,2 sulfonate-5 du polymère acétone-pyrogallol |
| --- | --- |
| Concentration (%): | 100 |
| Méthode d’emballage: | OP8 |
| Température de régulation: | Néant |
| Température critique: | Néant |
| Rubrique générique ONU: | 3228 |
| Remarques: | Néant. |

## Annex 1 (ENGLISH ONLY)

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	Japan	Date 	May  25, 2004

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name	Acetone-pyrogallol copolymer 1,2-Naphthoquinonediazido-5-sulphonate

1.2	Chemical formula 	C24H21N3O6S1

1.3	Other names/synonyms	Acetone-pyrogallol copolymer 2-Diazo-1-naphthol-5-sulphonate

UN number  UN3228

CAS number  68584-99-6

1.5	Proposed classification for the Recommendations

1.5.1    proper shipping name (3.1.2)  Self-reactive solid type E

1.5.2    class/division 4.1	subsidiary risk(s)   None

packing group II

1.5.3    proposed special provisions, if any  274

1.5.4    proposed packing instruction(s)   P520

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range	>290 °C

2.2	Boiling point or range	not applicable

2.3	Relative density at :

2.3.1    15 °C	600kg/m3

2.3.2    20 °C	600kg/m3

2.3.3    50 °C	600kg/m3

2.4	Vapour pressure at :

2.4.1    50 °C	not applicable

2.4.2    65 °C	not applicable

2.5	Viscosity at 20 °C 	not applicable

2.6	Solubility in water at 20 °C	not soluble

2.7	Physical state at 20°C (2.2.1.11)	solid/liquid/gas2

2.8	Appearance at normal transport temperatures, including colour and odour

Yellow powder , odourless

2.9	Other relevant physical properties

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.31) 	not applicable

3.1.2	Is combustion sustained? (2.3.1.31) yes/no

3.2	Autoignition temperature 	not known

3.3	Flammability range (LEL/UEL)	not known

3.4	Is the substance a flammable solid? (2.4.21) yes/no

3.4.1	If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?	yes/no

If yes, state:

4.1.1	Inhibitor/stabilizer used

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.11)  yes/no

4.2.1 If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.41)	yes/no

4.3.1 If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.11)	yes/no

If yes, state:

4.4.1	exit box of flow chart    Exit E

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package?65°C

Is the temperature control required? (2.4.2.3.41)	yes/no

4.4.2	proposed control temperature for a 50 kg package	°C

4.4.3	proposed emergency temperature for a 50 kg package	°C

4.5	Is the substance pyrophoric? (2.4.31) 	yes/no

4.5.1 If yes, give details

4.6	Is the substance liable to self-heating? (2.4.31) 	yes/no

4.6.1 If yes, give details

4.7	Is the substance an organic peroxide (2.5.11) 	yes/no

If yes state:

4.7.1 exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package? 65 °C

Is temperature control required? (2.5.3.4.11) 	yes/no

4.7.2	proposed control temperature for a 50 kg package	°C

4.7.3	proposed emergency temperature for a 50 kg package	°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.41) 	yes/no

4.8.1 If yes, give details

4.9	Does the substance have oxidizing properties (2.5.11)	yes/no

4.9.1 If yes, give details

4.10	Corrosivity (2.81) to:	Not corrosive

4.10.1 mild steel 	mm/year 	 	at 	°C

4.10.2 aluminium	mm/year  	at	°C

4.10.3 other packaging materials (specify)

mm/year   at	°C

mm/year   at	°C

4.11	Other relevant chemical properties

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11)     19400	mg/kg	Animal species  rat

5.2	LD50, dermal (2.6.2.1.21)	mg/kg	Animal species

5.3	LC50, inhalation (2.6.2.1.31)		mg/litre	Exposure time	 hours

or		ml/m3	Animal species

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)	not applicable

5.5	Skin exposure (2.81) results	Exposure time   	24  hours

Animal species	rabbits

5.6	Other data

5.7	Human experience

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1    Fire (include suitable and unsuitable extinguishing agents)

Use Dry chemical, CO2 as extinguish media

6.1.2    Spillage

Eliminate all ignition sources. Do not touch or walk through spilled material by naked hands. Take up with spilled material using clean non-sparking tools and place into loosely covered plastic containers for later disposal. Prevent entry into floor drains, storm sewer, waterways or confined areas.

6.2	Is it proposed to transport the substance in:

6.2.1   Bulk Containers (6.81)		yes/no

6.2.2   Intermediate Bulk Containers (6.51)?	yes/no

6.2.3   Portable tanks (6.71)?			yes/no

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known)

9.2	Minimum test pressure

9.3	Minimum shell thickness

9.4	Details of bottom openings, if any

9.5	Pressure relief arrangements

9.6	Degree of filling

9.7	Unsuitable construction materials

Annex 2 (ENGLISH ONLY)

TEST REPORT

1.	Name of the Self-reactive solid: 	ACETONE-PYROGALLOL COPOLYMER

1,2-NAPHTHOQUINONEDIAZIDO-5-SULPHONATE

2.	General data

2.1	Composition	: 100%

2.2	Molecular formula	: C24H21N2O6S1

2.3	Physical form	: Solid

2.4	Colour	: Yellow

2.5	Density	: 600kg/m3

2.6	Particle diameter	: None

3.	Detonation (test series A)

Box 1 of the flow chart	: Does it propagate a detonation?

3.1	Method	: BAM 50/60 steel tube test (test A.1)

3.2	Sample conditions	: Temperature 26 °C, Humidity 70%

3.3	Observations	: Fragmented part of the tube: 11.6 cm

3.4	Result	: No

3.5	Exit	: 1.3

4. 	Deflagration (test series C)

Box 5 of the flow chart	: Can it propagate a deflagration?

4.1	Method 1	: Time/pressure test (test C.1)

4.2	Sample conditions	: Temperature 18 °C, Humidity 76%

4.3	Observations 	: No pressure rise to 300psi

4.4	Result 	: No

4.5	Method 2 	: Deflagration test (test C.2)

4.6	Sample conditions	: Temperature 16 °C , Humidity 74%

4.7	Observations	: Deflagration rate 0.15 mm/s

4.8	Result  	: No

4.9	Final result 	: No

4.10	Exit 	: 5.3

5.	Heating under confinement (test series E)

Box 9 of the flow chart	: What is the effect of heating it under defined confinement?

5.1	Method 1	: Koenen test (test E.1)

5.2	Sample conditions	: Temperature 20 °C, Humidity 91% , Mass 13.9 g

5.3	Observations 	: Limiting diameter  less than 1.0 mm

5.4	Result	: Low

5.5	Method 2	: Dutch pressure vessel test (test E.2)

5.6	Sample conditions 	: Temperature 18 °C, Humidity 89% , Mass 50 g

5.7	Observations	: Limiting diameter less than 1.0 mm

5.8	Result	: No

5.9	Final result 	: No

5.10	Exit	: 9.4

6.	Thermal stability (outside of the flow chart: test series H)

6.1	Method	: Heat accumulation storage test (test H.4)

6.2	Sample conditions	: Dewar vessel

(Diameter 60mm, Height  180mm , Mass 500 cc)

6.3	Observations	: at 60 °C no exothermal reaction

at 65°C self-promotion decomposition,

SADT 65 °C

6.4	Result	: Control temperature is not required

7. 	General remarks 	: The classification scheme is given in Fig.1

8.	Proposed assignment

8.1	Proper shipping name	: SELF-REACTIVE SOLID TYPE E

8.2	UN number	: 3228

8.3	Division 	: 4.1

8.4	Technical name	: ACETONE-PYROGALLOL COPOLYMER

1,2-NAPHTHOQUINONEDIAZIDO-5-SULPHONATE

8.5	Concentration	: 100%

8.6	Subsidiary risks	: None

8.7	Packing group 	: II

8.8	Packing Method	: OP8

8.9 	Control temperature 	: None

8.10	Emergency temperature	: None

* * * *

Figure 1: FLOW CHART SCHEME FOR SELF-REACTIVE SUBSTANCES

Figure1: FLOW CHART SCHEME FOR SELF-REACTIVE SUBSTANCES (cont'd)

# Footnotes

This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

# Text boxes

NATIONS UNIES

Secrétariat

ST

?

confinement

of heating it under defined

What is the effect

?

explosive power

What is its

IN IBCs OR TANKS

FOR TRANSPORT

MAY BE CONSIDERED

400 KG/450 LITRES

IN PACKAGES OF NOT MORE THAN

ACCEPTED FOR TRANSPORT

FOR EXEMPTION

SHALL BE CONSIDERED

Exit E

Box 12

Box 13

Box 11

13.2 None

13.1 Low

12.3 None

12.2 Low

12.1 Not low

11.2 No

11.1 Yes

?

for exemption

in IBCs or tanks, or

to be considered for transport

self-reactive substance

Is the

Exit G

Exit F

from box 9

?

confinement

of heating it under defined

What is the effect

?

confinement

of heating it under defined

What is the effect

SELF-REACTIVE SUBSTANCE

NET MASS

MORE THAN 50 KG

IN PACKAGES OF NOT

TRANSPORT

ACCEPTED FOR

NET MASS

MORE THAN 50 KG

IN PACKAGES OF NOT

TRANSPORT

ACCEPTED FOR

?

confinement

of heating it under defined

What is the effect

?

a deflagration

Can it propagate

?

a deflagration

Can it propagate

SUBSIDIARY RISK LABEL

WITH 'EXPLOSIVE '

NET MASS

NOT MORE THAN 25 KG

IN PACKAGES OF

TRANSPORT

ACCEPTED FOR

8.4 No

8.3 Low

8.2 Medium

?

in package

deflagrate rapidly

Does it

?

a deflagration

Can it propagate

?

for transport

detonate as packaged

Can it

2.2 No

Box 2

2.1 Yes

Violent

8.1

Box 8

Yes, rapidly

3.1

3.3 No

3.2 Yes, slowly

Box 3

4.3 No

4.2 Yes, slowly

Box 4

Yes, rapidly

4.1

?

for transport

explode as packaged

Can it

10.2 No

Box 10

10.1 Yes

9.4 No

9.3 Low

Violent

9.1

Box 9

Medium

9.2

Violent

7.1

Box 7

7.4 No

7.3 Low

7.2 Medium

6.2 No

Box 6

6.1 Yes

5.3 No

5.2 Yes, slowly

Box 5

Yes, rapidly

5.1

?

a detonation

Does it propagate

1.3 No

1.2 Partial

Box 1

1.1 Yes

PACKAGING

IN THAT

FOR TRANSPORT

NOT ACCEPTED

Exit D

Exit C

Exit B

Exit A

go to box 11