| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/2004/8 10 December 2003 ENGLISH Original: ENGLISH and FRENCH |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-thirty-second session, 9-12 March 2004,
 agenda item 4.2.15.)

DRAFT CORRIGENDUM 1 TO SUPPLEMENT 1 TO REGULATION No. 99

(Gas-discharge light sources)

Transmitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-first session, and is transmitted for consideration to WP.29 and to AC.1.  It is based on document TRANS/WP.29/GRE/2003/28, as amended TRANS/WP.29/GRE/51, paras. 25 and 26).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Text of the Regulation,

## Paragraph 2.4., sub-paragraph 2.3.4., correct the numbering to read "2.4.3.".

Paragraph 3.10., correct to read:

"3.10.	UV radiation

The UV radiation of the gas-discharge light source shall be such that:

400 nm

∫ Ee(()∙S(()∙d(

(=250 nm

kuv =    ____________________   ≤ 10-5  W/lm

780 nm

km ∙  ∫ Ee(()∙V(()∙d(

(=380 nm

where:

…."

_________