Informal Document No.  GRE-52-5

(52nd GRE, 30 March – 2 April 2004,

agenda item 2.2.)

Red light to the front from red rearmost side marker lamps

(transmitted by the expert from the United Kingdom)

Proposal

Amend Regulation 91:

7.1.2

Add to existing table:

| Side-marker lamp category | SM1 | SM2 |
| --- | --- | --- |
| … | … | … | … |
| Maximum Intensity | Within the specified angular field | 25,0 cd | 25,0 cd |
|  | Not within the specified angular field | 0,25 cd | 0,25 cd |

Justification

In GRE/2003/11 France proposes to improve the wording of Regulation 48 paragraph 5.10 concerning the visibility of red light to the rear.

The UK can agree that the use of "cause confusion" is ambiguous, open to interpretation and should be suppressed. This could be done by using the text from paragraph 4.10 of the draft GTR (informal document 12 to GRE 51). However there needs to be an objective limit on the red light which is allowed to be emitted forwards from rearmost side marker lamps. Therefore we propose this amendment to Regulation 91 to apply to all side marker lamps, for simplicity. The value of 0.25 cd can be discussed further but was suggested at a previous GRE meeting and would apply everywhere outside the specified angular field. (Which covers 10 degrees up and down and either 30 deg or 45 deg to the left and right, depending on the category of SML).

Vehicle Technology and Standards 6

1 March 2004