## Slide 1: 1st meeting EVSC electronic vehicle stability control
Ad hoc working group of GRRF
Technical University of Budapest
Hungary
26th and 27th Nov. 2004
Document No. EVSC04-04

## Slide 2: Philosophy of Stability Control Systems
Requirements for stability systems:
Driver’s intention must be followed in every situation, which means
  The system intervenes if the driver cannot control the situation
  The optimal vehicle behavior is calculated from a reference model based on the measured driver’s intention
  The intervention should minimize the error between the measured and the calculated (optimal) variables
Fail silent characteristics
min
Slide derived from lecture Prof. Palkovics at 56th GRRF

## Slide 3: 1st meeting EVSC electronic vehicle stability control
Technical State of art for existing systems:
Measurement of physical state variables of motor vehicle (and trailer):
- driver intention for direction (Steering wheel angle)
- driver intention longitudinal dynamics (speed, Braking)
- single wheel speeds via ABS-sensors (slip information)
- yaw-rate information
- lateral acceleration information

## Slide 4: 1st meeting EVSC electronic vehicle stability control
Technical State of Art for Existing Systems:
Control variables
- braking of single wheels (or axles)
- engine power control
- steering input
Motor vehicles
- directional and roll stability control
Trailers
- roll stability control

## Slide 5: 1st meeting EVSC electronic vehicle stability control
Equipment with EVSC:
Passenger- and Light Commercial Vehicles
- middle and high class passenger vehicles up to 100%
- Van-type vehicles commencing
Heavy Commercial Vehicles
- possibility for vehicles with electronicaly controlled pneumatic braking systems (EPB)
- Single Units (2- and 3 axle busses with EPB)
- Tractors for semitrailers (today 2 axle vehicles with EPB)
- Semitrailers (Roll-over stability control)

## Slide 6: 1st meeting EVSC electronic vehicle stability control
Open questions for a general equipment of CV‘s:
Vehicles with conventional braking systems
- EVSC as add -on device including ABS for medium and heavy vehicles not yet available (in development)
- EVSC for full-trailers not yet available (compatibility in combinations ?)
Possible Equipment of Commercial Vehicles Today
- For HCV restricted to vehicles with electronicaly controlled pneumatic braking systems (EPB)
- Single Units (2- and 3 axle busses with EPB)
- Tractors for semitrailers (today 2 axle vehicles with EPB)
- Semitrailers (Roll-over stability control)

## Slide 7: 1st meeting EVSC electronic vehicle stability control
Next steps for introduction of EVSC:
1. Question, if equipment should be
- on a voluntary basis (with incentive excemption from R.111) or
- as a mandatory requirement
Vehicles for the transport of dangerous goods (ADR)
- tractors for semitrailers for category FL and OX vehicles
- semitrailers with tanks for the transport of dangerous goods (FL and OX- vehicles)
- Single Unit tank vehicles ADR
Equipment of long distance Touring Busses and Coaches
- 2 and 3 axle Busses with electronicaly controlled braking systems (EBS)
Equipment of light commerial vehicles >3,5t to 5t (Category N2)
- Vehicles of Van-type