# Informal document No. 35-GRSP-7

# (35th GRSP, 3 - 7 May 2004,

# agenda item B.4.6.)

# ECONOMIC COMMISSION FOR EUROPE

## INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

# Working Party on Passive Safety (GRSP)

# REGULATION  NO. 22  INTERPRETATION  NEEDED

# Transmitted by the Expert from Poland

UN ECE Regulation No. 22, in paragraph 7.4.2.2.9, sets a verification requirement for the testing apparatus that is impossible to meet, just by a virtue of basic laws of physics:

"7.4.2.2.9.	With the unloaded carriage and a drop height of up to 450 mm, the velocity of the carriage after 250 mm of travel shall be 4.0 ± 0.1 m/sec..."

Comment:

There must be a mistake in the above sentence. Even in the case of neglecting the friction of the carriage, which implies a free drop in vacuum conditions, no object could possibly reach a velocity of 4.0 m/sec under the earth gravity of 9,81 m/sec2.

The above can be proved by a simple calculation:

(a) potential vs. kinetic energy balance:

(b) based on the above, the free drop velocity is:

(c) for the height of 0.25 m (250 mm), the free drop velocity is:  = 2.21 m/sec

The real value of velocity will always be smaller because of friction of the carriage bearings, so the verification requirement for the carriage velocity to reach 4.0 m/sec is impossible to meet.

To reach the required value of 4.0 m/sec,

(d) the drop height, resulting from eq. (a), would have to be at least: 0,815 m

We suspect a typing error, but since it is a test apparatus verification requirement, an official explanation, eg. a corrigendum, would be most appreciated, so the test results could be validated in accordance to the requirements of the Regulation No. 22.

_______________