# UN/SCETDG/27/INF.19

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

Item 3(b) of the provisional agenda

# EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

Default classification of fireworks

Information on test results for a rocket

##### Transmitted by the expert from Denmark

# Introduction

A UN Test Series 6 has been carried out on a rocket which was according to the UN default classification list to be classified as UN 0335 (1.3G). The test results clearly show that the proper classification is UN 0333 (1.1G). The rocket contains 11% flash composition (16% if the rocket motor is not taken into account).

These tests took place in Germany on 18 – 19 April, 2005, in co-operation with Bundesanstalt für Materialforschung und -prüfung (BAM).

Later, a UN 4(b) test was also performed, and no fire or explosion was observed.

# Test results

UN Test Series 6:

6 (a) test:	1.1G

6(b) test:	Not performed

6(c) test:	1.1G

UN Test Series 4(b):

No fire or explosion observed.

Result of the chemical analysis (approx.):

Bursting charge:	25 g (51% KClO4, 9% S, presence of Mg/Al)

Effect charge:	120 g (12% KClO4, 18% KNO3, 18% BaNO3, 10% S, 37% insoluble material, presence of Mg/Al/Ca).

Ignition charges:	5 g (51% KClO4, 12% S).

Composition according to the manufacturer:

Conclusion

The expert from Denmark would like to ask the Sub-Committee to reconsider the default classification criteria for rockets, at least as regards the border line between 1.3G and 1.1G (i.e. 25% flash composition).

________________