# UN/SCETDG/27/INF.24

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Provisions for the transport of solid substances in bulk containers
- Revised rationalised approach -

Transmitted by the International Council of Chemical Associations (ICCA)

1.	BACKGROUND

Provisions for the use of bulk containers for the transport of solid substances in bulk were included in a new chapter 4.3 of the thirteenth revised edition of the UN Model Regulations.

At the same time two new bulk container codes (BK1 for transport in sheeted bulk containers and BK2 for transport in closed bulk containers) were added in column 6 of the Dangerous Goods List for some 25 UN entries.

These provisions were the result of a series of discussions, which started with document ST/SG/AC.10/C.3/1999/92 (Germany), followed by documents ST/SG/AC.10/C.3/2001/37 (UK and Germany) and ST/SG/AC.10/C.3/2002/29 (United Kingdom and Germany) (and UN/SCETDG/21/INF.66) before they were finally adopted in the 21st session in July 2002.

During these discussions, ICCA promised to present in the biennium (2003-2004) a proposal for a rationalised approach for the assignment of bulk container codes to extend the number of substances involved (ST/SG/AC.10/C.3/40 para 37).

The proposed approach (ST/SG/AC.10/C.3/2004/42) which primary based on the previous documents on this issue, as well as on the rationalised approach for assignment of tank instructions for solids was discussed in the Sub-Committee Meeting, 25th session, July 2004. Several experts considered that the fact that substances are allowed for carriage in bulk in tanks is not a sufficient justification for allowing their carriage in bulk containers, which do not present the same safety guarantees as portable tanks and packagings. Some experts could agree that a less restrictive approach could be envisaged and made reference to the criteria for the use of flexible IBCs.

ICCA withdrew its proposal and would introduce a revised proposal, taking into account the comments and suggestions made.

2.	INTRODUCTION

As a result of the discussion ICCA took into consideration the solid substances that are currently being allowed to be transported in flexible IBCs i.e. substances with Packing Instruction IBC08 in column 8 of the Dangerous Goods List:

However, in case of an accidental spillage, the potential quantity released from a Bulk Container is much bigger than with FIBCs. Therefore, a number of additional restrictions should apply for the assignment of bulk container codes in column 10 of the Dangerous Goods List:

- Only solid substances of PG III

- No solids of classes 1, 5.2, 6.2, and 7

- No solids which are not allowed to be transported in portable tanks i.e. without a Portable Tank Instruction in column 10 of the Dangerous Goods List

The following allocation of the two bulk container codes BK1 (sheeted bulk container) or BK2 (closed bulk container) is proposed:

  - Class 4.1:	BK1, BK2	with subsidiary risk:	BK2 only

  - Class 4.2:	BK2

  - Class 4.3:	BK2

  - Class 5.1:	BK1, BK2	with subsidiary risk:	BK2 only

  - Class 6.1:	BK2

  - Class 8:		BK2

  - Class 9:		BK1, BK2

Annex 1 provides an overview of the UN numbers, which meet the criteria, and shows the proposed allocation of BK codes. The UN numbers, to which BK codes have already been allocated in the UN Model Regulations, have been highlighted (these allocations would of course remain unchanged).

Annex 2 provides the same information but in more details

3.	PROPOSAL

The following changes in Column 10 of the Dangerous Goods List in Chapter 3.2 are proposed:

- Solids with UN numbers as listed in the Annex 1 should be permitted to be transported in bulk container by adding BK2 or BK1 & BK2 in column 10, as listed in Annex 2.

- The allocation of bulk container codes to UN number 3170 should remain unchanged (class 4.3, PG. III: although this rationalised approach would allocate code BK 2 only, the current allocation of BK1 & BK2 should remain unchanged).

ICCA is not requesting the UNSCETDG meeting to make a decision on this proposal but invites the comments from delegates, in order to allow ICCA to make a revised proposal at the December meeting, taking into account the comments made.

- JUSTIFICATION

The solids proposed for transport in bulk containers are already permitted for the transport in flexible IBC.

Taking into account that the provisions of the chapters 4.3 and 6.8 have to be complied with, and taking into account the proposed additional restrictions, ICCA is of the opinion that the transport of these substances in bulk can be carried safely.

Annex 1

List of UN numbers concerned

Class 	Sub.	PG	Proposed		Apply to UN numbers

risk	BK code(s)		(xxxx: already permitted in BK1 and /or BK2

4.1		III	BK1, BK2	1309, 1312, 1325, 1328, 1332, 1334, 1338, 1346,

1350, 1869, 2001, 2213, 2538, 2687, 2717, 2878,

2989, 3178, 3181

4.2		III	BK2	1361, 1362, 1363, 1364, 1365, 1373, 1376, 1932,

2008, 2545, 2546, 2881, 3088, 3174, 3189, 3190,

3205, 3313, 3341, 3342, 3400

4.2	6.1	III	BK2	3128, 3191

4.2	8	III	BK2	3126, 3192, 3206

4.3		III	BK2	1396, 1398, 1403, 1405, 1435, 2813, 2844,

2950, 2968, 3170*, 3208

* UN 3170 has currently BK1, BK2 (to remain)

4.3	4.2	III	BK2	1418, 1436, 3135, 3209

4.3	6.1	III	BK2	1408, 3134

4.3	8	III	BK2	3131

5.1		III	BK1, BK2	1438, 1444, 1451, 1454, 1458, 1459, 1465, 1466,

1467, 1474, 1477, 1479, 1481, 1482, 1483, 1486,
 				1492, 1498, 1499, 1505, 1507, 1872, 1942, 2067,
				 2469, 2720, 2722, 2724, 2725, 2726, 2728, 2880
				 3215, 3377, 3378

5.1	6.1	III	BK2	1500, 3087

5.1	8	III	BK2	1511, 3085

6.1 		III	BK2	1544, 1548, 1549, 1550, 1551, 1557, 1564, 1566,

1579, 1588, 1601, 1616, 1655, 1663, 1673, 1690,

1709, 1812, 1884, 2020, 2025, 2026, 2074, 2077,

2233, 2237, 2239, 2291, 2446, 2473, 2505, 2512,

2516, 2570, 2588, 2651, 2655, 2659, 2660, 2674,

2713, 2716, 2729, 2757, 2759, 2761, 2763, 2771,

2775, 2777, 2779, 2781, 2783, 2786, 2811, 2853,

2854, 2855, 2856, 2862, 2871, 2875, 2876, 3027,

3143, 3146, 3283, 3284, 3285, 3288, 3345, 3349,

3427, 3438, 3439, 3457, 3458, 3459, 3460, 3462,

3464, 3465, 3466, 3467

8		III	BK2	1740, 1759, 1773, 1907, 1910, 2214, 2215, 2280,

2331, 2430, 2440, 2475, 2503, 2507, 2508, 2578,

2579, 2585, 2698, 2802, 2812, 2823, 2834, 2865,

2869, 2905, 2967, 3147, 3253, 3259, 3260, 3261,

3262, 3263, 3453

8	6.1	III	BK2	2923

9		III	BK1, BK2	1841, 1931, 2071, 2211, 2216, 2590, 3077, 3314

Annex 2

| UN No. | Name and descripton | Class or division | Subsi-diary risk | UN packing group | Special provisions | Limited quantities | Packagings and IBCs |  | Portable tanks and bulk containers |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc-tions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | PP11 B3 | T1 BK1 BK2 | TP33 |
| 1312 | BORNEOL | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1328 | HEXAMETHYLENETETRAMINE | 4.1 |  | III |  | 5 kg | P002 IBC08 | B3 | T1 BK1 BK2 | TP33 |
| 1332 | METALDEHYDE | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1334 | NAPHTHALENE, CRUDE or NAPHTHALENE, REFINED | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1338 | PHOSPHORUS, AMORPHOUS | 4.1 |  | III |  | 5 kg | P410 IBC08 | B3 | T1 BK1 BK2 | TP33 |
| 1346 | SILICON POWDER, AMORPHOUS | 4.1 |  | III | 32 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1350 | SULPHUR | 4.1 |  | III | 242 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1869 | MAGNESIUM or MAGNESIUM ALLOYS with more than 50% magnesium in pellets, turnings or ribbons | 4.1 |  | III | 59 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2001 | COBALT NAPHTHENATES, POWDER | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2213 | PARAFORMALDEHYDE | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | PP12 B3 | T1 BK1 BK2 | TP33 |
| 2538 | NITRONAPHTHALENE | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2687 | DICYCLOHEXYLAMMONIUM NITRITE | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2717 | CAMPHOR, synthetic | 4.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2878 | TITANIUM SPONGE GRANULES or TITANIUM SPONGE POWDERS | 4.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1361 | CARBON, animal or vegetable origin | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | PP12 B3 | T1 BK2 | TP33 |
| 1362 | CARBON, ACTIVATED | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | PP11 B3 | T1 BK2 | TP33 |
| 1363 | COPRA | 4.2 |  | III | 29 | NONE | P003 IBC08 LP02 | PP20 B3, B6 | T1 BK2 |  |
| 1364 | COTTON WASTE, OILY | 4.2 |  | III |  | NONE | P003 IBC08 LP02 | PP19 B3, B6 | T1 BK2 |  |
| 1365 | COTTON, WET | 4.2 |  | III | 29 | NONE | P003 IBC08 LP02 | PP19 B3, B6 | T1 BK2 |  |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGETABLE or SYNTHETIC, N.O.S. with oil | 4.2 |  | III |  | NONE | P410 IBC08 | B3 | T1 BK2 | TP33 |
| 1376 | IRON OXIDE, SPENT or IRON SPONGE, SPENT obtained from coal gas purification | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1932 | ZIRCONIUM SCRAP | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2545 | HAFNIUM POWDER, DRY | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2546 | TITANIUM POWDER, DRY | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2881 | METAL CATALYST, DRY | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 |  | III | 223 274 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3174 | TITANIUM DISULPHIDE | 4.2 |  | III |  | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 |  | III | 223 274 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 |  | III | 223 274 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 |  | III | 183 223 274 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3341 | THIOUREA DIOXIDE | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3342 | XANTHATES | 4.2 |  | III | 223 | NONE | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 |  | III | 223 274 | 1 kg | P002 IBC08 |  | T1 BK2 | TP33 |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | 6.1 | III | 223 274 | NONE | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | 6.1 | III | 223 274 | NONE | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | 8 | III | 223 274 | NONE | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | 8 | III | 223 274 | NONE | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | 8 | III | 182 223 274 | NONE | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 |  | III | 223 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 |  | III | 37 223 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 |  | III | 38 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1405 | CALCIUM SILICIDE | 4.3 |  | III | 223 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1435 | ZINC ASHES | 4.3 |  | III | 223 | 1 kg | P002 IBC08 | B4 | T1 BK2 | TP33 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 |  | III | 223 274 | 1 kg | P410 IBC08 | PP83 B4 | T1 BK2 | TP33 |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 |  | III |  | 1 kg | P410 IBC08 | B2, B4 | T1 BK2 | TP33 |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 |  | III |  | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 |  | III | 223 | 1 kg | P002 IBC08 | B4 | T1 BK2 | TP33 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 |  | III | 223 244 | 1 kg | P002 IBC08 | B4 | T1 BK1 BK2 | TP33 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 |  | III | 223 274 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | 4.2 | III | 223 | NONE | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | 4.2 | III | 223 | NONE | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | 4.2 | III | 223 274 | NONE | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | 4.2 | III | 223 274 | NONE | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | 6.1 | III | 39 223 | 1 kg | P003 IBC08 | PP20 B4, B6 | T1 BK2 | TP33 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | 6.1 | III | 223 274 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | 8 | III | 223 274 | 1 kg | P410 IBC08 | B4 | T1 BK2 | TP33 |
| 1438 | ALUMINIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1444 | AMMONIUM PERSULPHATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1451 | CAESIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1454 | CALCIUM NITRATE | 5.1 |  | III | 208 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLID | 5.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1465 | DIDYMIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1466 | FERRIC NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1467 | GUANIDINE NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1474 | MAGNESIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 |  | III | 206 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1486 | POTASSIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1492 | POTASSIUM PERSULPHATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1498 | SODIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1499 | SODIUM NITRATE AND POTASSIUM NITRATE MIXTURE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1505 | SODIUM PERSULPHATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1507 | STRONTIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1872 | LEAD DIOXIDE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1942 | AMMONIUM NITRATE, with not more than 0.2% total combustible material, including any organic substance, calculated as carbon to the exclusion of any other added substance. | 5.1 |  | III | 306 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2067 | AMMONIUM NITRATE BASED FERTILIZER | 5.1 |  | III | 186 306 307 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2469 | ZINC BROMATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2720 | CHROMIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2722 | LITHIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2724 | MANGANESE NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2725 | NICKEL NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2726 | NICKEL NITRITE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2728 | ZIRCONIUM NITRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water | 5.1 |  | III | 223 313 314 | 5 kg | P002 IBC08 | PP85 B4 | T1 BK1 BK2 |  |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 3377 | SODIUM PERBORATE MONOHYDRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 1500 | SODIUM NITRITE | 5.1 | 6.1 | III |  | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | 6.1 | III | 223 274 | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 1511 | UREA HYDROGEN PEROXIDE | 5.1 | 8 | III |  | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | 8 | III | 223 274 | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 |  | III | 43 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1548 | ANILINE HYDROCHLORIDE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 |  | III | 45 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1550 | ANTIMONY LACTATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1551 | ANTIMONY POTASSIUM TARTRATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 |  | III | 43 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 |  | III | 177 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 |  | III | 47 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 |  | III | 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1616 | LEAD ACETATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 |  | III | 43 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1663 | NITROPHENOLS (o-, m-, p-) | 6.1 |  | III | 279 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1673 | PHENYLENEDIAMINES (o-, m-, p-) | 6.1 |  | III | 279 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1690 | SODIUM FLUORIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1709 | 2,4-TOLUYLENEDIAMINE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1812 | POTASSIUM FLUORIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1884 | BARIUM OXIDE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2020 | CHLOROPHENOLS, SOLID | 6.1 |  | III | 205 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 |  | III | 43 66 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 |  | III | 43 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2074 | ACRYLAMIDE, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2077 | alpha-NAPHTHYLAMINE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2233 | CHLOROANISIDINES | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2237 | CHLORONITROANILINES | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2239 | CHLOROTOLUIDINES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 |  | III | 199 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2446 | NITROCRESOLS, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2473 | SODIUM ARSANILATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2505 | AMMONIUM FLUORIDE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2512 | AMINOPHENOLS (o-, m-, p-) | 6.1 |  | III | 279 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2516 | CARBON TETRABROMIDE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2570 | CADMIUM COMPOUND | 6.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2651 | 4,4'-DIAMINODIPHENYL-METHANE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2655 | POTASSIUM FLUOROSILICATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2659 | SODIUM CHLOROACETATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2660 | NITROTOLUIDINES (MONO) | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2674 | SODIUM FLUOROSILICATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2713 | ACRIDINE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2716 | 1,4-BUTYNEDIOL | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2729 | HEXACHLOROBENZENE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2853 | MAGNESIUM FLUOROSILICATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2854 | AMMONIUM FLUOROSILICATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2855 | ZINC FLUOROSILICATE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2862 | VANADIUM PENTOXIDE, non-fused form | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2871 | ANTIMONY POWDER | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2875 | HEXACHLOROPHENE | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2876 | RESORCINOL | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 |  | III | 43 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | 6.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 |  | III | 61 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3427 | CHLOROBENZYL CHLORIDES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3438 | alpha-METHYLBENZYL ALCOHOL, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3439 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3457 | CHLORONITROTOLUENES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3458 | NITROANISOLES, SOLID | 6.1 |  | III | 279 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3459 | NITROBROMOBENZENES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3460 | N-ETHYLBENZYLTOLUIDINES, SOLID | 6.1 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3462 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 |  | III | 210 223 274 | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 3464 | ORGANOPHOSPHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | III | 43 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3465 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3466 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3467 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1740 | HYDROGENDIFLUORIDES, SOLID, N.O.S. | 8 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1773 | FERRIC CHLORIDE, ANHYDROUS | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1907 | SODA LIME with more than 4% sodium hydroxide | 8 |  | III | 62 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 1910 | CALCIUM OXIDE | 8 |  | III | 106 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2214 | PHTHALIC ANHYDRIDE with more than 0.05% of maleic anhydride | 8 |  | III | 169 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2215 | MALEIC ANHYDRIDE | 8 |  | III |  | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 2280 | HEXAMETHYLENEDIAMINE, SOLID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2331 | ZINC CHLORIDE, ANHYDROUS | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2440 | STANNIC CHLORIDE PENTAHYDRATE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2475 | VANADIUM TRICHLORIDE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2503 | ZIRCONIUM TETRACHLORIDE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2507 | CHLOROPLATINIC ACID, SOLID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2508 | MOLYBDENUM PENTACHLORIDE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2578 | PHOSPHORUS TRIOXIDE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2579 | PIPERAZINE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2698 | TETRAHYDROPHTHALIC ANHYDRIDES with more than 0.05% of maleic anhydride | 8 |  | III | 29 169 | 5 kg | P002 IBC08 LP02 | PP14 B3 | T1 BK2 | TP33 |
| 2802 | COPPER CHLORIDE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2812 | SODIUM ALUMINATE, SOLID | 8 |  | III | 106 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2823 | CROTONIC ACID, SOLID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 |  | T1 BK2 | TP33 |
| 2834 | PHOSPHOROUS ACID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2865 | HYDROXYLAMINE SULPHATE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 |  | III | 223 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2905 | CHLOROPHENOLATES, SOLID or PHENOLATES, SOLID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 2967 | SULPHAMIC ACID | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3253 | DISODIUM TRIOXOSILICATE | 8 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 |  | III | 223 274 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK2 | TP33 |
| 3453 | PHOSPHORIC ACID, SOLID | 8 |  | III |  | 5 kg | P002 IBC08 LP01 | B3 | T1 BK2 | TP33 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | 6.1 | III | 223 274 | 5 kg | P002 IBC08 | B3 | T1 BK2 | TP33 |
| 1841 | ACETALDEHYDE AMMONIA | 9 |  | III |  | 5 kg | P002 IBC08 LP01 | B3, B6 | T1 BK1 BK2 | TP33 |
| 1931 | ZINC DITHIONITE (ZINC HYDROSULPHITE) | 9 |  | III |  | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 | TP33 |
| 2071 | AMMONIUM NITRATE BASED FERTILIZER | 9 |  | III | 186 193 | 5 kg | P002 IBC08 LP02 | B3 | T1 BK1 BK2 |  |
| 2211 | POLYMERIC BEADS, EXPANDABLE, evolving flammable vapour | 9 |  | III | 207 | 5 kg | P002 IBC08 | PP14 B3, B6 | T1 BK1 BK2 | TP33 |
| 2216 | FISH MEAL (FISH SCRAP), STABILIZED | 9 |  | III | 29 117 300 308 | NONE | P900 IBC08 | B3 | T1 BK1 BK2 | TP33 |
| 2590 | WHITE ASBESTOS (chrysotile, actinolite, anthophyllite, tremolite) | 9 |  | III | 168 | NONE | P002 IBC08 | PP37 B2, B3 | T1 BK1 BK2 | TP33 |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S. | 9 |  | III | 179 274 | 5 kg | P002 IBC08 LP02 | PP12 B3 | T1 BK1 BK2 | TP33 |
| 3314 | PLASTICS MOULDING COMPOUND in dough, sheet or extruded rope form evolving flammable vapour | 9 |  | III | 207 | 5 kg | P002 IBC08 | PP14 B3, B6 | T1 BK1 BK2 |  |

_______________