# UN/SCETDG/28/INF.11

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-eighth session

Geneva, 28 November – 7 December 2005

Item 6 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL REGULATIONS
ON THE TRANSPORT OF DANGEROUS GOODS

## Substances whose transport is prohibited

### Transmitted by the expert from Italy

For some UN entries, modal regulations contain specific provisions, prohibiting the transport of specific compounds and mixtures.

As far as IMDG Code is concerned, such a prohibition is established by assigning to the relevant entries Special Provision 900: in SP 900 a list of substances whose transport is prohibited is given.

With regard to ICAO T.I., specific compounds whose transport is prohibited are mentioned as “FORBIDDEN” in the Dangerous Good List.

In ADR/RID/ADN a specific Special Provision is assigned to the relevant entries, when specific compounds and mixtures are not accepted for carriage.

This situation is particularly relevant for Ammonium salts: the approaches used in the modal regulations are illustrated in the following table:

| UN number | Proper Shipping Name | ADR/RID/ADN Special Provision | IMDG Code Special Provision | ICAO T.I. |
| --- | --- | --- | --- | --- |
| 1450 | BROMATES, INORGANIC, N.O.S. | 604 | 900 | * |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 605 | 900 | * |
| 1462 | CHLORITES, INORGANIC, N.O.S. | 606 | 900 |  |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 608 | 900 | * and A37 |
| 1791 | HYPOCHLORITE SOLUTION | 559 | 900 |  |
| 1908 | CHLORITE SOLUTION | 606 | 900 |  |
| 3210 | CHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 605 | 900 | * |
| 3212 | HYPOCHLORITES, INORGANIC, N.O.S. | 559 | 900 |  |
| 3213 | BROMATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 604 | 900 | * |
| 3214 | PERMANGANATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 608 | 900 | * and A37 |

NOTE TO THE TABLE:

for ADR/RID/ADN

559	Mixtures of a hypochlorite with an ammonium salt are not to be accepted for carriage.

UN No. 1791 hypochlorite solution is a substance of Class 8.

604	Ammonium bromate and its aqueous solutions and mixtures of a bromate with an ammonium salt are not to be accepted for carriage.

605	Ammonium chlorate and its aqueous solutions and mixtures of a chlorate with an ammonium salt are not to be accepted for carriage.

606	Ammonium chlorite and its aqueous solutions and mixtures of a chlorite with an ammonium salt are not to be accepted for carriage.

608	Ammonium permanganate and its aqueous solutions and mixtures of a permanganate with an ammonium salt are not to be accepted for carriage.

for IMDG Code

900	The transport  of the following substances is prohibited:

Ammonium bromate

Ammonium bromate,  solution

Ammonium chlorate

Ammonium chlorate, solution

Ammonium chlorite

Ammonium hypochlorite

.....

......

for ICAO T.I.

*	means that Ammonium salts are prohibited in the Dangerous Goods List

A37	This entry is not intended to include Ammonium permanganate, the transport of which is prohibited under any circumstances

Taking care that, in many cases, the prohibition is applicable to all modes of transport, it would be appropriate to reflect such prohibitions also in the UN Recommendations - Model Regulations.

If that is accepted, the way of coping with that (with one Special Provision, with several Special Provisions, other way) need to be defined and applied.

____________