## Slide 1
ITS Warnings: Design and Performance Considerations
Peter C. Burns
IHRA - ITS Working Group
Informal Document No. ITS-11-4

## Slide 2: Outline
IHRA-ITS
Definition of warning and examples
Importance of the warning HMI
Warning design considerations
Factors affecting warning effectiveness
Assessing warnings
Research needs
Next steps
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: IHRA-ITS WG
Mandate: exchange information on ITS safety research, present national safety-related interests in ITS, coordinate research and encourage collaborations.
Research Goals:
Improve our understanding of the safety benefits and risks associated with ITS systems,
Develop procedures and criteria for the evaluation of the safety of in-vehicle information, control and communication systems
Coordinate international policy-oriented research to optimize the safety performance of on-board ITS technologies.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Safety critical warning
Definition:
A signal informing the driver of a hazardous situation, which if not corrected by an immediate action, will result in equipment damage and/or personal injury.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
Examples
Forward collision warning system threat level icons
Automotive Collision Avoidance System Field Operational Test (NHTSA, 2005)
Heads-up Display (HUD)

## Slide 6
Forward collision warnings (FCW)
CAMP (2005)
High Head Down Display
Heads-up Display (HUD)

## Slide 7
Forward collision warning system threat level icons
SAVE-IT (2004)
Heads-up Display (HUD)
Warning comes with auditory crash alarm

## Slide 8
Lane Departure Warning Display
SAVE-IT (2004)
Heads-up Display (HUD)
Warning comes with rumble strip sound

## Slide 9: Importance of the Human-Machine Interface
Warning systems sense the road traffic environment, filter this information for hazards, calculate their severity and then warn the driver.
System performance depends on sensor coverage, sensor reliability and accuracy, warning decision logic, the warning itself and the resulting human performance.
Ultimately, system performance depends on a timely and appropriate response from the driver.
Given this, a warning system can be no better than its interface.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Stages of perception-response time
Warning and/ or event stimulus
Detection
Identification
Decision
Response
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Total Brake Response Time
Warning
Winters (1998)
Notes: <number>
<footer>
<header>
<date/time>
Components of Total Brake Response Time (TBRT). Taken from Winters, J.J. (1998) AN INVESTIGATION OF AUDITORY ICONS AND BRAKE
RESPONSE TIMES IN A COMMERCIAL TRUCK-CAB ENVIRONMENT, Viginia Tech, MSc Thesis.

## Slide 12
Frequency of Warnings
(Martin & Burgett, 2001)
Safety critical forward collision situations are relatively uncommon events.

## Slide 13: Perception-response times
(Olson et al. 1984)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Warning design considerations
Activation criteria – When?
Levels and priorities of warnings
Presentation modality, information and location
Response options
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Modeling System Performance: Signal Detection Theory
 | Warning | No Warning
Hazard | Hit | Miss
No Hazard | False Alarm | Correct rejection
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Warning Levels
Information - such as indicators, tell the driver if they are on or off
Advisory - such as fuel low that tell the driver the state of the vehicle
Warning - response is required
  Cautionary
  Imminent
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: ISO Prioritization Procedure
Priority helps to determine when, where and how system messages are to be.
Priority sets the relative importance of two or more messages, which determines their ranking in a time sequence or emphasis of presentation.
If messages are not managed properly, drivers may fail to obtain critical safety information.
This procedure provides a basis for the management of messages competing for the driver’s limited attention.
A priority index is calculated according to message criticality and urgency ratings.
ISO TS 16951: 2003
Notes: <number>
<footer>
<header>
<date/time>
ISO/TS 16951:2003(E) ISO TC 22/ SC13/ WG8: Road Vehicles - Ergonomic aspects of transport information and control systems — Procedures for determining priority of on-board messages presented to drivers.

## Slide 18
ISO Criticality ratings

## Slide 19
ISO Urgency ratings

## Slide 20: Warning Modality and Characteristics
Auditory – speech, tone, loudness, musicality, duration, direction…
Visual – symbols, text, light, brightness, location, colour, flashing…
Haptic (touch) – vibration, location, intensity, direction.
Kinaesthetic (body motion) – vehicle slowing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Visual Displays
Visual displays can be used to convey higher criticality and urgency by:
Colour – red
Luminance – greater luminance and contrast
Blinking – shorter blinking cycle, smaller duty rate, (rather than continuous display)
Size – larger
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Auditory Tones
Higher criticality and urgency can be indicated by:
Intensity – higher sound pressure level (dB(A))
Tone frequency – higher frequencies
Periodicity - shorter intermittent cycle, larger duty rate (rather than continuous tone display)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Crash avoidance response options
Immediate hard braking for evasion of crash.
Immediate steering manoeuvre for evasion of crash.
Immediate termination of initiated or initiating action.
Seek awareness of situation and perform one of the above responses.
Immediate decision to retake control by the driver.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Some factors mediating warning effectiveness
Conspicuity
Comprehension
Driver frustration and annoyance
Expectancy
Frequency of warnings
Individual differences and condition
Response options/ uncertainty
Trust
Willingness and/or ability to comply
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Warnings Assessment
Standard performance tests that are practical, meaningful, reliable, and objective do not exist.
Equipment performance (sensor coverage, accuracy and reliability, detection performance)
Driver-system performance (fast or timely, appropriate and successful response).
Range of scenarios (context, integration, prioritization)
Range of potential users (typical, least informed most endangered)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Warnings Research Needs
Need for comprehensive science-based model of driver responses to warnings
Warning design guide
Assessment methods
New warning concepts (e.g., adaptive intelligent warnings)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27
Warnings interface design guide - 2007
Assessment procedures and performance criteria - 2010
Possible IHRA contributions with respect to warnings

## Slide 28: Summary and Conclusions
Interface design is crucial for ITS warning system effectiveness
Theory and models are needed to support the development of effective warning systems
Research is needed to gain a better understanding of warning parameters, particularly for a
  Warning design guide
  Assessment procedures
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29
Thank you