## Slide 1: Integrated Safety by Pre-Crash Triggering
Dr. Yngve Haland
Senior Adviser
Autoliv Inc.
ECE / WP 29 / ITS Informal Group
November 18, 2005 Geneva
Informal Document No. ITS-11-5

## Slide 2: Integrated Safety Chart
Crash
Crash non avoidable
Mayday
Telematics
Response
Rescue, care
Post Crash
Studies
Threatening situation
Golden
Hour
Long Term
Driver’s Awareness
Night Vision, Blind Spot, Parking Aid
Relieving Some Driver Control
ACC +, Queue Assist, Parking Assistance
Alerting The Driver
Lane Departure Warning, Lane Change Assist
Taking Control
ESC, Pre Crash Braking
Pretriggering of Restraints
Pre Safe, PRINTS
Keeping the car Fit
Steering, Brakes, Tires, TPI
Driver’s Condition
Alcohol, Drowsiness
Active
Safety
Passive
Safety
Rescue & Heal
Conventional
Restraints
ALR/YH 051118

## Slide 3: Pre-Crash Triggering Scope
Triggering Systems prior to the crash allow
  Collision Avoidance
  Collision Severity Mitigation
  Occupant and Pedestrian Protection Enhancement
Not only Reversible Systems like
  moderate Automatic Braking (~0.4 g)
  Motorized Pretensioners, Sunroofs, Seat etc
But also Non Reversible Systems like
  hard Automatic Braking (>0.5 g)
  Front & Side Airbags, Hood Lifters etc
ALR/YH 051118

## Slide 4: Pre-Crash Triggering example: Active Bumper
ALR/YH 051118

## Slide 5: Pre-Crash Triggering example: Collision Mitigation by Braking
ALR/YH 051118

## Slide 6: Pre-Crash Triggering of Restraints Benefits in Side Impacts
SOURCE : Real-world Crash Performance of Recent Model Cars – Next Steps in Injury Prevention
Pete Thomas, Richard Frampton – Vehicle Safety Research Centre, Loughborough University, UK
IRCOBI Conference – Lisbon (Portugal), September 2003
ALR/YH 051118

## Slide 7: Pre-Crash Triggering of Restraints Benefits in Side Impacts
Impact speeds in regulatory or rating tests are lower than in real life:
90% of fatalities in tree or pole impacts are with impact speeds above 30 Km/h
70% of fatalities in car-to-car impacts are with impact speed above 65 Km/h
Protecting occupants at higher impact speeds requires new protection
systems that need to be deployed earlier and even prior to the impact
ALR/YH 051118

## Slide 8: Pre-Crash Triggering of Restraints Benefits in Frontal Impacts
V=48 km/h
Available Ride-down Space
Typical F-D
(Occupant)
PBP
KAB
Severity
reduction
Reversible Actuators
Pre-impact
Braking
Active
Bumper
Non-reversible Actuators
Occupant Pre-load
Pre2
Ideal F-D
(Occupant)
LLC
Active vents
Adaptive & Optimized
Energy Mgmt
Airbags
OOP-friendly
Inflation rate
ALR/YH 051118

## Slide 9: Pre-Crash Triggering of Restraints Benefits in Frontal Impacts
Pre-Crash Triggering Restraint Systems allow:
slower deployment
improved balance between non-aggressiveness and occupant coupling
Leading to
no deployment-related injuries
enhanced occupant protection
ALR/YH 051118

## Slide 10: Frontal Pre-Crash Triggering proposed System Objectives (1)
  Pre-Crash activation of
    non reversible systems (e.g. airbags)
    and/or
    reversible systems with potentially severe impacts on traffic (e.g. > 0.5 g braking)
  is evidently dictating the most challenging
  specifications for the complete systems and for
  the sensors.
ALR/YH 051118

## Slide 11: Frontal Pre-Crash Triggering proposed System Objectives (2)
  Sensing System
    Airbag activation decision 80 ms prior to impact for severe frontal impacts ( = 2,65 m at 120 km/h)
    Overall reliability as with current sensing systems
  Protection System
    Airbags and inflators designed for ~120 ms deployment time
    Optimization for Very Low Risk deployment and...
    …maximum possible Occupant-Car coupling
ALR/YH 051118

## Slide 12: Frontal Pre-Crash Triggering Sensing System Reliability vs. Performances (1)
  Sensing Reliability is measured by
    occurrence of “False Positive” decisions (undesired firing decisions)
    occurrence of “False Negative” decisions (no firing in severe crashes)
  Both criteria depend on
    accuracy of impact point prediction
    correct identification of “target” (number of objects, type, size, mass, stiffness)
    processing time
ALR/YH 051118

## Slide 13: Frontal Pre-Crash Triggering Sensing System Reliability vs. Performances (2)
Sensing System Comparison - Short Range - Assuming adequate FoV
Sensing Resolution and Accuracy Separation Classification
Technologies Distance Angle potential potential
Required for 20 cm 1°
Pre-Crash
Radar OK fair (3°) fair (Range) poor
Single camera poor fair fair good
Stereo Vision fair OK fair (Azimuth) OK
Scanning Lidar OK fair fair poor
3D Camera (1) fair OK OK (Range?) OK
(1) High number of pixel required
Conclusion: At least two Sensing Technologies must be associated to provide desired performances and thus decision reliability
ALR/YH 051118

## Slide 14: Frontal Pre-Crash Triggering Example of Sensing Technologies
Stereo Vision for Pedestrian Sensing
Distance
Separation
Classification
ALR/YH 051118

## Slide 15: Frontal Pre-Crash Triggering Example of Sensing Technologies
Radar + Stereo Vision for Pre-Crash
“ Hit ”
“ Near Miss ”
ALR/YH 051118

## Slide 16: Frontal Pre-Crash Triggering Sensor Reliability - General
  In general terms:
    the slower the actuators, the earlier the activation decision
    the earlier the decision, the lower its reliability (False Positive)
    need for reliability depends on annoyance and consequences of False Positive decisions
    consequences are linked to potential safety impacts of a False Negative decision
ALR/YH 051118

## Slide 17: Frontal Pre-Crash Triggering Sensor Reliability - Non Reversible Systems (1)
  Current development work
    show that sensor combinations (fusion) can provide good accuracy in predicting the impact position and time (e.g. 20 cm @ -80 ms)
  Inherent weaknesses will be
    inability to evaluate mass/stiffness prior to contact
    gray zone (e.g. 20 cm)
  Consequences will be
    non desirable activation for impacts against objects with “big” signature but low mass (e.g. bushes)
    “late” firing in crashes with small overlaps
ALR/YH 051118

## Slide 18: Frontal Pre-Crash Triggering Sensor Reliability - Non Reversible Systems (2)
  Acceptance of weaknesses
    depends on statistical probability and physical consequences
    must make reference to State-of-the-Art systems of which weaknesses are known and accepted
  Examples of action
    statistical study about likelihood of impact against “zero mass” objects
    development of backup (alternative) solutions in case of late activation
ALR/YH 051118

## Slide 19: Frontal Pre-Crash Triggering Regulatory Considerations
  Pre-Crash activation of Restraint Systems
    possible in current regulatory and rating tests; no change needed
  Pre-Crash braking
    all current test procedures specify impact speeds and obstacle types
    issue # 1: change “impact speed” into “initial speed” and permit automatic intervention resulting in lower impact speed
    issue # 2: time to automatic braking activation might be dependent on obstacle type
ALR/YH 051118

## Slide 20: Conclusions
  Effectiveness and feasibility of Pre-Crash activation of Brakes and reversible Restraint Systems are widely recognized
  Pre-Crash activation of non reversible Restraint can provide substantial enhancement of protection performances
  Reliability of Sensor decision is crucial
  Recent developments indicate that Sensor Fusion techniques can provide adequate reliability
  Specific approach of reliability issues is nevertheless needed
  Regulations and Rating Test procedures must be revisited to accommodate Pre-Crash interventions
ALR/YH 051118