## Slide 1
ETRTO POSITION
41st GRB Meeting
Geneva 22/02/2005
Informal document No. GRB-41-18
(41st GRB, 22-24 February 2005,
agenda item 1.2.1.)

## Slide 2: Amendment of UN/ECE Regulation 51-03
ETRTO Position
The tyre should not be doubly legislated unless the new amended vehicle noise regulation 51 takes into account the limit(s) for the tyre in a harmonised way with the current Tyre/Road Noise Directive & ECE/Regulation 117.
Any tyre type fulfilling the requirements of EC/Dir 2001/43 & UN-ECE/Reg 117 must be acceptable for conducting the vehicle homologation.

## Slide 3: AMENDMENT of UN/ECE REG 51
Referring to Paragraph 2.2.2 Footnote 1
The tyre contribution for overall sound emission being important, this Regulation has taken into account the tyre/road sound emission regulations
Full coherence between ECE/Regulations 51-03 and ECE/Regulation 117 needs to be addressed

## Slide 4: Limits for the New Amd. UN/ECE Reg. 51-03
The new method has a different approach for the evaluation of the vehicle sound overall emission & is not correlated to the current one.
Therefore the limits for the new method should be established taking into account the new testing conditions only .
ETRTO has established a procedure
to evaluate the coherence
between the 2 Regulations.

## Slide 5
COHERENCY BETWEEN TYRE & VEHICLE REGULATIONS
* To cover all tyre sizes that can fit M1 vehicles the highest tyre limits of ECE/Reg 117 is considered
Limit for the overall
Vehicle Sound Emission
(Power Train / Tyres ratio)
50% -50%
75 dB(A)
Tyre Contribution
50%
Tyre Rolling sound Emission
76 dB(A) *@ 80 kp
70dB(A) @ 50 kph
+ (~1,5 to 2) dB(A) (tyre torque)
-------------
72 dB(A)
Power Train/Tyre ratio
50% - 50%
Corresponds Power Train
Contribution
72 dB(A)
Power Train Contribution
50%


## Slide 6: Proposed Limits versus EC/Dir 2001/43 & ECE/Reg 117

## Slide 7
Unique limit for gasoline & diesel vehicles :
 73 dB(A)
    Off-road & sports category:
    Limits to be proposed after their definition is clarified??
French proposition for M1 vehicle category

## Slide 8: Possible Impact of the French proposition on ECE/Reg 117
M1 vehicles | Sound level limits dB(A)
ECE/Reg 51-03 M1 M1 sportive M1 off-road | 73 ? To be defined ? To be defined
Impact on Reg 117 Highest Limit C1(e) 76 | M1 = -2 dB(A) ~74
Clear definition
is needed
for
M1 sportive
&
M1 off-road

## Slide 9
German proposition for M1 category
CATEGORY | STEP 1 dB(A) | STEP 2 dB(A) | STEP 3 dB(A)
M1 | 71 | 70 | 69
M1s | 73 | 72 | 71
M1o | 72 | 72 | 71
The basis for the definition of M1s & M1o needs to be clarified

## Slide 10: Possible Impact of the German proposition on Tyre Dir 2001/43 & ECE/Reg 117
M1 vehicles | Sound level as Step 1 dB(A) | Sound level as Step 2 dB(A) | Sound level as Step 3 dB(A)
Limits for Reg 51.03 | 71 | 70 | 69
Impact on Reg 117 Highest Limit C1(e) 76 | -4 dB(A) ~72 | -5 dB(A) ~71 | -6 dB(A) ~70

## Slide 11
Is it realistic to require in the future that four tyres would have the same rolling sound emission as only one today?

## Slide 12: Feasibility & Economic impact
As already practiced for many regulations we request that a feasibility study & a cost benefit analysis be performed.

## Slide 13: The Compromise to achieve
The challenge is to build a tyre whose performance characteristics (especially safety related) are all maximized:
Tread wear
Rolling resistance
Tyre weight
Tyre/road noise
  Endurance
  High speed capability
  Dry and wet braking
  Aquaplaning
  Handling
  Heat build up
Safety
Environment

## Slide 14: Legislation for Tyre Rolling Sound Emissions Points to consider
  Improvements in technology allow today’s tyre industry to better manage the interactions between SPL & wet braking distance.
  If limits for SPL are reduced significantly then there is a risk that tomorrow’s tyre industry will no longer be able to manage the tradeoffs.
  Focusing on SPL might jeopardise other safety or environmental performances.
  The level of any performance criterion is the result of the compromise chosen for the other criteria whether legislated or not.
  Care has to be taken when fixing limits based only on the analysis of the tyre rolling sound emission values of a sample of vehicles without considering the whole population of vehicles & tyres.

## Slide 15: Legislation for Tyre Rolling Sound Emissions Points to consider
  Current & future trends in vehicle design entail larger & wider tyres.
  For the moment the benefits in sound level reduction according to the UN-ECE Reg 51.03 have not been demonstrated on the public roads.

## Slide 16
THANK YOU