## Slide 1
GRRF EVSC Ad-Hoc Working Group Document No. EVSC05-07 25 January 2005 Tractor – Trailer Data Communications

## Slide 2: ISO11992 – 2003:
Part 2: Defines Brakes and Running Gear Messages that may be transmitted by the Electric Control Line
Messages Defined:
Towing vehicles: 28 of which 3 are mandatory
Trailers: 57 of which 4 are mandatory
Other than the mandatory messages the support of all other messages is optional

## Slide 3: Informal ISO11992 Working Group:
Members:
Dr.G.Heess - Daimlerchrysler
Mr.P-L.Rydberg - Volvo Sweden
Mr.P.Teyssier - Volvo France
Mr.D.Jordan - Wabco
Mr.J.Crawley - Haldex
Mr.M.Pehle - BPW
Mr.C.F.Ross - Knorr-Bremse (Chairman)
Dr.U.Ulken - Task Force 4 Chairman
Responsible for ISO11992

## Slide 4: Informal ISO11992 Working Group:
Objective: To consider the defined messages and define how they should categorised and how specific messages should be supported.
Message categories:
Functions and associated ISO11992:2003 parameters specified elsewhere within this Regulation that shall be supported by the towing vehicle and trailer.

## Slide 5: Informal ISO11992 Working Group:
Objective: To consider the defined messages and to consider how they should categorised and whether a specific message should be supported.
Message categories:
Functions and associated ISO11992:2003 parameters shall be supported by the towing vehicle .
  No requirement for the trailer to receive any currently defined message status other than those that are mandatory.

## Slide 6: Informal ISO11992 Working Group:
Objective: To consider the defined messages and to consider how they should categorised and whether a specific message should be supported.
Message categories:
Functions and associated ISO11992:2003 parameters that shall be supported by the trailer.
  Wheel based vehicle speed.

## Slide 7: Informal ISO11992 Working Group:
Objective: To consider the defined messages and to consider how they should categorised and whether a specific message should be supported.
Message categories:
When the trailer supports a specified function the trailer shall transmit the associated ISO11992:2003 parameter appropriate to the status of the function and the towing vehicle shall display this status to the driver
  VDC Active.
  Tyre pressure sufficient / insufficient
  Brake lining sufficient / insufficient

## Slide 8: Draft Amendments to ISO11992:
Task Force 4 has proposed the following messages should be included within ISO11992:
Towing Vehicle to Trailer:
VDC Active (Includes both yaw and roll over control)
Request for the “Relative brake demand value for front or left vehicle side”.
Request for the “Relative brake demand value for rear or right vehicle side”.
Wheel based vehicle speed

## Slide 9: Draft Amendments to ISO11992:
Task Force 4 has proposed the following messages should be included within ISO11992:
Trailer to Towing Vehicle:
Support of axle or side wise brake force distribution
Lateral acceleration
Stop lamps request
Geometric data index & geometric data indexed content
Brake cylinder pressures – left & right for up to 3 axles
Wheels speed – first axle left and right
Axle load – identified by wheel location
Time and date information.

## Slide 10: Geometric Data Indexed Content:

## Slide 11: Informal ISO11992 Working Group:
Proposal: To re-introduce Annex 16 into ECE Regulation 13 to specify how certain messages should be supported by the towing vehicle and trailer.
Status: Proposal produced for discussion with the intent of updating ECE Regulation 13.
Group Recommendations:
The draft proposal should be held in abeyance until decisions have been made with respect to ESVC in terms of compatibility and the ISO11992 Standard has been amended to take account of those decisions.

## Slide 12: EVSC Ad-Hoc Working Group:
Considerations:
Are the message categories defined by the Informal ISO1192 Group adequate for the purposes of ESVC?
Regulation 13 Defined – all vehicles with an electric control line
Functions that must be supported by the towing vehicle
Functions that must be supported by the trailer
Functions that when supported by the trailer the status will be displayed to the driver.
What is required:
Functions that when supported by either the towing vehicle or trailer the associated message must by transmitted reflecting the status of the function

## Slide 13: EVSC Ad-Hoc Working Group:
Considerations:
Is the current definition of VDC active satisfactory?
ISO11992 definition:
“Signal which indicates that Vehicle Dynamic Control (VDC) is active passive. VDC contains Roll Over Prevention (ROP) or Yaw Control (YC) or both. Active means that the VDC actually controls the engine torque (in the case of a commercial vehicle) or the wheel brake pressure at one or more wheels.”

## Slide 14: EVSC Ad-Hoc Working Group:
Considerations:
Is the current definition of VDC active satisfactory:
Proposal from the Informal ISO11992 Group:
For the purposes of this Regulation and the above requirement the following should be noted:
“VDC” (vehicle dynamic control) means an electronic “vehicle stability function” which is a function within the braking system and reacts to to stabilise the vehilce during dynamic manoeuvres.
The parameter “VDC Active” shall only be set to 01 when a “vehicle stability function” event occurs where the intent is to impact on vehicle stability. Interventions by the “vehicle stability function” in any process designed to determine the physical characteristics of the vehicle are not considered to be “VDC Active” events.
Recommendation:
ISO11992 definition of VDC active should be revised

## Slide 15: Further Development of ISO11992:
Additional messages:
Towing Vehicle to Trailer:
  Towing vehicle is/is not equipped with a directional control system
  Towing vehicle is/is not equipped with a directional and roll over control system.
  Request for the trailer roll stability function to be disabled
  Request for the trailer yaw control function to be disabled
Trailer to Towing Vehicle:
  Trailer is/is not equipped with a yaw control system
  Reduce engine power – VDC Active
  Trailer does/does not support braking via the electric control line
  Have separate messages that independently define semi and centre axle trailers.
  Trailer roll stability function has/has not been disabled
  Trailer yaw control function has/has not been disabled

## Slide 16: Further Development of ISO11992:
Next meeting of task Force 4: 15 & 16 march 2004
Comments required on the following:
Definition of messages
Proposed messages
Definition of new messages