## Slide 1: EVSC Performance Evaluation
Document No. EVSC05-18
Proposed Approach
Prepared by the Expert from Russian Federation
April 2005

## Slide 2: What do we try to avoid when driving a vehicle ?
Loss of stability…

## Slide 3: Factors of stability loss
Under steer
Over steer
Roll over
One of the factors happens earlier than the other two. It depends on road adhesion coefficient, position of a vehicle center of mass, vehicle track…

## Slide 4: Stability loss happens…
…Due to inadequate steering input:
  Steering wheel angle
  Steering wheel rotation velocity
Outputs concerned:
  Yaw rate
  Yaw acceleration
  Lateral forces on wheels
  Lateral acceleration on wheels
  Roll angle
  Rate of roll angle

## Slide 5: The objective is…
…To choose the the evaluation criteria for “good” stability
“Good” stability” means that there is enough reserve in increase of lateral forces on the front and the rear wheels…

## Slide 6
The manufacturer sets the value of lateral force which can be generated when driving a vehicle without its stability loss…

## Slide 7: Why the EVSC is used?
Automatic application of brakes shall ensure that the limit value of lateral forces cannot be generated.
Brakes shall be applied when certain set value of lateral force is reached only on wheels having enough reserve in increase of lateral force.
The possibility of driving a vehicle on certain types of roads (characterized by minimum curve radius), taking into account the adhesion coefficient, shall exist. For determination of adhesion coefficient, ABS can be used.

## Slide 8
We shall check by the tests what kind of improvements were reached by application of EVSC…

## Slide 9: Setting evaluation criterions…
…In the condition of the particular adhesion coefficient vehicle allows driving on the certain trajectory with the certain speed and acceleration without stability loss

## Slide 10: Proposed test procedures
At high adhesion coefficient:
Step steering input (constant speed, increase of steering wheel angle from run to run);
Entering the curve (constant radius, increase of speed from run to run)
At low adhesion coefficient:
Entering the curve (constant radius, increase of speed from run to run)

## Slide 11: Proposed test procedures (con‘d)
Besides that, we have to be assured that the EVSC does not interfere driving a vehicle:
Lane change (set trajectory, increase of speed from run to run, reaching the maximum allowable speed) performed for the conditions when EVSC is activated and deactivated

## Slide 12: Techniques for avoiding stability loss (rolling over) when testing
Static tilting angle on the test platform can be corresponded with the critical value of lateral acceleration for the conditions of steady-state driving on a circle, when vehicle rolling over can be occurred.
For the conditions of steady-state driving on a circle the steering wheel angle corresponding with the value of lateral acceleration can be determined.
Such steering wheel angle is used as the steering input for the step steering test.

## Slide 13: Techniques for reducing driver’s influence and increasing safety for the Lane-change test
Recording of the driver’s steering inputs corresponding with the position of vehicle on the trajectory. The test runs with the incorrect inputs are excluded from the further consideration.
Outside observer informing the driver by radio in regards to vehicle behavior on the test trajectory.

## Slide 14
Thank you for your attention!