## Slide 1
Head Restraints for Rear Seating Positions
Europe, ECE R-17:
„Non-use position“ clearly recognizable to the occupant as not being included for the use of the head restraint
In Practice: No intermediate position (notch) below 750 mm possible
USA, FMVSS 202 (Draft):
Generate a torso angle difference for the H-point manikin of >10°
or
Return to an “in use” position automatically (occupant recognition system needed!!)
Foldable / retractable head restraints in non use position
Lowest in use position
750 mm above R-point
measured along torso line
R
R
R
R
Head Restraint IWG Document: HR-1-6