## Slide 1: ABSTRACT from ACEA Whiplash Test Series on Repeatability and Reproducibility of Proposed Test Procedures
September 2004
Céline Adalian & Raimondo Sferco
GRSP-Informal Head Restraints GTR
OICA presentation
1 February 2005
Head Restraint IWG Document: HR-1-7

## Slide 2: Purpose of the ACEA Study
Test series conducted in two phases
  Phase 1: Repeatability testing
      3 different seats used
      3 repeat tests of each seat
      All repeat testing conducted at Thatcham
  Phase 2: Reproducibility testing
      3 different seats used
      Testing conducted in five different labs (using the same test protocol)
      One test per configuration

## Slide 3: HRMD Setup used
Initial Geometric assessment with HRMD
Seat = mid height / mid rails
HR = mid position if locked or else fully down
Sample picture of HRMD measurement

## Slide 4: Parameters investigated with respect to test set-up
Initial position of seat
  Seat back angle
  Head restraint stem angle
Initial position of SAE Manikin + HRMD
  H point
  Backset and head restraint height

## Slide 5: Seat setup as results of HRMD measurements Seat back and stem angle
Points marked with a “+” are from the tests made at Thatcham (repeatability assessment)

## Slide 6: HRMD setup HRMD H-point measurement result scatter
Points marked with a “+” are from the tests made at Thatcham (repeatability assessment)

## Slide 7: HRMD setup HRMD height and backset measurement result scatter
Points marked with a “+” are from the tests made at Thatcham (repeatability assessment)

## Slide 8: HRMD torso angle vs backset measurement result scatter

## Slide 9: Conclusions on HRMD measurements and set-up procedure
Analysis shows that reproducibility and repeatability issues still exists.
The use of the HRMD procedure by the different labs caused seat back angle (stem angle) differences of up to 4 deg. This could be seen as significant. One degree change in the stem angle will lead in theory to 15 mm increase in backset.
In the practical measurement the maximum differences of backset and height for reproducibility were more than 20 mm.