## Slide 1: Head Restraints Working Group Meeting Paris, France
February 1-2, 2005
U.S. FMVSS No. 202 Final Rule
Head Restraint IWG Document:HR-1-8

## Slide 2: Topics
Backset Requirement
Dynamic Compliance Option

## Slide 3: Backset Requirement
Definition of Backset:
  Minimum horizontal distance between the back of a representation of the head of a seated 50th percentile male occupant and the head restraint.
FMVSS No. 202 Final Rule Requirement
  Front Outboard Seats – Maximum of 55 mm with head restraint height adjusted from 750 to 800 mm.
  Rear Seats – No limit.

## Slide 4: Head Restraint Measurement Device
Measurement Device
  Measured using the ICBC head form mounted on a SAE J826 manikin.
    At any head restraint height between 750 and 800 mm, inclusive.
    Seat back angle set at 25 degrees
    Seat cushion at highest position.

## Slide 5: Need for Backset
Consensus of biomechanical community:
  Backset is important in limiting internal neck forces and length of time a person is injured.
Supporting Research:
  Olsen, et al. (1990)
    Field data showed reduced backset coupled with greater height results in lower injury severity and shorter duration of symptoms.
  Svensson, et al. (1993)
    Sled test findings indicated that a reduction of backset from 100 to 40 mm would result in significant reduction in whiplash.
  Eichenberger, et al. (1996)
    Field data and sled test showed positive correlation between head restraint backset and head rotation of volunteers and reported whiplash injury.

## Slide 6: Backset Philosophy
Closer is better for safety
  Majority of estimated benefits are due to backset.
Occupant comfort is a competing factor
  When too close, it will prevent occupant from sitting in desired posture.
55 mm is a compromise between these factors
  50 mm is the target backset.
  Additional 5 mm is acknowledgement of ±5 mm measurement variability.
  55 mm will accommodate ≈ 90% of preferred head positions.
    Short stature occupants who prefer seat backs steeper than 25 degrees are most likely to have comfort issue.
    Problem relieved by reclining seat back. 3 mm for every degree.

## Slide 7: Dynamic Compliance Option
Reasons for the option
  Better represents real world events and provides greater assurance of effective performance.
  Encourages continued development of active systems.
May also be used for static head restraint certification.
Dynamic performance criteria
  Head-to-torso rotation limit - 12 degrees
  HIC15 limit – 500
  Measured with Hybrid III 50th percentile male dummy
Static width minimum maintained
  Dynamic test is only in the longitudinal direction.

## Slide 8: Dynamic Compliance Option
Full vehicle sled test
  Target: half sine pulse
    17.3 ± 0.6 km/h ΔV
    86 m/s2 (8.8 g) peak acceleration
    88 ms duration
Seat Setup
  Seat back angle = 25 degrees.
  Head restraint height at mid-position.
  Any backset adjustment position.
  Separate seat cushion adjustment set to highest H-point position.

## Slide 9: Injury Criteria
Whiplash injury criteria
  Many injury criteria have been postulated, but there in no consensus, due to a lack of clear understanding of the whiplash mechanism.
  NIC, Nij, Nkm, NDC, LNL, individual upper and lower neck loads, moments and accelerations.
Head-to-torso rotation
  Consensus among researchers that reducing head-to-torso rotation will reduce neck injury. (Viano, 2002; Yoganandan, 2000; Langweider, 2000)

## Slide 10: Test Dummy
No consensus exists on the best test dummy for whiplash assessment.
  BioRID II – Fully segmented spine
    Exhibits spurious acceleration spikes, ambiguous upper neck loads and incorrect seated height (Kim, 2000 and 2003)
  RID 2 – Thor thorax and articulated neck
    Neck is too soft in flexion and needs support. Less neck rotation than volunteer tests.
  Hybrid III – Solid spine
    Criticized for its neck being too stiff.
    Head rotation vs. displacement similar to volunteers (Viano, 2002).
    Neck flexibility similar of tensed volunteers (Kim, 2003)

## Slide 11: Test Dummy
Hybrid III 50th selected in Final Rule
  Other dummies are not ready, as a regulatory tool.
    BioRID II and RID 2 are still changing.
  Shows sufficient correlation with human head-to-torso rotation (selected injury criterion).
  Has been shown to rank OEM seats as a function of whiplash risk.
  Used by manufacturers as a seat design tool.
NHTSA welcomes development of more biofidelic tools.

## Slide 12: Probability of Whiplash vs. Head-to-Torso Rotation
Whiplash Probability Function
  Using published data of whiplash injury risk of SAAB seats as compared to head-to-torso rotation of Hybrid III dummy, a logistic regression was used to develop a whiplash probability function.
At 12 degrees of head-to-torso rotation the probability of whiplash is 7.3%.

## Slide 14: Questions?
NHTSA FMVSS No. 202 Final Rule documents:
  http://dms.dot.gov
  Search “19807”
    Final rule = 19807-2
    Final Economic Assessment = 19807-1