Distr.
GÉNÉRALE

ST/SG/AC.10/C.3/2006/35
10 avril 2006

FRANÇAIS
Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT DES 
MARCHANDISES DANGEREUSES ET DU SYSTÈME
GÉNÉRAL HARMONISÉ DE CLASSIFICATION
ET D’ÉTIQUETAGE DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport
des marchandises dangereuses

Vingt-neuvième session
Genève, 3-12 (matin) juillet 2006
Point 7 de l’ordre du jour provisoire

PROPOSITIONS DIVERSES D’AMENDEMENTS AU RÈGLEMENT TYPE

Transport de diverses matières des classes 3 à 9 en citernes mobiles

Communication de l’expert du Royaume-Uni

Introduction

- Le Sous-Comité se souviendra qu’au cours des exercices biennaux précédents un système permettant de mettre en conformité les citernes mobiles et les matières selon une méthode rationnelle a été élaboré. Ces matières ont été répertoriées pour la première fois dans la onzième édition révisée du Règlement type. Depuis lors, de nouvelles matières ont été ajoutées à la liste des matières qu’il est possible de transporter dans des citernes mobiles et un certain nombre de documents de travail et d’information ont également cherché à en expliquer les critères sous-jacents aux fins de la mise au point des principes directeurs.

- L’expert du Royaume-Uni n’est pas sans savoir que plusieurs des matières figurant dans la Liste des marchandises dangereuses du Règlement type ne sont pas assorties d’un code-citerne; il joint en annexe la liste de ces matières. Aucune de ces matières ne semble entrer dans la catégorie de celles considérées comme impropres à un transport en citernes mobiles et n’est mentionnée dans les règles générales relatives aux citernes mobiles (voir la partie I du document ST/SG/AC.10/C.3/2005/51, présenté par l’expert des États-Unis d’Amérique).

- L’expert du Royaume-Uni souhaiterait pouvoir débattre de la compatibilité de ces codes-citernes avec les matières énumérées ci-après et, si le Sous-Comité y consent, il propose de répertorier ces codes dans les colonnes 10 et 11 de la Liste des marchandises dangereuses.

Annex (ENGLISH ONLY)

| UN NUMBER | PROPER SHIPPING NAME | CLASS | SUB HAZARD | PG | PROPOSEDPORTABLE TANK CODE | PROPOSED TP CODE | RID/ADR TANK (CODE) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| UN 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 |  | I | T11 | TP1 TP27 | YES (L4BN)(L1.5BN) |
| UN 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 |  | II | T7 | TP1 TP8 TP28 | YES (L1.5BN)(LGBF) |
| UN 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 |  | III | T4 | TP1 TP29 | YES (LGBF) |
| UN 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | 6.1 | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | 6.1 | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1380 | PENTABORANE | 4.2 | 6.1 | I | T21 | TP2 TP7 | YES (L21DH) |
| UN 1471 | LITHIUM HYPOCHLORITE, DRY OR LITHIUM HYPOCHLORITE MIXTURE | 5.1 |  | II | T3 | TP33 | YES (SGAN) |
| UN 1748 | CALCIUM HYPOCHLORITE,DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY | 5.1 |  | II | T3 | TP33 | YES (SGAN) |
| UN 1748 | CALCIUM HYPOCHLORITE,DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY | 5.1 |  | III | T1 | TP33 | YES (SGAV) |
| UN 2208 | CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 10% but not more then 39% available chlorine | 5.1 |  | III | T1 | TP33 | YES (SGAN) |
| UN 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% and not more than 16% water | 5.1 |  | II | T3 | TP33 | YES (SGAN) |
| UN 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% and not more than 16% water | 5.1 |  | III | T1 | TP33 | YES (SGAV) |
| UN 1259 | NICKEL CARBONYL | 6.1 | 3 | I | T14 | TP2 TP7 TP13 TP27 | YES (L15CH) |
| UN 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1647 | METHYL BROMIDE AND ETHYLENE DIBROMIDE MIXTURE, LIQUID | 6.1 |  | I | T14 | TP2 TP13 | YES (L10CH) |
| UN 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 |  | II | T7 | TP2 | YES (L4BH) |
| UN 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 |  | III | T4 | TP1 | YES (L4BH) |
| UN 1699 | DIPHENYLCHLOROARSINE, LIQUID | 6.1 |  | I | T14 | TP2 TP13 | YES (L10CH) |
| UN 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 2024 | MERCURY COMPOUND LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 2609 | TRIALLYL BORATE | 6.1 |  | III | T4 | TP1 | YES (L4BH) |
| UN 3122 | TOXIC LIQUID, OXIDIZING, N.O.S. | 6.1 | 5.1 | I | T14 | TP2 | YES (L10CH) |
| UN 3122 | TOXIC LIQUID, OXIDIZING, N.O.S. | 6.1 | 5.1 | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3123 | TOXIC LIQUID, WATER REACTIVE, N.O.S. | 6.1 | 4.3 | I | T14 | TP2 | YES (L10CH) |
| UN 3123 | TOXIC LIQUID, WATER REACTIVE, N.O.S. | 6.1 | 4.3 | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3140 | ALKALOIDS, LIQUID, N.O.S or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3140 | ALKALOIDS, LIQUID, N.O.S or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3140 | ALKALOIDS, LIQUID, N.O.S or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3141 | ANTIMONY COMPOUND, INORGANIC, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 |  | I | T14 | TP2 TP27 | YES (L10BH) |
| UN 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 |  | II | T11 | TP2 TP27 | YES (L4BN) |
| UN 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 |  | III | T7 | TP1 TP28 | YES (L4BN) |
| UN 2809 | MERCURY | 8 |  | III | T4 | TP1 | YES (L4BN) |
| UN 2904 | CHLOROPHENOLATES,LIQUID, or PHENOLATES LIQUID | 8 |  | III | T4 | TP1 | YES (L4BN) |
| UN 3093 | CORROSIVE LIQUID, OXIDIZING, N.O.S. | 8 | 5.1 | I | T14 | TP2 TP27 | YES (L10BH) |
| UN 3093 | CORROSIVE LIQUID, OXIDIZING, N.O.S. | 8 | 5.1 | II | T11 | TP2 TP27 | YES (L4BN) |
| UN 3094 | CORROSIVE LIQUID, WATER, REACTIVE, N.O.S. | 8 | 4.3 | I | T14 | TP2 TP27 | YES (L10BH) |
| UN 3094 | CORROSIVE LIQUID, WATER, REACTIVE, N.O.S. | 8 | 4.3 | II | T11 | TP2 TP27 | YES (L4BN) |
| UN 3151 | POLYHALOGENATED BIPHENYLS, LIQUID or POLYHALOGENATED TERPHENYLS, LIQUID | 9 |  | II | T4 | TP1 | YES (L4BH) |

-----

# Text boxes

NATIONS UNIES

Secrétariat

ST