| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/53 29 March 2006 ENGLISH Original: ENGLISH and FRENCH |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth-session

Geneva, 20-23 June 2006

Item 4.2.5. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 11 TO THE 02 SERIES OF AMENDMENTS TO REGULATION No. 7

(Front and rear position (side) lamps, stop-lamps and end-outline marker lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-fifth session, and is submitted for consideration to WP.29 and to AC.1 (TRANS/WP.29/GRE/55, para. 24 as amended by ECE/TRANS/WP.29/1050, para. 23).  It is based on document TRANS/WP.29/GRE/2005/27, as amended by ECE/TRANS/WP.29/GRE/2005/27/Rev.1.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

### The title of the Regulation, amend to read:

"UNIFORM PROVISIONS CONCERNING THE APPROVAL OF FRONT AND REAR POSITION (SIDE) LAMPS, STOP-LAMPS AND END-OUTLINE MARKER LAMPS FOR POWER-DRIVEN VEHICLES AND THEIR TRAILERS"

Insert a new paragraph 0., to read (including the insertion of a reference to a new footnote 1/ and a new footnote 1/):

"0.	SCOPE

This Regulation applies to:

0.1.	front and rear position (side) lamps and stop lamps for vehicles of categories L, M, N, O and T 1/; and,

0.2.	end-outline marker lamps for vehicles of categories M, N, O and T.

_________________

1/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

Paragraph 4.2.1.1., the reference to footnote 1/ and footnote 1/, renumber as footnote 2/ and amend to read:

"2/	1 for Germany, .... 48 for New Zealand, 49 for Cyprus, 50 for Malta, 51 for the Republic of Korea, [52 for Malaysia and 53 for Thailand].  Subsequent numbers shall be assigned .... "

Paragraph 6.1. (the table), the reference to footnote 1/ and footnote 1/, renumber as footnote 3/.

Paragraph 6.1. (the table), the reference to footnote 2/ and footnote 2/, renumber as footnote 4/.

Paragraph 7.2., the reference to footnote 2/ and footnote 2/, renumber as footnote 5/.

- - - - -