## Slide 1
Vehicle noise behavior - French concept
Vehicle speed
Vehicle noise
(N_i ; v_i)
Vehicle noise simulated (N ; v)
Vehicle noise measured (N ; v)
L wot i
L wot measured
L wot simulated
Model :
L tyre = L_tyre (v ref)+ a*log (v/v ref)
L engine expecting = L engine (N ref) + b (N – N ref)
L vehicle (N, v) = L engine expecting (N) « + » L tyre (v)
L limit = L vehicle (N, v) +2 dB
L tyre (v)
≥ 3 dB
Homologation point
from Annex 3
limit (N ; v)
2 dB
ASEP Measurements
Critique :
Compliquée
Bruit pneumatique incomplet (effet couple)
Robuste
Informal document No. GRB-44-3
(44th GRB, 4-6 September 2006
agenda item 1.2.1.3.)

## Slide 2
Vehicle noise behavior French concept : Construction of the model
Vehicle speed
Vehicle noise
L wot i (N ref, v ref)
Tyre noise measurements
L wot i homologation point
from Annex 3
V ref
Measurements
Tyre noise model :
L tyre = L_tyre (v ref)+ a*log (v/v ref)
Régression
logarithmique
a et L tyre (v ref)
L engine (N ref) = L wot i (Nref) « - » L tyre ( v ref)
L engine (N ref)
Measurements
Measurements

## Slide 3
Vehicle noise behavior French concept : Model Application for (N, v)
Vehicle speed
Tyre noise
Model :
L engine expecting = L engine (N ref) + b (N – N ref)
L tyre (v)
Engine speed
Engine noise
L engine expecting (N)
Model :
L tyre = L_tyre (v ref)+ a*log (v/v ref)
Tyre noise calculation at v
V
L tyre (v)
N
L engine expecting (N)
Engine noise expecting at N
Slope 5 or 6 dB / 1000
Model :
L vehicle (N, v) = L engine expecting (N) « + » L tyre (v)
L engine (N ref)
Tyre noise measurements