## Slide 1: Application of Low Noise Road surfaces in the Netherlands: Excellent results but not enough to meet the legal targets
Prepared by the Netherlands
For GRB 44 Sept 2006 Geneva
Informal document No. GRB-44-5
(44th GRB, 4-6 September 2006
agenda item 6.)

## Slide 2: Why should we reduce noise? Noise = Health
DALY= Disability Adjusted Life Years

## Slide 3: Noise abatement
Health  Laws  Levels of protection
Conventional way: barriers and insulation.
High growth of traffic  uncontrollable rise of cost
NL: 4 bln EURO for national infrastructure alone
All studies: source abatement is most effective and most cost efficient
(max 1 bln EURO)

## Slide 4: Sources of road traffic noise
engine
intake
exhaust
gearbox
tyre/road contact
wind

## Slide 5: Source related noise abatement in the road sector
  Direct noise abatement at the source
    Vehicles (power train and wind noise)
    Tires
    Road surfaces
  Indirect noise abatement at the source:
    Town & infrastructure planning
    Traffic management
      Speed & Driving behavior
      Restriction of vehicles allowed in areas or time

## Slide 6: Responsibilities
  Vehicle Noise limits: EU and UN/ECE
  Tire Noise limits: EU and UN/ECE
  Road surfaces: national or local

## Slide 7: Potential of traffic noise reduction engine, tyre and road surface
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Porous asphalt:
Since 1940? reduction of splash & spray on airport runways Since 1980: application as low noise road surface (-3 dB at 120 km/h)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Acoustic optimisation of porous asphalt
1990: Two layered porous asphalt with improved surface texture
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: new types of silent Roads
2000: application of semi porous thin layers (very smooth surface texture
Two-layered Porous Asphalt
Thin Layer (semi porous)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Noise reducing Asphalt Layers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: History of low noise road surfaces in the Netherlands
Number of registered
low noise road surface products
2001: Stimulation program Min Env
2004: Innovation program
Min Env + Min Transp
1998: Type approval system Min Env
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Croad for light vehicles
0 = reference
- 2
- 4
- 6
- 8 dB(A)
50 km/h
120 km/h
speed
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Status low noise surfaces in the Netherlands 2006
Highways:
60% single layer porous
3% double layer porous
Pilots on thin layers
Future
Double layer = standard in high noise regions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Can we sit back and relax now?
Inhabitants of EU15 exposed to road traffic noise (data from 2000):
>55 dB(A) >65 dB(A) >75dB(A)
Percentage of population 32% 13% 2%
Number of inhabitants (mln) 120 49 8
Conclusion: NO!
the necessary reduction is much bigger than the 5 dB we get from road surfaces
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Spread in vehicle noise levels build up of two components: road surface effect, tyre/vehicle effect
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: What if we do not achieve the vehicle/tire targets?
Health targets are often not reachable
Local situations will enforce more often drastic measures
  drastic reduced speed
  Toll tunnel
  total vehicle ban
Final cost for society is much higher than necessary

## Slide 18: The end
Thank you for your attention