## Slide 1: Additional Sound Emission Provisions Proposal from France
GRBIG-ASEP-02-002

## Slide 2
New test method of ECE51 represents the actual behaviour of today's cars in urban traffic
But this new procedure does not cover almost all realistic behaviours in urban traffic (higher engine speed)
Most of vehicles under normal driving conditions does not differ significantly from a "normal behaviour“
But what is a "normal behaviour“ and how can we identify it ?
Background

## Slide 3
« Non linear » noise causes can be identify on engine
(intake system, switches, exhaust system, controlled valves, adaptive software, ...)
Tyre/road doesn’t make « non linear » noise
 Engine ONLY need to be studying IN CASE OF DOUBT
“Normal behaviour"

## Slide 4
Tests made on full throttle condition on ISO 10 844 test track
Engine noise is given by : L engine = Lvehicle – Ltyre
Limit is given by the homologation point and Engine noise behaviour
Experimental approach and ASEP limit curve
Homologation point :
- Engine noise :
L wot rep eng = Lwot rep – L tyre(50 km/h)
Engine speed
N L90 = 1,6509×PMR-0,3166
Engine noise behaviour : 5 dB / 1000 rpm
Limit :
0,005 × (N – N L90) + L wot rep eng + x dB

## Slide 5
Off Cycle Emission need to cover high engine speed and urban traffic behaviour :
  Engine speed from NL90 to N max
  Speed from 20 to 70 km/h
  Acceleration under a max
Off Cycle Emission shall identify
« non linear » noise :
  Tyre noise must to be significantly
  lower than Engine noise
Gear ratio is chosen in this range
Limit curve of engine speed, speed and acceleration

## Slide 6
Practical proposal
2 practical approaches to determine Engine noise :
Few Pass by to cover NL90 to N max
Few Coast down to qualify Tyre noise
One Pass by to adjust
Lwot(7.5m) to Lwot(2.5m)
One Pass by to cover NL90 to N max
Few Coast down to qualify Tyre noise
Several points
Continuous line

## Slide 7
Explicit criteria and informations on the method
Globally applicable
Performance based on realistic behaviours in urban traffic
(high engine speed and urban speed and acceleration)
In technology neutral : No definitive choose of gear
Repeatable / reproducable
Fitness for purpose : To identify « non linear » noise
Relative limit based on Annexe 3 : L wot rep
Gear selection : Variable
Entry speed : from 20 to 70 km/h
Target acceleration : No target acceleration
Maximum engine speed : to be define
Exit speed : Variable
Wide open throttle
Mulitple test conditions : Yes
Engine speed range : NL90 to N max
Relating to “doubt” ?
Work load Only few passes need to be done