## Slide 1: FRONTAL COLLISION OF BUSES
Information learned from the ECBOS Summary Report
Dr MATOLCSY Mátyás
Informal document No. GRSG-90-31
(90th GRSG, 24-28 April 2006
agenda item 1.4.7.)
Transmitted by the expert from Hungary

## Slide 2: GENERAL INFORMATION
The accident analysis (statistics) of ECBOS project covers
5 years period: 1994-1998
8 EU countries: France Germany Netherlands
Austria Italy Spain
UK Sweden
Bus categories: M2, M2(above 16 passengers), M3
but not similarly in the 8 countries

## Slide 3: GENERAL INFORMATION
Types of accident:
Frontal collision
Frontal accident
Rollover
Overturning
Bus runs out of road / turns off the road
Side impact
Rear impact
Other accident
Non collision accident
Unknown type of accident

## Slide 4: GENERAL INFORMATION
The statistics are based on 8 EU countries
The whole community 25 EU countries
Whole Europe 43 countries
Contracting parties of 1958 Geneva Agreement 43 countries
Contracting parties of R107 bus regulation 35 countries
Contracting parties of R.66 roof strength regulation 32 countries

## Slide 5: GENERAL INFORMATION
Definitions used for casualties
Fatal in the accident / at the scene
in 1 day
in 6 days
in 7 days
in 30 days
Serious injury hospitalized patient
more than 1 day in hospital
more than 3 days in hospital
more than 6 days in hospital
Slight injury everyone who needs medical treatment, but no need for hospitalization *
Injury without specification used in 3 countries
* note: the number of slight injuries is generally underreported in police reports, says ECBOS report

## Slide 6: INJURY RATIOS IN FRONTAL COLLISIONS
 | Frontal accident casualties compared to all bus accident casualties | Fatalities related to all casualties in frontal accidents | Frontal accidents fatalities compared to all fatalities in bus accidents
Austria (1) France UK Netherlands Spain Sweden | 4,1 % 71,2 % 60,0 % (2) 56,7 % (3) 9,6 % (4) 14,0 % (5) | 9,2 % 7,2 % | 12,7 % 62,7 % 34,0 % 83,3 % 24,5 %
Germany Italy |  | No detailed data No detailed data | 
Remarks: (1) The ratio of unknown / not specified accidents is high, 30%
(2) The „frontal impact” is emphasized instead of „frontal accident”
(3) On city roads; on rural roads this figure is 46,7%
(4) Without frontal collisions against fixed obstacles (only against vehicles)
(5) Only collisions with other vehicles are counted. „Single vehicle accidents” (e.g.
frontal collision with rigid objects, rollover) cover 31,4% of the total casualties.

## Slide 7: DRIVER/PASSENGER (D/P) INJURY RATE
Assumptions:
D/P injury probability (IP) in different accident situations:
  in frontal impact the driver has higher IP than the passenger
  in side impact the driver has lower IP
  in rear impact the driver has lower IP
  in rollover they have equal IP
  in non impact type accidents the driver has lower IP
Only the frontal impact is more dangerous for the driver than for the passengers

## Slide 8: DRIVER/PASSENGER (D/P) INJURY RATE
Assumptions (cont.):
The average passenger capacity of a bus is 50
The buses are fully loaded in the accident
The IP is equal for all passengers in frontal collisions
These assumptions contain simplifications, but they help to recognise general tendencies

## Slide 9: DRIVER/PASSENGER (D/P) INJURY RATE
From the ECBOS statistics
D/P fatality rate D/P injury rate
Austria (3/29) 0,10 5:1 0,08 4:1
France (16/98) 0,16 8:1 0,13 7:1
Germany (20/75) 0,27 13:1 0,11 6:1
UK (6/93) 0,06 3:1 0,09 5:1
Italy (30/74) 0,41 20:1 0,16 8:1
Netherlands (1/8) 0,12 6:1 0,18 9:1
Spain (24/176) 0,14 7:1 0,09 5:1
Sweden (4/10) 0,40 20:1 0,40 20:1
Average 104/563 0,18 9:1 0,16 8:1

## Slide 10: DRIVER/PASSENGER (D/P) INJURY RATE
Comparison between ECBOS data and earlier estimations
 | D/P fatality rate | D/P serious injury rate | D/P injury rate
ECBOS min. value ECBOS max. value ECBOS average | 3:1 20:1 9:1 |  | 4:1 20:1 8:1
Japanese data (1992-94) German data (1979) UK data (1971-92) Spanish data (1984-88) | 80:1 8:1 5:1 6:1 | 13:1 10:1 4:1 | 2:1
All types of bus accidents are considered

## Slide 11: DRIVER/PASSENGER (D/P) INJURY RATE
Japanese data (1992-94) for D/P casualty rates
In frontal collisions the estimated ranges for D/P casualty rates
  fatality (10 ~ 100) : 1
  serious injury (6 ~ 20) : 1
  slight injury (3 ~ 6) : 1
Casualties | In all bus accidents | In frontal collisions
fatality serious injury slight injury | 80 : 1 13 : 1 7 : 1 | 120 : 1 18 : 1 4 : 1

## Slide 12: CONCLUSIONS, PROPOSALS OF THE ECBOS REPORT
Use 3pt seat belt in (correct restraining of children)
Develop seat regulations (R14, R80)
Specify deceleration pulse for M2 vehicles
Protect driver / co-driver in frontal impact
Improve compatibility between buses and other vehicles

## Slide 13: PROPOSAL OF AN EXPERT GROUP (MADRID MEETING)
This table was presented in the inform.doc. GRSG-87-31
 | Object of regulatory work | Related ECE regulation | Related EU directive | Responsible WG | Proposed priority | Estimation of needed work
1. 2. 3. 4. 5. 6. 7. 8. | Strength of bus seats and their anchorages General safety of buses (all kind) External projection Safety belt anchorage Structural integrity Underrun protection Limit of deceleration Compatibility and agressivity | R.80/01 R.17/04 R.10,07/Rev.1. R.61/00 R.14/05 R.16/04 R.107/Rev.1* R.93/00 - - | 91/676-03/20EC 2001/85/EC 76/115-96/38EC 77/541-00/3EC 2001/85/EC 92/114/EC - - | GRSP GRSG GRSG GRSP GRSG GRSG GRSG GRSP | A B B B A B B B | M M S S M M L M
Symbols:
A = first priority
B = second step priority
* = it could be an independent new regulation, too
S = short work, less than 2 years, it does not need further study and analysis
M = medium size work, 2-4 years, it needs certain study
L = Long term work, more then 4 years, further study, analysis, international discussion is nee