#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2007/40

23 August 2007

Original:  ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-second session

# Geneva, 3-12 (a.m.) December 2007

# Item 6 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Definition of closed cargo transport unit

Transmitted by the expert from Belgium */

## Background

1.	In July 2007, the Sub-Committee of Experts on the Transport of Dangerous Goods decided to introduce the following definition of a closed cargo transport unit in section 1.2.1:

Closed cargo transport unit: means a cargo transport unit which totally encloses the contents by permanent structures. Cargo transport units with fabric sides or tops are not considered closed cargo transport units.

(See also ST/SG/AC.10/C.3/62, paras. 61-62 and annex 1).

2.	The structure of this text (the definition itself, followed by an exception) is not optimal; a definition ought to be written in such a way that there are no exceptions to it.

3.	Moreover, the exception made for cargo transport units with fabric sides or tops does not eliminate all unacceptable possibilities:

-	some flexible sides or tops remain possible (e.g. made out of plastics film, if someone might wish to use this material);

-	rigid sides or tops with openings in them (e.g. with a lattice-work or barred surfaces).

Proposal

- In consideration of the foregoing, it is proposed to amend the definition of a closed cargo transport unit in section 1.2.1 to read as follows:

Closed cargo transport unit: means a cargo transport unit which totally encloses the contents by permanent structures with complete and rigid surfaces.

____________

# Footnotes

*/ In accordance with the programme of work of the Sub-Committee for 2007-2008 approved by the Committee at its third session (refer to ST/SG/AC.10/C.3/60, para. 100 and ST/SG/AC.10/34, para. 14) (Further measures to facilitate global harmonization of transport of dangerous goods regulations with the UN Model Regulations).

# Text boxes

STSTE

Secretariat