## Slide 1
Guidelines for Safety Critical Warnings
Peter Burns
IHRA-ITS
Transmitted by the representative of Canada | Informal Document No. ITS-15-09 15th ITS informal group, 16 November 2007, agenda item 5.

## Slide 2
Need for Warning HMI Standards
Lack of specific standards for driver assistance system HMI
New technology provides good opportunity to standardize
Standard HMI will improve system performance with:
  Better understanding and attention from drivers
  Reduced confusion
  More accurate and consistent expectations

## Slide 3: Integrated Safety Chain
Normal driving
Deviation from normal driving
Emerging situation
Critical situation
Crash unavoidable
(Tingvall, 2007)
Notes: <number>
<footer>
<header>
<date/time>
Tongvall describes five stages in the sequence of events leading up to a crash –“normal driving”, “deviation from normal driving”, “emerging situation”, “critical situation” and “crash unavoidable”. Each of these stages can be seen as defining a set of countermeasures. So where do we start with warnings? We decided to look at the most critical situations, the last few seconds that provide an opportunity to avoid a crash

## Slide 4: Safety Critical Warnings
A signal informing the driver of a hazardous situation, which if not corrected by an immediate action (0 to 3 seconds), will result in equipment damage and/or personal injury.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: A WARNING SYSTEM CAN BE NO BETTER THAN ITS INTERFACE
FAILURE DUE TO:
Not noticed
Confusion
Misunderstood
Ignored it…
TIMELY &
APPROPRIATE
RESPONSE
WARNING PERFORMANCE
  Sensor coverage
  Sensor reliability
  Sensor accuracy
  Warning decision logic
  Warning itself
WARNING FUNCTION
Senses road traffic environment
Filters & processes information
  for hazard
Calculates severity & urgency
Issues warning
WARNING
FAILURE
No response
Inappropriate response
Slow response
WARNING
SYSTEM
WARNING!
HAZARD

## Slide 6: Factors mediating warning effectiveness
Conspicuity
Comprehension
Driver frustration and annoyance
Expectancy
Frequency of warnings
Individual differences and condition
Response options/ uncertainty
Trust
Willingness and/or ability to comply
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Warning design considerations
Activation criteria – When? ….. Frequency
Levels and priorities of warnings
Presentation modality, information and location
Response options
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Crash avoidance response options
Immediate hard braking.
Immediate steering manoeuvre.
Immediate termination of initiated or initiating action.
Seek awareness of situation and perform one of the above responses.
Immediate decision to retake control by the driver.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9
Current Status and Scope
Some good generic warning guidelines are available, but these need to be consolidated, promoted & applied.
IHRA-ITS working group is developing warning guidelines to support the UN-ECE WP.29 ITS informal group.
These guidelines are based on a consolidation of published guidelines, research and expert opinion.
Scope - safety critical warnings.
These guidelines are intended for people who design and evaluate high-level warning systems for vehicles.

## Slide 10: Starting Principle
There are more effective and reliable ways to protect people and property than warnings:
Eliminate the hazard through improved design, or
Offer some form of protection to limit damage.
If that does not work then - Warn
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11
Eliminate the blind spots
Actively prevent back-up collisions
Warn
Warning System Last: Example

## Slide 12: Guidelines
Warnings should be distinguishable in the driving environment (Sweden).
Warnings should be distinct from other warnings. (Japan).
Warnings should be displayed in a least two modalities (UK).
Warnings should provide spatial cues to the hazard location (Canada).
Warnings should inform the driver of the hazard (UK).
Warnings should elicit timely responses or decisions (Canada).
Multiple warnings should be prioritized (Canada).
False / nuisance warnings rate should be low (France).
Non-operational system status and degraded performance of warnings should be displayed (Australia).
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Guideline 1
Warning shall be distinguishable in the driving environment.
The warning shall be possible to detect in the presence of irrelevant signals and ambient noise.
Testing should be undertaken to determine if a warning can be correctly perceived.
Examples
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14
Volvo (2007)

## Slide 15: Guideline 2
Warnings should be distinct from other warnings
Warnings should be noticeable without confusion with other messages or warnings.
Testing should be undertaken to determine if a warning can be correctly distinguished from other warnings in the context of use.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16
Obstacle
!
Low fuel
!
Example 2

## Slide 17: Guideline 3
Warnings should be displayed in at least two sensory modalities.
Warnings presented in only one single modality may be missed if that modality is already occupied. Presentation in more than one modality increases the probability of perception.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18
Example 3

## Slide 19: Guideline 4
Warnings should provide spatial cues to the hazard location.
Hazards can be located to the front, sides, rear and corners of the vehicle. They can be near, far, stationary and approaching.
Where is it?
Orienting a driver to the source of a hazard can hasten responses and lead to more appropriate responses.
If this is not possible, care should be taken not to orient the driver inappropriately – away from the hazard or appropriate response options.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20
Blind Spot
!
Example 4

## Slide 21: Guideline 5
Warnings should inform the driver of the nature of the hazard
Communicate the element(s) of the situation that the warning system has identified as an immediate threat to the safety.
What is it?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22
Slow
Curve
Example 5
Slow
!

## Slide 23: Guideline 6
Warnings should elicit timely responses or decisions.
Warnings should increase a driver’s opportunity to avoid threats. Timely responses are critical for threat avoidance.
Onset of warnings should account for driver perception-response times.
Early warnings provide more opportunity to avoid a situation, however they can be a nuisance if they become frequent and unnecessary (McGehee et al., 1998).
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Examples 6
Good Example: A forward collision warning comes on with just enough time for most drivers to detect the warning, chose an avoidance response and take action.
Bad Example: A forward collision warning system warns the driver too late, when it is no longer possible to avoid or mitigate the collision. Or it warns the driver too early, and the signal becomes a nuisance.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Guideline 7
Multiple warnings should be prioritized.
Multiple warnings should be prioritized so the most urgent and critical messages are effectively communicated to the driver.
Warnings can be managed by prioritization procedures that establish the relative timing and urgency of messages. Prioritized warnings will help to avoid confusing the driver with overlapping signals.
In the case of simultaneous high-level warnings, all messages should be communicated to the driver.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Examples 7
1. A forward vehicle starts braking as your vehicle crosses the lane marking.
The Forward Collision Warning (FCW) overrides the Lane Departure Warning (LDW) due to higher priority (urgency and criticality). Use case from INSAFES (2007)
2. Simultaneous LDW and message from the navigation system (e.g., turn left). Guidance message is overridden by a lane departure warning.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Guideline 8
False and nuisance warnings rate should be low.
High false alarm rates reduce driver trust in the system and a lack of trust can reduce response time.
Too many nuisance alarms can be irritating and effect the utility of the system. Adjustable warning thresholds can help to reduce nuisance alarms.
Providing some control over sensitivity settings may help to improve acceptance and performance.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Examples 8
Good Example: A lane departure warning system that only warns when the vehicle is crossing the lane boundary.
Bad Example: A forward collision warning system that frequently warns for non-threatening obstacles beyond the vehicle’s path of travel.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Guideline 9
Non-operational or degraded performance of warnings should be displayed.
The driver should be informed whenever the system is malfunctioning or operating outside its operating conditions (non-functioning).
A brief auditory tone can be used to indicate a malfunction followed by a continuous visual message (Campbell et al., 2007).
The driver should be informed whenever the warning system is off.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30
Off
Example 9

## Slide 31: Summary and Conclusions
HMI is crucial for ITS warning system effectiveness
First consider ways to eliminate or mitigate hazards rather than relying on a warning system
Consistent application of good HMI standards and warning guidelines will improve system performance
Further research should focus on warning parameters, particularly for assessment procedures.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32
Thank you