PROPOSAL FOR A CORRIGENDUM TO REGULATION No. 13 (Braking)

#### Note by the Secretariat

A.	PROPOSAL

Annex 5,

Paragraph 1., amend to read:

"1.	This annex applies to certain vehicles for which are subject to section 9.2.3. of Annex B to the European Agreement concerning the International Carriage of Dangerous Goods by Road (ADR) contains specific requirements as concerns anti-lock and endurance braking performance."

Add new paragraphs 2.4. to 2.4.1., to read:

"2.4.	Braking requirements for EX/III vehicles of categories O1 and O2

2.4.1.	Notwithstanding the provisions of paragraph 5.2.2.9. of this Regulation, EX/III vehicles, as defined in Regulation No. 105, of categories O1 and O2, irrespective of their mass, shall be equipped with a braking system which automatically brakes the trailer to a stop if the coupling device separates while the trailer is in motion."

Ｂ.	JUSTIFICATION

According to the table in section 9.2.1. of Part 9 to the ADR (Requirements concerning the construction of vehicles), EX/III, vehicles shall fulfill the requirements of paragraph 9.2.3.2.2., which specifies:

"9.2.3.2.2.	Trailers shall be fitted with an effective braking device which acts on all the wheels, is actuated by the drawing vehicle's service-brake control and automatically stops the trailer in the event of breakage of the coupling."

However, it is possible at the present time to type approve an EX/III trailer of category O2 with a maximum mass not exceeding 1.5 tonnes according to current text of paragraph 5.1.3.1. of Regulation No. 105 and of Annex 5 to Regulation No. 13 without fulfilling the above mentioned requirements of paragraph 9.2.3.2.2. of the ADR.  Regarding O1 vehicles, which are not covered by Regulation No. 105, the prescriptions of Regulation No. 13 are not in conformity with the prescriptions of paragraph 9.2.3.2.2. of Part 9 of the ADR.

The above-mentioned proposal aims at correcting this inconsistency and aligning the provisions of Annex 5 to Regulation No. 13 with those specified in paragraph 9.2.3.2.2. of the ADR.

- - - - -