## Slide 1: Revision of ECE R41
ASEP Concept for Motorcycles
By Heinz Steven
20.02.2007

## Slide 2: Aim
Check the noise emission behaviour of a motorcycle for driving conditions that occur in real world traffic but are not covered by the ISO 362-2 test(s) (not to exceed concept). This should especially include driving conditions on rural roads.
The checks should make sure that the noise emission behaviour of the motorcycle under these conditions does not deviate significantly from what one would expect from the ISO 362-2 results.

## Slide 3: ASEP test area limitations
Vehicle speeds between 20 km/h (v_AA’) and 80 km/h (v_BB’)
Engine speeds at BB’ up to 0.85*(s – n_idle) + n_idle for pmr <= 66,
up to 3,4105*pmr-0,3315* (s – n_idle) + n_idle, for pmr > 66
with s – rated engine speed in min-1,
n_idle – idling speed in min-1
pmr = Pn in kW/(m0 in kg +75)*1000
pmr is the power to mass ratio index. This is the rated power of the vehicle (Pn) in kW di-vided by the kerb mass of the vehicle (m0) in kg + 75 (to account for the mass of the driver) and multiplied by 1000.

## Slide 4: ASEP test area limitations

## Slide 5: ASEP test area limitations

## Slide 6: Reference Point
The reference point is L_wot_i, the wot test result from ISO 362-2 in gear i and n_PP_i, the corresponding engine speed at PP’.
For engine speeds within the test area but other than n_PP_i a slope has to be defined in order to take into account that the the noise emission increases with engine speed.
The slope might be different for engine speeds below and above n_PP_i.
In addition to that it may be necessary to consider an additional tolerance value of x dB.

## Slide 7: Example for an ASEP limit curve
Reference point, 3000 min-1, 74 dB(A), (tolerance to be added)
n_max ASEP

## Slide 8: Tests to be done
The data of the ECE R41 test campaign in 2006 do not allow the definition of a complete ASEP test. Additional data has to be collected in order to
  define the appropriate ASEP limit curve (slope; tolerance),
  identify the appropriate PMR threshold value below which it may be not necessary to apply ASEP tests.
A test protocol was developed by the R41 task force that defines 3 different driving conditions (vehicle and engine speeds and gear selection) to be used for test campaigns.

## Slide 9: Revision of ECE R41
Thank You