## Slide 1: UN/ECE GRB R41WG
DEG conclusions
8 August 2007
Notes: <number>

## Slide 2: General - 1
In February 2007, GRB agreed:
  That ISO362-2 is practical and repeatable
  To increase the number of MCs in the database to 60 ( from an original sample size of 33)
  That the database is diverse and broad enough and that R41WG/DEG should prepare the data for a limits discussion (standstill limits and reduction effects; cost-efficiency modelling ideas; consequences for resources (equipment, time))
  That R41WG/DEG should collect more ASEP data (to define ASEP limit line and the PMR exclusion cut-off value)
Notes: <number>

## Slide 3: General - 2
From April to July 2007, ASEP tests were conducted by Japan & IMMA
Meeting on 2 July 2007 to check data collection process
4/DEG meeting on 7/8 August to analyse data and prepare material for R41WG and GRB in September 2007
Notes: <number>

## Slide 4: R41 – ISO correlation

## Slide 5
Sports
Small engine capacity
Big engine capacity
Utility / Comfort
1170cc
1352cc
ON/OFF ROAD
660cc
499cc
1284cc
897cc
798cc
674cc
400cc
656cc
996cc
680cc
498cc
CRUISERS
499cc
1130cc
1584cc
3X49cc
3X 125cc
95cc
106cc
2298cc
249cc
599cc
1552cc
399 cc
998cc
2 x 125cc
Japan
IMMA
650cc
BASt
998cc
India
SUPERSPORTS
SPORTS &
TOURERS
UTILITY & SCOOTERS
223cc
165cc
149cc
99cc
88cc
Class II
Class I
2X599cc
125cc
125cc
244cc
656cc
1157cc
656cc
1157cc
Class I :Up to 25kW/t
Class II :25-50kW/t
Class III :Above 50kW/t
2X49cc
3X100cc
110cc
249cc
249cc
3X399cc
1157cc

## Slide 6
ECE R41-03 vs ISO 362-2

## Slide 7: Standstill limit values
Standstill limit values are those which give the same degree of severity as the R41 limit values taking into account the change in the test procedure
These values were calculated from the Lurban noise levels that correspond to the highest valid R41 noise test result (keeping any difference between the R41 result and its limit value)

## Slide 8
ECE R41-03 vs ISO 362-2
Standstill limit
current limit value

## Slide 9
ECE R41-03 vs ISO 362-2
Standstill limit
1 outlier (R41 test in 3rd gear; ISO test in 2nd gear)

## Slide 10
ECE R41-03 vs ISO 362-2
Standstill limit
Deletions = 2(COP) + 1 (cycle detection) + 4 (gearing) (filter: LISO,WOT – LECE>2 dB(A))
Cycle detection
Out of COP tolerance
Out of COP tolerance
Tuned gearing (4 outliers (3 at 80 dB(A); 1 at 79 dB(A))

## Slide 11
 | ECE R41 |  | ISO 362-2 |  | Vehicles excluded (%)
 | Class | Limit (dB) | Class | Limit (dB) | 
Class 1 | -80cc | 75 | < 25 kW/t | 74 | 0 (but reduced margin relative to limit)
Class 2 | 80-175cc | 77 | 25-50 kW/t | 75 | 13
Class 3 | 175cc- | 80 | > 50 kW/t | 78 | 16
Standstill limit values

## Slide 12: Cost-effectiveness analysis
Qualitative benefits exist (more robust test procedure for OE and RESS, excluding number of existing models at standstill limits)
Most existing ambient noise prediction models do not cover MCs; the limited number of models that do cover MCs show that Leq contribution from MCs is small except for cities with high MC population
Reliable quantitative cost-effectiveness analysis of reduction scenarios beyond standstill limits not possible although costs could be assessed

## Slide 13: Consequences for resources
Potentially more lengthy/costly but offset by:
  Duration of noise tests small compared to overall noise test session (eg. travel to and from test site; test site set-up; establishing entry speed; ...)
  Increasing experience for testers and preparatory deskwork
  Reducing # test runs from 4 to 3
Higher equipment specifications needed but already commonplace
Notes: <number>

## Slide 14: ASEP campaign results

## Slide 15: General
Tests to the latest ASEP test protocol were done by Japan and IMMA
25 MCs were used (61 to 385 kW/t)
ASEP data was analysed by linear regression to establish the noise increase/decrease slopes

## Slide 16
Lmax(n) = Lwot i + 5*(n – ni)/1000 + 2 dB (n>ni)
Lmax(n) = Lwot,i – 0.95*(ni - n)/1000 + 2 dB (n < ni)
ASEP limit line
2 dB/1000 rpm

## Slide 17
Exclusion of MCs with PMR below 130 kW/t

## Slide 18
Exclusion of CVT MCs

## Slide 19: Enforcement testing

## Slide 20: Enforcement options
At international level:
  Type Approval & Conformity of Production
At national level:
  Stationary test with reference value
  Drive-by acceleration test with reference value (DEG awaits BASt research conclusions)

## Slide 21: Summary

## Slide 22
Base TA test |  |  |  |  | ASEP test (R41WG to discuss its use) | Roadside enforcement (via national implementing legislation) |  | Tampering
ECE R41 |  | ISO 362-2 |  | Vehicles excluded (%) | +5dB/1000rpm -0.95dB/1000rpm 2dB tolerance | Stationary | Drive-by | Prohibition of easily removable parts
Class | Limit (dB) | Class | Limit (dB) |  | PMR>130 kW/t + exemption of CVT | See ECE R41 | [Lowest WOT gear data as reference value] | Provisions for multi-mode manually adjustable systems
-80cc | 75 | < 25 kW/t | 74 | 0 (but reduced margin relative to limit) |  |  | [Entry speed estimated on speedometer] | Tightening the type approval of RESS
80-175cc | 77 | 25-50 kW/t | 75 | 13 | Other issues: 3 runs instead of 4 family concept for class boundaries (lowest PMR version to be tested with corresponding lower class limit) |  |  | 
175cc- | 80 | > 50 kW/t | 78 | 16 |  |  |  |