## Slide 1
ASEP GRB 08 Tyre influence in vehicle noise
Den Haag – 19 th to 21 th september 2007

## Slide 2
Tyre noise contribution and influence
Large variations between tyre noise and L wot i : from 2 dB to 10 dB
This difference depends of vehicle design :
- engine,
- tyre
- gear ratios
This influence introduce a gap between
vehicle noise in gear i
and vehicle noise in gear i-1 or i-n
This influence may be important
ACEA Data base

## Slide 3
Simulation using F/D model
Engine speed
Vehicle noise
Vehicle noise expected (N ; v)
L wot i
To evaluate this influence, vehicle noise behaviour is studying
by using the simple and realistic vehicle noise model
Using by F/D proposal
F/D Model :
L vehicle (N, v) = L engine (N) « + » L tyre (v)
L tyre = L_tyre (v ref)+ a*log (v/v ref)
L engine = L engine (N ref) + b (N – N ref)
L tyre (v)
Gear i
Gear i-1

## Slide 4
Vehicle simulated :
Gear i-n : 15 kph/1000 rpm
Gear i : 30 kph/1000 rpm
L wot i = 74 dB(A)
Tyre :
L tyre 50 kph = 72 dB(A) or 64 dB(A)
a = 40
Engine :
b = 5 dB/1000rpm
Simulation 1
At 3000 rpm :
L wot i – L tyre = 3 dB :
L veh gear i – L veh Gear i-n = 5,9 dB
L wot i – L tyre = 10 dB :
L veh gear i – L veh Gear i-n = 0,9 dB
L wot i – L tyre = 2 dB
L wot i – L tyre = 10 dB
High difference of gear ratios
High tyre noise slope

## Slide 5
Vehicle simulated :
Gear i-n : 15 kph/1000 rpm
Gear i : 20 kph/1000 rpm
L wot i = 74 dB(A)
Tyre :
L tyre 50 kph = 72 dB(A) or 64 dB(A)
a = 32
Engine :
b = 5 dB/1000rpm
At 3000 rpm :
L wot i – L tyre = 3 dB :
L veh gear i – L veh Gear i-n = 2,1 dB
L wot i – L tyre = 10 dB :
L veh gear i – L veh Gear i-n = 0,3 dB
L wot i – L tyre = 2 dB
L wot i – L tyre = 10 dB
Low difference of gear ratios
Low tyre noise slpoe
Simulation 2

## Slide 6
Conclusions
Gap between vehicle noise in gear i and gear i –n can go up to 5 dB depending to vehicle design.
To take account of the influence of tyre noise in vehicle noise, different approaches have been tested :
- Using combination with speed or engine speed and acceleration or gear ratios
   Relation between tyre influence and acceleration or gear ratios depends
  of each vehicle design.
- Using tyre noise influence as F/D proposal
Two alternatives can be chosen :
- Using Tyre noise into the model
   More precise approache to take into account this gap
  - Not using Tyre noise into the model
 Give a larger tolerance for vehicle which have high tyre noise or low engine noise