## Slide 1
GRB – ASEP – 08 Criteria to compare proposals
Den Hagg – September 2007

## Slide 2
Proposals
F/D proposal  GRBIG-ASEP-05-010
- F/D proposal with D improvement  GRB-IG-ASEP-07-006
- F/D proposal with F improvement  GRB-IG-ASEP-07-007
- F/D proposal with option for a limit derived anchor point  GRB-IG-ASEP-07-009
- Chairman proposal  GRB-IG-ASEP-07-002
- OICA proposal  GRBIG-ASEP-05-003
We can check 6 proposals or improvement of proposal :

## Slide 3
Engine speed
Speed
Acceleration
Vehicle
noise
Vehicle Measurement
Models concepts
Vehicle behaviour
One Reference point :
L ref (x ref) is derived from annex 3 result and/or limit (and additional elements as L tyre and PMR)
x ref = N ref and/or V ref and/or a ref are derived from Annex 3 result and/or additional elements
One noise vehicle behaviour :
L limit (N, V, a) is derived from L ref (x ref) by applying a model and a tolerance
L ref
x ref
L limit Gear i
Tolerance
Each concept is based on the same construction :

## Slide 4
 | REFERENCE POINT |  |  | 
 | L ref | N ref | V ref | a ref
F/D proposal | L wot i | N wot i | V wot i | -
F/D proposal with D improvement | L wot i limit derived from L urban limit & L tyre & PMR | N urban | 50 kph | -
F/D proposal with F improvement | L wot i | N wot i | V wot i | -
F/D proposal with option for a limit derived anchor point | L wot i limit derived from L urban limit L urban & L wot i | As F/D | As F/D | -
Chairman proposal | L urban limit | - | 50 kph | a urban
OICA proposal | L wot i | N wot i | - | -
Reference point
The reference point is based on Annex 3 result and/or limit and additional statistical results :

## Slide 5
Vehicle noise behaviour
 | LIMIT CONCEPT |  |  |  | 
 | Model | Slope behaviour | Reference point | Limit plotting | Gear ratio
F/D proposal | vehicle physics | Typical engine physics | Vehicle (annexe 3 derived) | Point by point | From Tyre noise
F/D proposal with D improvement | vehicle physics | Typical engine physics | statistical with tyre noise correction | Point by point | From Tyre noise
F/D proposal with F improvement | vehicle physics | Typical engine physics | Vehicle | Line for each gear ratio | From Tyre noise
F/D proposal with option for a limit derived anchor point | vehicle physics | Typical engine physics | Vehicle with additionnaltolerance for silent vehicle | As F/D | From Tyre noise
Chairman proposal | statistical | Statistical | statistical | Point by point | From acceleration
OICA proposal | Linear vehicle fit | Individual vehicle physics | vehicle | Line | ?
The vehicle noise behaviour is based on differents approach from individual to statistics :

## Slide 6
Uncertainties and dispersions
To choose the method, we need to study 2 points
Vehicle
noise
L ref
x ref
L limit
Vehicle
noise
The uncertainties to determine
the reference point and vehicle noise behaviour
Spread of “normal” vehicles compared to the model
Vehicle measurement
Vehicle behaviour
Proposal 1
Proposal 2
Proposal 3

## Slide 7
 |  | F/D proposal | F/D proposal with F improvement | F/D proposal with option for a limit derived anchor point | F/D proposal with D improvement | Chairman proposal | OICA proposal
Uncertainties : influents Factors | Reference point | L wot i N wot i V wot i | As F/D | As F/D | L tyre | - | L wot i N wot i
 | Limit line or point | L tyre N wot V wot | L tyre 50 kph N wot V wot | As F/D | As F/D | a wot V wot | L wot N wot
Dispersion : Influents factors | Reference point and slope | Engine noise slope vs engine speed | Engine and vehicle noise noise slope | As F/D | Engine noise slope N urban | Vehicle noise slope vs speed and acceleration a urban | Regression
 | Tolerance between vehicle noise behaviour and limit | [2] dB | [1] dB | As F/D | [1] dB | [ ] dB | [2] dB + 1.5 dB / 1000 rpm
Additional tolerance on Reference point |  | - | - | L wot limit from L urban limit and L wot | L wot limit from L urban limit | L urban limit | -
Influent factors must be check and study one by one :
Uncertainties, dispersions and tolerances
The tolerance will be adjust to discriminate “normal” vehicles to “abnormal” vehicles

## Slide 8
Conclusions
for all proposals using an ASEP limit linked with L urban limit
 L ASEP is a function of L urban limit and additional data(s)
All proposals can be link with L urban limit not to discriminate silent vehicles
All method present uncertainties on ASEP limit
Three following points need to be checked to compare proposals :
  - Uncertainties on the limit
  - Spread of normal vehicle compare to each model
  - Tolerance necessary to discriminate “normal” to “abnormal” vehicles