| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRRF/2007/21/Corr.1 26 November 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Sixty-second session

Geneva, 25-28 September 2007

Item 8(c) of the provisional agenda

TYRES

Regulation No. 106

(Pneumatic tyres for agricultural vehicles)

Corrigendum to ECE/TRANS/WP.29/GRRF/2007/21

Submitted by the experts from the European Tyre and Rim Technical Organisation (ETRTO) (/

Page 2, Annex 5, Table 5 (1 of 2), replace by the following:

"Table 5 (1 of 2) Agricultural Implement Tyres – Normal section Sizes

| Tyre size designation | Theoretical rim width code (A1) | Nominal section width (S1) | Overall diameter (D) | Nominal rim diameter (d) |
| --- | --- | --- | --- | --- |
|  |  |  |  | (*) |  |
|  |  | (mm) | (mm) | (mm) |
| 4.00 – 8 IMP | 3 | 112 | 418 | 425 | 203 |
| 4.00 – 9 IMP | 3 | 112 | 443 | 460 | 229 |
| 4.0 – 10 IMP | 3 | 114 | 455 | 465 | 254 |
| 4.00 – 10 IMP | 3 | 114 | 465 | 475 | 254 |
| 4.00 – 12 IMP | 3 | 112 | 519 | 536 | 305 |
| 4.00 – 15 IMP | 3 | 112 | 595 | 612 | 381 |
| 4.00 – 18 IMP | 3 | 112 | 672 | 688 | 457 |
| 4.50 – 19 IMP | 3 | 124 | 720 | 733 | 483 |
| 4.80 – 8 IMP | 3,75 | 121 | 423 | 449 | 203 |
| 5.0 – 10 IMP | 4 | 145 | 505 | 517 | 254 |
| 5.00 – 12 IMP | 4 | 145 | 567 | 580 | 305 |
| 5.00 – 14 IMP | 4 | 145 | 618 | 631 | 356 |
| 5.00 – 15 IMP | 3 | 130 | 639 | 655 | 381 |
| 5.50 – 16 IMP | 4 | 150 | 685 | 703 | 406 |
| 5.90 – 15 IMP | 4 | 150 | 665 | 681 | 381 |
| 6.00 - 9 IMP | 4,5 | 169 | 543 | 556 | 229 |
| 6.00 – 16 IMP | 4 | 158 | 712 | 729 | 406 |
| 6.50 – 16 IMP | 4,5 | 173 | 735 | 754 | 406 |
| 6.70 – 15 IMP | 4,5 | 182 | 704 | 720 | 381 |
| 7.00- 12 IMP | 5 | 187 | 667 | 685 | 305 |
| 7.50 – 10 IMP | 6 | 214 | 634 | 649 | 254 |
| 7.50 – 16 IMP | 5,5 | 202 | 785 | 801 | 406 |
| 7.50 – 18 IMP | 5,5 | 202 | 836 | 852 | 457 |
| 7.50 – 20 IMP | 5,5 | 202 | 887 | 903 | 508 |
| 7.50 – 24 IMP | 5,5 | 202 | 989 | 1013 | 610 |
| 7.60 – 15 IMP | 5,5 | 193 | 734 | 751 | 381 |
| 13.50 – 16.1 IMP | 11 | 353 | 1021 | 1043 | 409 |

"

Page 3, after table 6 (1 of 2), add the following note 3., to read:

"3.	Overall diameters (D) in column (*) apply to tyres marked with classification code 'I-3' – see Annex 10."

Page 5, after table 7 (2 of 2), in note 4., put the coefficient b between quotation marks.

Page 5, the justification, first paragraph, line 4, amend to read:

"Annex 5 of Regulation … paragraphs 6.1.2., 6.2.2., 6.3.1., 6.3.3. and 6.4.1.1."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.