## Slide 1: ASP- Additional Sidewall Protection
Presentation for GRRF Sixty-first Session
February 5-7, 2007
Informal document No. GRRF-61-24
(61st GRRF, 5 - 9 February 2007,
agenda item 6.4.)

## Slide 2: Definition ASP
“ASP” (Additional Sidewall Protection) is an additional protective rubber layer applied to the sidewall of the casing for improving resistance against sidewall abrasion.”
Purpose of ASP: …”enhancing safety and durability of tyres in urban use”….“to provide additional abrasion protection of the sidewall in aggressive urban usage”

## Slide 3: How does it work?
Casing sidewall is inspected and buffed PRECURE: MOLDCURE:
  Cushion is applied
  Pre-cured ASP is applied - Un-vulcanized wear rubber applied
Cushion-binding rubber
ASP- wearing rubber

## Slide 4: Application cushion

## Slide 5: Application of ASP

## Slide 6: ASP ready for vulcanization

## Slide 7: The “issue”
For tyres with overall max section width limited to +2% the application of ASP might exceed max overall section width of ECE 109 : 315/80R22.5 315/70R22.5 13R22.5
The BIPAVER proposal only deal with tyres exceeding max ECE-R109 Overall section width.

## Slide 8: Final Product
Total section width is Max 8 mm wider than max section width of a new original tire permitted by Reg. 54.
Additional thickness max 8mm
BIPAVER proposal: Max Overall width up to max 8mm

## Slide 9: Example: 315/80R22.5 Amended ECE 109: Max R54 + 1,5 % = 323 mm
Max R54: 318 mm
R109: +1,5% = 323 mm

## Slide 10: Example: 315/80R22.5 Amended ECE 109: Max R54 + 1,5 % = 323 mm One side ASP only permissible
Max R54: 318 mm
R109: +1,5% = 323 mm
ASP: Max R54 + 8 mm ASP: Max 326 mm
No additional reduction of dual spacing vs. amended ECE 109
Facing outwards:
The word ASP
Marking OUTSIDE
Facing inwards:
The word ASP