## Slide 1
Commercial vehicle wheel detachment and fixings
Department for Transport
GRRF 61st Session
Lawrence Thatcher
Informal document No. GRRF-61-37
(61st GRRF, 5-9 February 2007
agenda item 7.4.)
Notes: .

## Slide 2: Phase 1 research
Heavy vehicle wheel detachment, frequency of occurrence and loose wheel fixing problem
Website: www.dft.gov.uk
URL:www.dft.gov.uk/stellent/groups/dft_roads/documents/page/dft_roads_613560.hcsp

## Slide 3: Research Objectives
1. Identify the current frequency of wheel detachment in the UK
2. Analyse existing sources of UK data on wheel fixing problems
3. Gather parallel information on wheel detachment from other countries

## Slide 4: Research objectives (cont’d)
4. Identify current wheel fixing standards and best practice in tightening methods
5. Survey the views of drivers, operators and manufacturers

## Slide 5
RESULTS

## Slide 6: TRL’s estimated frequency of wheel fixing/detachment problems
 | Estimated number of incidents per year |  |  |  | 
 | Wheel defects (loose, missing, damaged nuts, etc) | Wheel detachment (no collision) | Wheel detachment (damage only accident) | Wheel detachment (injury accident) | Wheel detachment (fatal accident)
Upper estimate | 11,000 | 400 | 134 | 27 | 7
Lower estimate | 7,500 | 150 | 50 | 10 | 3

## Slide 7: Do wheels fall off abroad?
Information with supporting data was received from:
  Finland
  Canada
  Japan
  USA
  New Zealand
Replies received from other countries:
  Luxemburg
  Sweden
  Norway
  Holland
  France
  Germany
  Ivory Coast

## Slide 8: Designs & Standards
Three different designs and three main standards: BS, DIN and ISO

## Slide 9
Conclusions

## Slide 10
Wheel clamp load critical
Current fixings adequate for clamping force providing relaxation is accounted for
Joint relaxation is a key maintenance issue
Wheel fixing problems not unique to UK – worldwide problem
Higher incidence of problems on left-side – bias small for loose wheel nuts - large for wheel detachment

## Slide 11
86% of operators have formal policies for wheel fixings, but 12% reported never re-torquing a wheel
Operators have daily safety check regimes, but drivers .......
  26% of drivers admit not always checking while 32% admit not always looking for loose wheels
  2% never check

## Slide 12: Where next?
Phase 2 - project will include:
  Comparison of torque vs angular tightening and assess repeatability of clamp force
  Assessment, testing and durability of wheel nut retention and movement indicator devices
  Further standardisation of best practice and wheel tightening methods
  Further education to encourage adoption of wheel maintenance procedures

## Slide 13
Thank you
for your attention