| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRSG/2007/13 1 February 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

Ninety-second session

Geneva, 16-20 April 2007

Item 3.5. of the provisional agenda

AMENDMENTS TO OTHER REGULATIONS UNDER THE 1958 AGREEMENT

Regulation No. 58 (Rear underrun protection)

Proposal for draft amendments to Regulation No. 58

Submitted by the expert from Japan

The text reproduced below was prepared by the expert from Japan in order to propose amendments to ECE/TRANS/WP.29/GRSG/2007/12, submitted by the experts from France and the European Commission, with regard the effective surface area of rear underrun protection devices.  The proposed amendments to ECE/TRANS/WP.29/GRSG/2007/12 are marked in bold characters.

A.	PROPOSAL

PART I., inserted new paragraph 7.4.2., amend to read:

"7.4.2.	The individual elements of the underrun protection, including those outboard of the lift mechanism, where provided, must have an effective surface area, in each case, of at least 350 cm2.

However, in cases where it is difficult to secure this effective surface area of the underrun protection in a truck with a gross vehicle weight (GVW) of seven tonnes or less due to its structure, Contracting Parties may specify in their national regulations the size of such area."

PART III., inserted new paragraph 25.8.2., amend to read:

"25.8.2.	The individual elements of the underrun protection, including those outboard of the lift mechanism, where provided, must have an effective surface area, in each case, of at least 350 cm2.

However, in cases where it is difficult to secure this effective surface area of the underrun protection in a truck with a gross vehicle weight (GVW) of seven tonnes or less due to its structure, Contracting Parties may specify in their national regulations the size of such area."

B.	JUSTIFICATION

Japan is of the opinion that it is not feasible to require 350 cm2 effective surface area of the underrun protection's individual elements for vehicles with a small width.

1.	Bumper width direction (see Figure 1)

The outer bumpers need to be positioned in such a way that they do not interfere with the lift's arms installed at the outside of the chassis frame.  If the outer bumpers are positioned in such a way that they do not protrude outside the tyre's outer edge, it will be impossible to secure sufficient length and area of bumpers for general vehicles with GVW of seven tonnes or less.

2.	Bumper height direction (see Figure 1)

If the bumper height is increased in an upward direction to secure a wider area, it will interfere with the rear lamps and body structures.  If the bumper height is increased in downward direction, the departure angle will decrease, which results in poor drivability.

# Text boxes

1,695

980

*/	Indicates inconformity resulting from securing the bumper area of 350 cm2 or more.

**/	If the bumper area of 350 cm2 or more is secured and the truck is loaded at rated capacity, the departure angle will be 7º.

Figure 1

Vehicle width 1,695

6,630

Wheel base 3,400

2,250 (< ⅔ wheel base)

Departure angle 8º*/ **/

Departure angle 10º

Arm movable up and down (lift)

Rear lamp

Bumper

Lamp visible angle

Outer bumper

Rear lamp

Area: 185 cm3

100

C/F width (700)

A small vehicle with a three-piece bumper: an example of lift installation in the truck tailgate

190 */

Outside of arms (1,220)

Outside of bumper (1,640)

Tyre's outer edge (1,680)

185

185

All dimensions are given in millimeters.

Internal width of outer bumpers (1,270)

ECE/TRANS/WP.29/GRSG/2007/13

page 3